## Slide 1: T4 – Radio and Electronic Fundamentals 5 exam questions – 5 groups
  T4A Names of electrical units, DC and AC, what is a radio signal, conductors and insulators, electrical components
  T4B relationship between frequency and wavelength, identification of bands, names of frequency ranges, types of waves
  T4C How radio works: receivers, transmitters, transceivers, amplifiers, power supplies, types of batteries, service life
  T4D Ohms law relationships
  T4E Power calculations, units, kilo, mega, milli, micro
Notes: 2006 Technician Class (Element 2) Master syllabus
Released 6 February, 2006
35 Exam questions
http://www.microhams.com
Created by Scott N7SS

## Slide 2: Circuits
A battery is analogous to a pump in a water circuit. It creates the pressure (voltage) in the circuit. The flow of electrons (or water) is known as current. Any restriction in the flow is resistance and reduces current.

## Slide 3: Voltage, Current, Resistance
+
-
Voltage
Current
Resistance (Load)
You need a circuit for electricity to flow
Components of a circuit: Source, Conductors, Load, Sink (Ground)
Notes: Voltage is also called Electromotive Force and is an electrical “pressure”. Current is a measure of the flow of electrons (volume) from the negative to positive poles. The load presents resistance to the flow of electrons. Voltage is measured across the positive and negative poles (in parallel) to measure the difference in “pressure”. To measure the electron flow, the meter must be placed in-line (in series) with the flow.
Direct Current (DC) is a constant voltage source that causes current to flow in only one direction and has a positive and negative pole – like a battery. Alternating Current is what is available in the wall and the constantly changing polarity causes current to alternate directions.

## Slide 4: Voltage, Current and Power
Potential – Electromotive Force
  Electromotive Force (E)
  Units – Volts
  Unit Symbol V – 10V
  Measured across (parallel to load)
Current – Electron flow
  Current (I)
  Unites – Amps, Amperes
  Unit Symbol A – 0.1A
  Measured through (inline with load)
Power (P)
  Watts
  Units – Watts
  Unit Symbol W – 60W
P
I
E
P = I x E
Notes: <number>
<footer>
<header>
<date/time>
Potential – Voltage or Electromotive force
Units are Volts named after Count Alessandro Giuseppe Antonio Anastasio Volta (Italian Inventor), invented the baterry.
Flow – Current, measured in amps, named after André-Marie Ampère (French) scientist and mathematician
Power – Measured in Watts, named after James Watt (Scottish/British) inventor

## Slide 5: Units of Measure
Power | Watt
Resistance | Ohm
Voltage | Volt
Current | Ampere
Frequency | Hertz

## Slide 6: T4A01 Electrical current is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
  D. Amperes

## Slide 7: T4A01 Electrical current is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
D. Amperes

## Slide 8: T4A02 Electrical Power is measured in which of the following units?
  A. Volts
  B. Watts
  C. Ohms
  D. Amperes

## Slide 9: T4A02 Electrical Power is measured in which of the following units?
  A. Volts
B. Watts
  C. Ohms
  D. Amperes

## Slide 10: T4A03 What is the name for the flow of electrons in an electric circuit?
  A. Voltage
  B. Resistance
  C. Capacitance
  D. Current

## Slide 11: T4A03 What is the name for the flow of electrons in an electric circuit?
  A. Voltage
  B. Resistance
  C. Capacitance
D. Current

## Slide 12: T4A04 What is the name of a current that flows only in one direction?
  A. An alternating current
  B. A direct current
  C. A normal current
  D. A smooth current

## Slide 13: Direct Current Alternating Current
DC
Current flows in one direction only
  Examples:
    Battery Operated Devices
    Cars
AC
Current flows in both directions, voltage and current vary with time
  Example: House Wiring

## Slide 14: T4A04 What is the name of a current that flows only in one direction?
  A. An alternating current
B. A direct current
  C. A normal current
  D. A smooth current

## Slide 15: T4A05 What is the standard unit of frequency?
  A. The megacycle
  B. The Hertz
  C. One thousand cycles per second
  D. The electromagnetic force

## Slide 16: T4A05 What is the standard unit of frequency?
  A. The megacycle
B. The Hertz
  C. One thousand cycles per second
  D. The electromagnetic force

## Slide 17: T4A06 How much voltage does an automobile battery usually supply?
  A. About 12 volts
  B. About 30 volts
  C. About 120 volts
  D. About 240 volts

## Slide 18: T4A06 How much voltage does an automobile battery usually supply?
A. About 12 volts
  B. About 30 volts
  C. About 120 volts
  D. About 240 volts

## Slide 19: T4A07 What is the basic unit of resistance?
  A. The volt
  B. The watt
  C. The ampere
  D. The ohm

## Slide 20: T4A07 What is the basic unit of resistance?
  A. The volt
  B. The watt
  C. The ampere
D. The ohm

## Slide 21: T4A08 What is the name of a current that reverses direction on a regular basis?
  A. An alternating current
  B. A direct current
  C. A circular current
  D. A vertical current

## Slide 22: T4A08 What is the name of a current that reverses direction on a regular basis?
A. An alternating current
  B. A direct current
  C. A circular current
  D. A vertical current

## Slide 23: T4A09 Which of the following is a good electrical conductor?
  A. Glass
  B. Wood
  C. Copper
  D. Rubber

## Slide 24: Conductors and Insulators
In a conductor, electric current can flow freely, in an insulator it cannot. Simply stated, most metals are good electrical conductors, most nonmetals are not. Metals are also generally good heat conductors while nonmetals are not.
Conductors – Copper, Silver, Gold, Aluminum, Platinum, Steel, …
Insulators – Glass, Wood, Rubber, Air, plastic …
Note: Salt water is a
Conductor, and so are you.

## Slide 25: T4A09 Which of the following is a good electrical conductor?
  A. Glass
  B. Wood
C. Copper
  D. Rubber

## Slide 26: T4A10 Which of the following is a good electrical insulator?
  A. Copper
  B. Glass
  C. Aluminum
  D. Mercury

## Slide 27: T4A10 Which of the following is a good electrical insulator?
  A. Copper
B. Glass
  C. Aluminum
  D. Mercury

## Slide 28: T4A11 What is the term used to describe opposition to current flow in ordinary conductors such as wires?
  A. Inductance
  B. Resistance
  C. Counter EMF
  D. Magnetism

## Slide 29: Voltage, Current, Ohm’s Law
As current flows through a conductor, the flow is impeded (similar to the flow of water in a pipe). This resistance to a flow causes a voltage difference ΔV. The amount voltage is defined by Ohms’ law.

## Slide 30: Voltage, Current and Resistance - Ohm’s Law
Resistance (R )
  Measure of conductivity
  Unit – Ohms
  Unit Symbol Ω - 100Ω
Ohm’s law - Defines the relationship between Voltage, Current and Resistance
E = I*R
I = E/R
R = E/I
E
I
R
Notes: <number>
<footer>
<header>
<date/time>
Georg Simon Ohm (German/Bavarian) - Law of cnoduction

## Slide 31: T4A11 What is the term used to describe opposition to current flow in ordinary conductors such as wires?
  A. Inductance
B. Resistance
  C. Counter EMF
  D. Magnetism

## Slide 32: T4A12 What instrument is used to measure the flow of current in an electrical circuit?
  A. Frequency meter
  B. SWR meter
  C. Ammeter
  D. Voltmeter

## Slide 33: T4A12 What instrument is used to measure the flow of current in an electrical circuit?
  A. Frequency meter
  B. SWR meter
C. Ammeter
  D. Voltmeter

## Slide 34: T4A13 What instrument is used to measure Electromotive Force (EMF) between two points such as the poles of a battery?
  A. Magnetometer
  B. Voltmeter
  C. Ammeter
  D. Ohmmeter

## Slide 35: T4A13 What instrument is used to measure Electromotive Force (EMF) between two points such as the poles of a battery?
  A. Magnetometer
B. Voltmeter
  C. Ammeter
  D. Ohmmeter

## Slide 36: Wavelength vs Frequency
The distance a radio wave travels in one cycle is called wavelength
The time it takes to complete one cycle is the period
The maximum displacement of wave from reference value is amplitude
One Wavelength
Time
V+
V-
0V
One Cycle
Amplitude

## Slide 37: Frequency to Wavelength Conversion
300
Freq (MHz)
Wavelength =
To convert from frequency to wavelength in meters:
Frequency and wavelength are inversely proportional – as one increases, the other decreases
Longer (wavelength) – Lower (frequency)

## Slide 38: T4B01 What is the name for the distance a radio wave travels during one complete cycle?
  A. Wave speed
  B. Waveform
  C. Wavelength
  D. Wave spread

## Slide 39: T4B01 What is the name for the distance a radio wave travels during one complete cycle?
  A. Wave speed
  B. Waveform
C. Wavelength
  D. Wave spread

## Slide 40: T4B02 What term describes the number of times that an alternating current flows back and forth per second?
  A. Pulse rate
  B. Speed
  C. Wavelength
  D. Frequency

## Slide 41: T4B02 What term describes the number of times that an alternating current flows back and forth per second?
  A. Pulse rate
  B. Speed
  C. Wavelength
D. Frequency

## Slide 42: T4B03 What does 60 hertz (Hz) mean?
  A. 6000 cycles per second
  B. 60 cycles per second
  C. 6000 meters per second
  D. 60 meters per second

## Slide 43: T4B03 What does 60 hertz (Hz) mean?
  A. 6000 cycles per second
B. 60 cycles per second
  C. 6000 meters per second
  D. 60 meters per second

## Slide 44: T4B04 Electromagnetic waves that oscillate more than 20,000 times per second as they travel through space are generally referred to as what?
  A. Gravity waves
  B. Sound waves
  C. Radio waves
  D. Gamma radiation

## Slide 46: T4B04 Electromagnetic waves that oscillate more than 20,000 times per second as they travel through space are generally referred to as what?
  A. Gravity waves
  B. Sound waves
C. Radio waves
  D. Gamma radiation

## Slide 47: T4B05 How fast does a radio wave travel through space?
  A. At the speed of light
  B. At the speed of sound
  C. Its speed is inversely proportional to its wavelength
  D. Its speed increases as the frequency increases

## Slide 48: T4B05 How fast does a radio wave travel through space?
A. At the speed of light
  B. At the speed of sound
  C. Its speed is inversely proportional to its wavelength
  D. Its speed increases as the frequency increases

## Slide 49: T4B06 How does the wavelength of a radio wave relate to its frequency?
  A. The wavelength gets longer as the frequency increases
  B. The wavelength gets shorter as the frequency increases
  C. There is no relationship between wavelength and frequency
  D. The wavelength depends on the bandwidth of the signal

## Slide 50: T4B06 How does the wavelength of a radio wave relate to its frequency?
  A. The wavelength gets longer as the frequency increases
B. The wavelength gets shorter as the frequency increases
  C. There is no relationship between wavelength and frequency
  D. The wavelength depends on the bandwidth of the signal

## Slide 51: T4B07 What is the formula for converting frequency to wavelength in meters?
  A. Wavelength in meters equals frequency in Hertz multiplied by 300
  B. Wavelength in meters equals frequency in Hertz divided by 300
  C. Wavelength in meters equals frequency in megahertz divided by 300
  D. Wavelength in meters equals 300 divided by frequency in megahertz

## Slide 52: T4B07 What is the formula for converting frequency to wavelength in meters?
  A. Wavelength in meters equals frequency in Hertz multiplied by 300
  B. Wavelength in meters equals frequency in Hertz divided by 300
  C. Wavelength in meters equals frequency in megahertz divided by 300
D. Wavelength in meters equals 300 divided by frequency in megahertz

## Slide 53: T4B08 What are sound waves in the range between 300 and 3000 Hertz called?
  A. Test signals
  B. Ultrasonic waves
  C. Voice frequencies
  D. Radio frequencies

## Slide 54: T4B08 What are sound waves in the range between 300 and 3000 Hertz called?
  A. Test signals
  B. Ultrasonic waves
C. Voice frequencies
  D. Radio frequencies

## Slide 55: T4B09 What property of a radio wave is often used to identify the different bands amateur radio operators use?
  A. The physical length of the wave
  B. The magnetic intensity of the wave
  C. The time it takes for the wave to travel one mile
  D. The voltage standing wave ratio of the wave

## Slide 56: T4B09 What property of a radio wave is often used to identify the different bands amateur radio operators use?
A. The physical length of the wave
  B. The magnetic intensity of the wave
  C. The time it takes for the wave to travel one mile
  D. The voltage standing wave ratio of the wave

## Slide 57: T4B10 What is the frequency range of the 2 meter band in the United States?
  A. 144 to 148 MHz
  B. 222 to 225 MHz
  C. 420 to 450 MHz
  D. 50 to 54 MHz

## Slide 58: T4B10 What is the frequency range of the 2 meter band in the United States?
A. 144 to 148 MHz
  B. 222 to 225 MHz
  C. 420 to 450 MHz
  D. 50 to 54 MHz

## Slide 59: T4B11 What is the frequency range of the 6 meter band in the United States?
  A. 144 to 148 MHz
  B. 222 to 225 MHz
  C. 420 to 450 MHz
  D. 50 to 54 MHz

## Slide 60: T4B11 What is the frequency range of the 6 meter band in the United States?
  A. 144 to 148 MHz
  B. 222 to 225 MHz
  C. 420 to 450 MHz
D. 50 to 54 MHz

## Slide 61: T4B12 What is the frequency range of the 70 centimeter band in the United States?
  A. 144 to 148 MHz
  B. 222 to 225 MHz
  C. 420 to 450 MHz
  D. 50 to 54 MHz

## Slide 62: T4B12 What is the frequency range of the 70 centimeter band in the United States?
  A. 144 to 148 MHz
  B. 222 to 225 MHz
C. 420 to 450 MHz
  D. 50 to 54 MHz

## Slide 63: T4C01 What is used to convert radio signals into sounds we can hear?
  A. Transmitter
  B. Receiver
  C. Microphone
  D. Antenna

## Slide 64: T4C01 What is used to convert radio signals into sounds we can hear?
  A. Transmitter
B. Receiver
  C. Microphone
  D. Antenna

## Slide 65: T4C02 What is used to convert sounds from our voice into radio signals?
  A. Transmitter
  B. Receiver
  C. Speaker
  D. Antenna

## Slide 66: T4C02 What is used to convert sounds from our voice into radio signals?
A. Transmitter
  B. Receiver
  C. Speaker
  D. Antenna

## Slide 67: T4C03 What two devices are combined into one unit in a transceiver?
  A. Receiver, transmitter
  B. Receiver, transformer
  C. Receiver, transistor
  D. Transmitter, deceiver

## Slide 68: T4C03 What two devices are combined into one unit in a transceiver?
A. Receiver, transmitter
  B. Receiver, transformer
  C. Receiver, transistor
  D. Transmitter, deceiver

## Slide 69: T4C04 What device is used to convert the alternating current from a wall outlet into low-voltage direct current?
  A. Inverter
  B. Compressor
  C. Power Supply
  D. Demodulator

## Slide 70: T4C04 What device is used to convert the alternating current from a wall outlet into low-voltage direct current?
  A. Inverter
  B. Compressor
C. Power Supply
  D. Demodulator

## Slide 71: T4C05 What device is used to increase the output of a 10 watt radio to 100 watts?
  A. Amplifier
  B. Power supply
  C. Antenna
  D. Attenuator

## Slide 72: T4C05 What device is used to increase the output of a 10 watt radio to 100 watts?
A. Amplifier
  B. Power supply
  C. Antenna
  D. Attenuator

## Slide 73: T4C06 Which of the battery types listed below offers the longest life when used with a hand-held radio, assuming each battery is the same physical size?
  A. Lead-acid
  B. Alkaline
  C. Nickel-cadmium
  D. Lithium-ion

## Slide 74: T4C06 Which of the battery types listed below offers the longest life when used with a hand-held radio, assuming each battery is the same physical size?
  A. Lead-acid
  B. Alkaline
  C. Nickel-cadmium
D. Lithium-ion

## Slide 75: T4C07 What is the nominal voltage per cell of a fully charged nickel-cadmium battery?
  A. 1.0 volts
  B. 1.2 volts
  C. 1.5 volts
  D. 2.2 volts

## Slide 76: T4C07 What is the nominal voltage per cell of a fully charged nickel-cadmium battery?
  A. 1.0 volts
B. 1.2 volts
  C. 1.5 volts
  D. 2.2 volts

## Slide 77: T4C08 What battery type on this list is not designed to be re-charged?
  A. Nickel-cadmium
  B. Carbon-zinc
  C. Lead-acid
  D. Lithium-ion

## Slide 78: T4C08 What battery type on this list is not designed to be re-charged?
  A. Nickel-cadmium
B. Carbon-zinc
  C. Lead-acid
  D. Lithium-ion

## Slide 79: T4C09 What is required to keep rechargeable batteries in good condition and ready for emergencies?
  A. They must be inspected for physical damage and replaced if necessary
  B. They should be stored in a cool and dry location
  C. They must be given a maintenance recharge at least every 6 months
  D. All of these answers are correct

## Slide 80: T4C09 What is required to keep rechargeable batteries in good condition and ready for emergencies?
  A. They must be inspected for physical damage and replaced if necessary
  B. They should be stored in a cool and dry location
  C. They must be given a maintenance recharge at least every 6 months
D. All of these answers are correct

## Slide 81: T4C10 What is the best way to get the most amount of energy from a battery?
  A. Draw current from the battery as rapidly as possible
  B. Draw current from the battery at the slowest rate needed
  C. Reverse the leads when the battery reaches the 1/2 charge level
  D. Charge the battery as frequently as possible

## Slide 82: T4C10 What is the best way to get the most amount of energy from a battery?
  A. Draw current from the battery as rapidly as possible
B. Draw current from the battery at the slowest rate needed
  C. Reverse the leads when the battery reaches the 1/2 charge level
  D. Charge the battery as frequently as possible

## Slide 83: Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
P= E2/R
P= I2*R
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 84: T4D01 What formula is used to calculate current in a circuit?
  A. Current (I) equals voltage (E) multiplied by resistance (R)
  B. Current (I) equals voltage (E) divided by resistance (R)
  C. Current (I) equals voltage (E) added to resistance (R)
  D. Current (I) equals voltage (E) minus resistance (R)

## Slide 85: T4D01 What formula is used to calculate current in a circuit?
  A. Current (I) equals voltage (E) multiplied by resistance (R)
B. Current (I) equals voltage (E) divided by resistance (R)
  C. Current (I) equals voltage (E) added to resistance (R)
  D. Current (I) equals voltage (E) minus resistance (R)

## Slide 86: T4D02 What formula is used to calculate voltage in a circuit?
  A. Voltage (E) equals current (I) multiplied by resistance (R)
  B. Voltage (E) equals current (I) divided by resistance (R)
  C. Voltage (E) equals current (I) added to resistance (R)
  D. Voltage (E) equals current (I) minus resistance (R)

## Slide 87: T4D02 What formula is used to calculate voltage in a circuit?
A. Voltage (E) equals current (I) multiplied by resistance (R)
  B. Voltage (E) equals current (I) divided by resistance (R)
  C. Voltage (E) equals current (I) added to resistance (R)
  D. Voltage (E) equals current (I) minus resistance (R)

## Slide 88: T4D03 What formula is used to calculate resistance in a circuit?
  A. Resistance (R) equals voltage (E) multiplied by current (I)
  B. Resistance (R) equals voltage (E) divided by current (I)
  C. Resistance (R) equals voltage (E) added to current (I)
  D. Resistance (R) equals voltage (E) minus current (I)

## Slide 89: T4D03 What formula is used to calculate resistance in a circuit?
  A. Resistance (R) equals voltage (E) multiplied by current (I)
B. Resistance (R) equals voltage (E) divided by current (I)
  C. Resistance (R) equals voltage (E) added to current (I)
  D. Resistance (R) equals voltage (E) minus current (I)

## Slide 90: T4D04 What is the resistance of a circuit when a current of 3 amperes flows through a resistor connected to 90 volts?
  A. 3 ohms
  B. 30 ohms
  C. 93 ohms
  D. 270 ohms

## Slide 91: T4D04 What is the resistance of a circuit when a current of 3 amperes flows through a resistor connected to 90 volts?
E
I
R
R = E / I
R = 90V / 3A = 30Ω
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 92: T4D04 What is the resistance of a circuit when a current of 3 amperes flows through a resistor connected to 90 volts?
  A. 3 ohms
B. 30 ohms
  C. 93 ohms
  D. 270 ohms

## Slide 93: T4D05 What is the resistance in a circuit where the applied voltage is 12 volts and the current flow is 1.5 amperes?
  A. 18 ohms
  B. 0.125 ohms
  C. 8 ohms
  D. 13.5 ohms

## Slide 94: T4D05 What is the resistance in a circuit where the applied voltage is 12 volts and the current flow is 1.5 amperes?
  A. 18 ohms
  B. 0.125 ohms
C. 8 ohms
  D. 13.5 ohms

## Slide 95: T4D06 What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
  D. 1.5 amperes

## Slide 96: T4D06 What is the current flow in a circuit with an applied voltage of 120 volts and a resistance of 80 ohms?
  A. 9600 amperes
  B. 200 amperes
  C. 0.667 amperes
D. 1.5 amperes

## Slide 97: T4D07 What is the voltage across the resistor if a current of 0.5 amperes flows through a 2 ohm resistor?
  A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts

## Slide 98: T4D07 What is the voltage across the resistor if a current of 0.5 amperes flows through a 2 ohm resistor?
E
I
R
E = I * R
E = 0.5A * 2Ω = 1V
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 99: T4D07 What is the voltage across the resistor if a current of 0.5 amperes flows through a 2 ohm resistor?
A. 1 volt
  B. 0.25 volts
  C. 2.5 volts
  D. 1.5 volts

## Slide 100: T4D08 What is the voltage across the resistor if a current of 1 ampere flows through a 10 ohm resistor?
  A. 10 volts
  B. 1 volt
  C. 11 volts
  D. 9 volts

## Slide 101: T4D08 What is the voltage across the resistor if a current of 1 ampere flows through a 10 ohm resistor?
A. 10 volts
  B. 1 volt
  C. 11 volts
  D. 9 volts

## Slide 102: T4D09 What is the voltage across the resistor if a current of 2 amperes flows through a 10 ohm resistor?
  A. 20 volts
  B. 0.2 volts
  C. 12 volts
  D. 8 volts

## Slide 103: T4D09 What is the voltage across the resistor if a current of 2 amperes flows through a 10 ohm resistor?
A. 20 volts
  B. 0.2 volts
  C. 12 volts
  D. 8 volts

## Slide 104: T4D10 What is the current flowing through a 100 ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
  C. 2 amperes
  D. 100 amperes

## Slide 105: T4D10 What is the current flowing through a 100 ohm resistor connected across 200 volts?
E
I
R
I = E / R
I = 200V / 100Ω = 2A
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 106: T4D10 What is the current flowing through a 100 ohm resistor connected across 200 volts?
  A. 20,000 amperes
  B. 0.5 amperes
C. 2 amperes
  D. 100 amperes

## Slide 107: T4D11 What is the current flowing through a 24 ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
  C. 10 amperes
  D. 216 amperes
Notes: 10A at 240v is 2400 watts! That 24 ohm resistor is actually a baseboard electric heater 

## Slide 108: T4D11 What is the current flowing through a 24 ohm resistor connected across 240 volts?
  A. 24,000 amperes
  B. 0.1 amperes
C. 10 amperes
  D. 216 amperes

## Slide 109: T4E01 What unit is used to describe electrical power?
  A. Ohm
  B. Farad
  C. Volt
  D. Watt

## Slide 110: T4E01 What unit is used to describe electrical power?
  A. Ohm
  B. Farad
  C. Volt
D. Watt

## Slide 111: T4E02 What is the formula used to calculate electrical power in a DC circuit?
  A. Power (P) equals voltage (E) multiplied by current (I)
  B. Power (P) equals voltage (E) divided by current (I)
  C. Power (P) equals voltage (E) minus current (I)
  D. Power (P) equals voltage (E) plus current (I)

## Slide 112: Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 113: T4E02 What is the formula used to calculate electrical power in a DC circuit?
A. Power (P) equals voltage (E) multiplied by current (I)
  B. Power (P) equals voltage (E) divided by current (I)
  C. Power (P) equals voltage (E) minus current (I)
  D. Power (P) equals voltage (E) plus current (I)

## Slide 114: T4E03 How much power is represented by a voltage of 13.8 volts DC and a current of 10 amperes?
  A. 138 watts
  B. 0.7 watts
  C. 23.8 watts
  D. 3.8 watts

## Slide 115: T4E03 How much power is represented by a voltage of 13.8 volts DC and a current of 10 amperes?
P
I
E
P = I * E
P = 10A * 13.8V = 138W
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 116: T4E03 How much power is represented by a voltage of 13.8 volts DC and a current of 10 amperes?
A. 138 watts
  B. 0.7 watts
  C. 23.8 watts
  D. 3.8 watts

## Slide 117: T4E04 How much power is being used in a circuit when the voltage is 120 volts DC and the current is 2.5 amperes?
  A. 1440 watts
  B. 300 watts
  C. 48 watts
  D. 30 watts

## Slide 118: T4E04 How much power is being used in a circuit when the voltage is 120 volts DC and the current is 2.5 amperes?
  A. 1440 watts
B. 300 watts
  C. 48 watts
  D. 30 watts

## Slide 119: T4E05 How can you determine how many watts are being drawn by your transceiver when you are transmitting?
  A. Measure the DC voltage and divide it by 60 Hz
  B. Check the fuse in the power leads to see what size it is
  C. Look in the Radio Amateur's Handbook
  D. Measure the DC voltage at the transceiver and multiply by the current drawn when you transmit

## Slide 120: Power Supply
This Diawa power supply has a meter that can display voltage and current

## Slide 121: T4E05 How can you determine how many watts are being drawn by your transceiver when you are transmitting?
  A. Measure the DC voltage and divide it by 60 Hz
  B. Check the fuse in the power leads to see what size it is
  C. Look in the Radio Amateur's Handbook
D. Measure the DC voltage at the transceiver and multiply by the current drawn when you transmit

## Slide 122: T4E06 How many amperes are flowing in a circuit when the applied voltage is 120 volts DC and the load is 1200 watts?
  A. 20 amperes
  B. 10 amperes
  C. 120 amperes
  D. 5 amperes

## Slide 123: T4E06 How many amperes are flowing in a circuit when the applied voltage is 120 volts DC and the load is 1200 watts?
P
I
E
I = P / E
I = 1200W / 120VDC = 10A
Notes: There is a relationship between voltage, current and resistance as shown by the circle above. To solve for a value, cover it with your finger and solve the remaining formula. Ohm’s law states: E=IxR, I=E/R, R=E/I. The power formula states: P=IxE, I=P/E, E=P/I
There is one more formula that can be derived from this. Since Ohm’s law states E=IxR, you can substitute E in the power formula with this value yielding P=Ix(IxR) or P=I^2xR.

## Slide 124: T4E06 How many amperes are flowing in a circuit when the applied voltage is 120 volts DC and the load is 1200 watts?
  A. 20 amperes
B. 10 amperes
  C. 120 amperes
  D. 5 amperes

## Slide 125
109 106 103 102 101 100 10-1 10-2 10-3 10-6 10-9 10-12
G M k h da d c m µ n p
giga mega kilo hecto deca deci centi milli micro nano pico
Units of Measurements
Gigahertz | 1
Megahertz | 1000
Kilohertz | 1,000,000
Hertz | 1,000,000,000
Ampere | 1
Milliampere | 1000
Microampere | 1,000,000
Nanoampere | 1,000,000,000
Notes: Note the shift in decimal places.

## Slide 126: T4E07 How many milliamperes is the same as 1.5 amperes?
  A. 15 milliamperes
  B. 150 milliamperes
  C. 1500 milliamperes
  D. 15000 milliamperes

## Slide 127: T4E07 How many milliamperes is the same as 1.5 amperes?
  A. 15 milliamperes
  B. 150 milliamperes
C. 1500 milliamperes
  D. 15000 milliamperes

## Slide 128: T4E08 What is another way to specify the frequency of a radio signal that is oscillating at 1,500,000 Hertz?
  A. 1500 kHz
  B. 1500 MHz
  C. 15 GHz
  D. 150 kHz

## Slide 129: T4E08 What is another way to specify the frequency of a radio signal that is oscillating at 1,500,000 Hertz?
A. 1500 kHz
  B. 1500 MHz
  C. 15 GHz
  D. 150 kHz

## Slide 130: T4E09 How many volts are equal to one kilovolt?
  A. one one-thousandth of a volt
  B. one hundred volts
  C. one thousand volts
  D. one million volts

## Slide 131: T4E09 How many volts are equal to one kilovolt?
  A. one one-thousandth of a volt
  B. one hundred volts
C. one thousand volts
  D. one million volts

## Slide 132: T4E10 How many volts are equal to one microvolt?
  A. one one-millionth of a volt
  B. one million volts
  C. one thousand kilovolts
  D. one one-thousandth of a volt

## Slide 133: T4E10 How many volts are equal to one microvolt?
A. one one-millionth of a volt
  B. one million volts
  C. one thousand kilovolts
  D. one one-thousandth of a volt

## Slide 134: T4E11 How many watts does a hand-held transceiver put out if the output power is 500 milliwatts?
  A. 0.02 watts
  B. 0.5 watts
  C. 5 watts
  D. 50 watts

## Slide 135: T4E11 How many watts does a hand-held transceiver put out if the output power is 500 milliwatts?
  A. 0.02 watts
B. 0.5 watts
  C. 5 watts
  D. 50 watts