## Slide 1: G7 -- PRACTICAL CIRCUITS [1 Exam Question – 1 Group]
  G7A Power supplies and filters; single-sideband transmitters and receivers
Notes: ELEMENT 3 - GENERAL CLASS as released by the Question Pool Committee of the National Conference of Volunteer Examiner Coordinators December 1, 2003
The questions contained within this pool must be used in all General class examinations beginning July 1, 2004, and is intended to be used up through June 30, 2007.

## Slide 2: G7A01 What safety feature does a power-supply bleeder resistor provide?
  A. It does not affect voltage regulation
  B. It discharges the filter capacitors
  C. It removes shock hazards from the induction coils
  D. It eliminates ground-loop current

## Slide 3: G7A01 What safety feature does a power-supply bleeder resistor provide?
  A. It does not affect voltage regulation
B. It discharges the filter capacitors
  C. It removes shock hazards from the induction coils
  D. It eliminates ground-loop current

## Slide 4: G7A02 What components are used in a power-supply filter network?
  A. Diodes
  B. Transformers and transistors
  C. Quartz crystals
  D. Capacitors and inductors

## Slide 5: G7A02 What components are used in a power-supply filter network?
  A. Diodes
  B. Transformers and transistors
  C. Quartz crystals
D. Capacitors and inductors

## Slide 6: G7A03 What should be the minimum peak-inverse-voltage rating of the rectifier in a full-wave power supply?
  A. One-quarter the normal output voltage of the power supply
  B. Half the normal output voltage of the power supply
  C. Double the normal peak output voltage of the power supply
  D. Equal to the normal output voltage of the power supply

## Slide 7: G7A03 What should be the minimum peak-inverse-voltage rating of the rectifier in a full-wave power supply?
  A. One-quarter the normal output voltage of the power supply
  B. Half the normal output voltage of the power supply
C. Double the normal peak output voltage of the power supply
  D. Equal to the normal output voltage of the power supply

## Slide 8: G7A04 What should be the minimum peak-inverse-voltage rating of the rectifier in a half-wave power supply?
  A. One-quarter to one-half the normal peak output voltage of the power supply
  B. Half the normal output voltage of the power supply
  C. Equal to the normal output voltage of the power supply
  D. One to two times the normal peak output voltage of the power supply

## Slide 9: G7A04 What should be the minimum peak-inverse-voltage rating of the rectifier in a half-wave power supply?
  A. One-quarter to one-half the normal peak output voltage of the power supply
  B. Half the normal output voltage of the power supply
  C. Equal to the normal output voltage of the power supply
D. One to two times the normal peak output voltage of the power supply

## Slide 10: G7A05 What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted?
  A. Substantially higher
  B. About the same
  C. Substantially lower
  D. Twice the transmission line impedance

## Slide 11: G7A05 What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted?
  A. Substantially higher
B. About the same
  C. Substantially lower
  D. Twice the transmission line impedance

## Slide 12: G7A06 In a typical single-sideband phone transmitter, what circuit processes signals from the balanced modulator and sends signals to the mixer?
  A. Carrier oscillator
  B. Filter
  C. IF amplifier
  D. RF amplifier

## Slide 13: G7A06 In a typical single-sideband phone transmitter, what circuit processes signals from the balanced modulator and sends signals to the mixer?
  A. Carrier oscillator
B. Filter
  C. IF amplifier
  D. RF amplifier

## Slide 14: G7A07 In a single-sideband phone transmitter, what circuit processes signals from the carrier oscillator and the speech amplifier and sends signals to the filter?
  A. Mixer
  B. Detector
  C. IF amplifier
  D. Balanced modulator

## Slide 15: G7A07 In a single-sideband phone transmitter, what circuit processes signals from the carrier oscillator and the speech amplifier and sends signals to the filter?
  A. Mixer
  B. Detector
  C. IF amplifier
D. Balanced modulator

## Slide 16: G7A08 In a single-sideband phone superheterodyne receiver, what circuit processes signals from the RF amplifier and the local oscillator and sends signals to the IF filter?
  A. Balanced modulator
  B. IF amplifier
  C. Mixer
  D. Detector

## Slide 17: G7A08 In a single-sideband phone superheterodyne receiver, what circuit processes signals from the RF amplifier and the local oscillator and sends signals to the IF filter?
  A. Balanced modulator
  B. IF amplifier
C. Mixer
  D. Detector

## Slide 18: G7A09 In a single-sideband phone superheterodyne receiver, what circuit processes signals from the IF amplifier and the BFO and sends signals to the AF amplifier?
  A. RF oscillator
  B. IF filter
  C. Balanced modulator
  D. Detector

## Slide 19: G7A09 In a single-sideband phone superheterodyne receiver, what circuit processes signals from the IF amplifier and the BFO and sends signals to the AF amplifier?
  A. RF oscillator
  B. IF filter
  C. Balanced modulator
D. Detector

## Slide 20: G7A10 What type of power supply circuit is often used to provide overvoltage protection at its output?
  A. Crowbar
  B. Circuit breaker
  C. Ferrite transformer
  D. Buck-out transistor

## Slide 21: G7A10 What type of power supply circuit is often used to provide overvoltage protection at its output?
A. Crowbar
  B. Circuit breaker
  C. Ferrite transformer
  D. Buck-out transistor

## Slide 22: G7A11 What type of capacitors should be used to filter the rectified DC output of a switching power supply?
  A. Capacitors with low equivalent series resistance
  B. Ordinary, large value electrolytic capacitors
  C. NPO-type ceramic disc or silver mica capacitors
  D. Capacitors with high equivalent series inductance

## Slide 23: G7A11 What type of capacitors should be used to filter the rectified DC output of a switching power supply?
A. Capacitors with low equivalent series resistance
  B. Ordinary, large value electrolytic capacitors
  C. NPO-type ceramic disc or silver mica capacitors
  D. Capacitors with high equivalent series inductance

## Slide 24: G7A12 Which of the following is an advantage of a switched-mode power supply as compared to a linear power supply?
  A. Higher output voltages are possible with the switched-mode supply
  B. Fewer circuit components are required for the switched-mode supply
  C. The relatively high frequency power oscillator allows the use of small, lightweight and low-cost transformers in the switched-mode supply
  D. All of these choices are correct

## Slide 25: G7A12 Which of the following is an advantage of a switched-mode power supply as compared to a linear power supply?
  A. Higher output voltages are possible with the switched-mode supply
  B. Fewer circuit components are required for the switched-mode supply
C. The relatively high frequency power oscillator allows the use of small, lightweight and low-cost transformers in the switched-mode supply
  D. All of these choices are correct

## Slide 26: G7A13 In a switched-mode power supply, what is the first step in converting the 120 volt AC input voltage to a 12 volt DC output voltage?
  A. The 120 volt AC is first rectified and filtered
  B. The 120 volt AC is first converted to 12 volt AC with a transformer
  C. The 120 volt AC is switched off when the waveform exceeds 12 volts, and is switched on again when the waveform drops below 12 volts
  D. An AC clamp is used to limit the input signal to no more than 20 volts DC

## Slide 27: G7A13 In a switched-mode power supply, what is the first step in converting the 120 volt AC input voltage to a 12 volt DC output voltage?
A. The 120 volt AC is first rectified and filtered
  B. The 120 volt AC is first converted to 12 volt AC with a transformer
  C. The 120 volt AC is switched off when the waveform exceeds 12 volts, and is switched on again when the waveform drops below 12 volts
  D. An AC clamp is used to limit the input signal to no more than 20 volts DC