## Slide 1: T6 – Communications Modes and Methods 3 exam questions - 3 groups
  T6A Modulation modes, descriptions and bandwidth (AM, FM, SSB)
  T6B Voice communications, EchoLink and IRLP
  T6C Non-voice communications - image communications, data, CW, packet, PSK31, Morse code techniques, Q signals
Notes: 2006 Technician Class (Element 2) Master syllabus
Released 6 February, 2006
35 Exam questions
http://www.microhams.com
Created by Scott N7SS

## Slide 2: Sample Emission Modes
Mode | Type | Bandwidth | Content
CW | Telegraphy | 10 Hz | Text Data
SSB | Telephony | 2800 Hz | Voice
AM | Telephony | 6 kHz | Voice
FM | Telephony | 5-15 kHz | Voice
SSTV / Fax | Image | 2800 Hz | Image
ATV | Image | 6 MHz | Image
PSK31 | Data | 31 Hz | Text Data
RTTY | Data | 250 Hz | Text Data
Pactor (I, II, III) | Data | 500-2800 Hz | Binary Data
AX.25 Packet | Data | 10-20 kHz | Binary Data

## Slide 3: T6A01 What are phone transmissions?
  A. The use of telephones to set up an amateur radio contact
  B. A phone patch between amateur radio and the telephone system
  C. Voice transmissions by radio
  D. Placing the telephone handset near a radio transceiver's microphone and speaker to relay a telephone call

## Slide 4: T6A01 What are phone transmissions?
  A. The use of telephones to set up an amateur radio contact
  B. A phone patch between amateur radio and the telephone system
C. Voice transmissions by radio
  D. Placing the telephone handset near a radio transceiver's microphone and speaker to relay a telephone call

## Slide 5: T6A02 Which of the following is a form of amplitude modulation?
  A. Frequency modulation
  B. Phase modulation
  C. Single sideband
  D. Phase shift keying

## Slide 6: Amplitude Modulation
An unmodulated RF
carrier wave
A carrier wave AM
modulated with a
simple audio tone
Notes: Note the identical sidebands. They peak and dip together.

## Slide 7: Amplitude Modulation
An unmodulated RF
carrier requires narrow
bandwidth
Modulation of the carrier
creates sidebands. This
requires more bandwidth.
Transmitter power is spread across this bandwidth

## Slide 8: AM and SSB
The carrier contains no
audio information.
The sidebands contain
duplicate audio information
By filtering out the carrier and one sideband,
we save spectrum and concentrate our RF
energy into a narrower bandwidth. SSB is
therefore more efficient.

## Slide 9: T6A02 Which of the following is a form of amplitude modulation?
  A. Frequency modulation
  B. Phase modulation
C. Single sideband
  D. Phase shift keying

## Slide 10: T6A03 What name is given to an amateur radio station that is used to connect other amateur stations to the Internet?
  A. A gateway
  B. A repeater
  C. A digipeater
  D. A beacon station

## Slide 11: T6A03 What name is given to an amateur radio station that is used to connect other amateur stations to the Internet?
A. A gateway
  B. A repeater
  C. A digipeater
  D. A beacon station

## Slide 12: T6A04 Which type of voice modulation is most often used for long distance and weak signal contacts on the VHF and UHF bands?
  A. FM
  B. AM
  C. SSB
  D. PM

## Slide 13: T6A04 Which type of voice modulation is most often used for long distance and weak signal contacts on the VHF and UHF bands?
  A. FM
  B. AM
C. SSB
  D. PM

## Slide 14: T6A05 Which type of modulation is most commonly used for VHF and UHF voice repeaters?
  A. AM
  B. SSB
  C. PSK
  D. FM

## Slide 15: Frequency Modulation
Unmodulated carrier, full power at all times
Waveform of modulating signal
Modulated carrier with frequency deviation and constant amplitude
“Over modulation” called “over deviation” on FM, causes the signal to become wider and potentially cause adjacent channel interference

## Slide 16: T6A05 Which type of modulation is most commonly used for VHF and UHF voice repeaters?
  A. AM
  B. SSB
  C. PSK
D. FM

## Slide 17: T6A06 Which emission type has the narrowest bandwidth?
  A. FM voice
  B. SSB voice
  C. CW
  D. Slow-scan TV

## Slide 18: Common required Bandwidth
CW – 5-10Hz
Phone / Voice
  SSB - 2-3 kHz
  AM – 4-6 kHz
  FM – 5-15 kHz
Digital
  PSK31 – 31 Hz
  RTTY – 250 Hz
Slow Scan TV – 3KHz
Fast Scan TV – 6Mhz

## Slide 19: T6A06 Which emission type has the narrowest bandwidth?
  A. FM voice
  B. SSB voice
C. CW
  D. Slow-scan TV

## Slide 20: T6A07 Which sideband is normally used for VHF and UHF SSB communications?
  A. Upper sideband
  B. Lower sideband
  C. Suppressed sideband
  D. Inverted sideband

## Slide 21: T6A07 Which sideband is normally used for VHF and UHF SSB communications?
A. Upper sideband
  B. Lower sideband
  C. Suppressed sideband
  D. Inverted sideband

## Slide 22: T6A08 What is the primary advantage of single sideband over FM for voice transmissions?
  A. SSB signals are easier to tune in than FM signals
  B. SSB signals are less likely to be bothered by noise interference than FM signals.
  C. SSB signals use much less bandwidth than FM signals
  D. SSB signals have no advantages at all in comparison to other modes.

## Slide 23: T6A08 What is the primary advantage of single sideband over FM for voice transmissions?
  A. SSB signals are easier to tune in than FM signals
  B. SSB signals are less likely to be bothered by noise interference than FM signals.
C. SSB signals use much less bandwidth than FM signals
  D. SSB signals have no advantages at all in comparison to other modes.

## Slide 24: T6A09 What is the approximate bandwidth of a single-sideband voice signal?
  A. 1 kHz
  B. 2 kHz
  C. Between 3 and 6 kHz
  D. Between 2 and 3 kHz

## Slide 25: T6A09 What is the approximate bandwidth of a single-sideband voice signal?
  A. 1 kHz
  B. 2 kHz
  C. Between 3 and 6 kHz
D. Between 2 and 3 kHz

## Slide 26: T6A10 What is the approximate bandwidth of a frequency-modulated voice signal?
  A. Less than 500 Hz
  B. About 150 kHz
  C. Between 5 and 15 kHz
  D. More than 30 kHz

## Slide 27: T6A10 What is the approximate bandwidth of a frequency-modulated voice signal?
  A. Less than 500 Hz
  B. About 150 kHz
C. Between 5 and 15 kHz
  D. More than 30 kHz

## Slide 28: T6A11 What is the normal bandwidth required for a conventional fast-scan TV transmission using combined video and audio on the 70-centimeter band?
  A. More than 10 MHz
  B. About 6 MHz
  C. About 3 MHz
  D. About 1 MHz

## Slide 29: T6A11 What is the normal bandwidth required for a conventional fast-scan TV transmission using combined video and audio on the 70-centimeter band?
  A. More than 10 MHz
B. About 6 MHz
  C. About 3 MHz
  D. About 1 MHz

## Slide 30: T6B01 How is information transmitted between stations using Echolink?
  A. APRS
  B. PSK31
  C. Internet
  D. Atmospheric ducting

## Slide 31: EchoLink® and IRLP
EchoLink® software allows licensed Amateur Radio stations to communicate with one another over the Internet, using voice-over-IP (VoIP) technology.

## Slide 32: T6B01 How is information transmitted between stations using Echolink?
  A. APRS
  B. PSK31
C. Internet
  D. Atmospheric ducting

## Slide 33: T6B02 What does the abbreviation IRLP mean?
  A. Internet Radio Linking Project
  B. Internet Relay Language Protocol
  C. International Repeater Linking Project
  D. International Radio Linking Project

## Slide 34: T6B02 What does the abbreviation IRLP mean?
A. Internet Radio Linking Project
  B. Internet Relay Language Protocol
  C. International Repeater Linking Project
  D. International Radio Linking Project

## Slide 35: T6B03 Who may operate on the Echolink system?
  A. Only club stations
  B. Any licensed amateur radio operator
  C. Technician class licensed amateur radio operators only
  D. Any person, licensed or not, who is registered with the Echolink system

## Slide 36: T6B03 Who may operate on the Echolink system?
  A. Only club stations
B. Any licensed amateur radio operator
  C. Technician class licensed amateur radio operators only
  D. Any person, licensed or not, who is registered with the Echolink system

## Slide 37: T6B04 What technology do Echolink and IRLP have in common?
  A. Voice over Internet protocol
  B. Ionospheric propagation
  C. AC power lines
  D. PSK31

## Slide 38: T6B04 What technology do Echolink and IRLP have in common?
A. Voice over Internet protocol
  B. Ionospheric propagation
  C. AC power lines
  D. PSK31

## Slide 39: T6B05 What method is used to transfer data by IRLP?
  A. VHF Packet radio
  B. PSK31
  C. Voice over Internet protocol
  D. None of these answers are correct

## Slide 40: T6B05 What method is used to transfer data by IRLP?
  A. VHF Packet radio
  B. PSK31
C. Voice over Internet protocol
  D. None of these answers are correct

## Slide 41: T6B06 What does the term IRLP describe?
  A. A method of encrypting data
  B. A method of linking between two or more amateur stations using the Internet
  C. A low powered radio using infra-red frequencies
  D. An international logging program.

## Slide 42: T6B06 What does the term IRLP describe?
  A. A method of encrypting data
B. A method of linking between two or more amateur stations using the Internet
  C. A low powered radio using infra-red frequencies
  D. An international logging program.

## Slide 43: T6B07 Which one of the following allows computer-to-radio linking for voice transmission?
  A. Grid modulation
  B. EchoLink
  C. AMTOR
  D. Multiplex

## Slide 44: T6B07 Which one of the following allows computer-to-radio linking for voice transmission?
  A. Grid modulation
B. EchoLink
  C. AMTOR
  D. Multiplex

## Slide 45: T6B08 What are you listening to if you hear a brief tone and then a station from Russia calling CQ on a 2-meter repeater?
  A. An ionospheric band opening on VHF
  B. A prohibited transmission
  C. An Internet linked DX station
  D. None of these answers are correct

## Slide 46: T6B08 What are you listening to if you hear a brief tone and then a station from Russia calling CQ on a 2-meter repeater?
  A. An ionospheric band opening on VHF
  B. A prohibited transmission
C. An Internet linked DX station
  D. None of these answers are correct

## Slide 47: T6B10 Where might you find a list of active nodes using VoIP?
  A. The FCC Rulebook
  B. From your local emergency coordinator
  C. A repeater directory or the Internet
  D. The local repeater frequency coordinator

## Slide 48: T6B10 Where might you find a list of active nodes using VoIP?
  A. The FCC Rulebook
  B. From your local emergency coordinator
C. A repeater directory or the Internet
  D. The local repeater frequency coordinator

## Slide 49: T6B11 When using a portable transceiver how do you select a specific IRLP node?
  A. Choose a specific CTCSS tone
  B. Choose the correct DSC tone
  C. Access the repeater autopatch
  D. Use the keypad to transmit the IRLP node numbers

## Slide 50: T6B11 When using a portable transceiver how do you select a specific IRLP node?
  A. Choose a specific CTCSS tone
  B. Choose the correct DSC tone
  C. Access the repeater autopatch
D. Use the keypad to transmit the IRLP node numbers

## Slide 51: T6C01 Which of the following is an example of a digital communications method?
  A. Single sideband voice
  B. Amateur television
  C. FM voice
  D. Packet radio

## Slide 52: T6C01 Which of the following is an example of a digital communications method?
  A. Single sideband voice
  B. Amateur television
  C. FM voice
D. Packet radio

## Slide 53: T6C02 What does the term APRS mean?
  A. Automatic Position Reporting System
  B. Associated Public Radio Station
  C. Auto Planning Radio Set-up
  D. Advanced Polar Radio System

## Slide 54: APRS – Automatic Position Reporting System
Real-time
location
mapping

## Slide 55: T6C02 What does the term APRS mean?
A. Automatic Position Reporting System
  B. Associated Public Radio Station
  C. Auto Planning Radio Set-up
  D. Advanced Polar Radio System

## Slide 56: T6C03 What item is required along with your normal radio for sending automatic location reports?
  A. A connection to the vehicle speedometer
  B. A connection to a WWV receiver
  C. A connection to a broadcast FM sub-carrier receiver
  D. A global positioning system receiver

## Slide 57: T6C03 What item is required along with your normal radio for sending automatic location reports?
  A. A connection to the vehicle speedometer
  B. A connection to a WWV receiver
  C. A connection to a broadcast FM sub-carrier receiver
D. A global positioning system receiver

## Slide 58: T6C04 What type of transmission is indicated by the term NTSC?
  A. A Normal Transmission mode in Static Circuit
  B. A special mode for earth satellite uplink
  C. A standard fast scan color television signal
  D. A frame compression scheme for TV signal

## Slide 59: National Television Systems Committee (NTSC)
Television Standards
  NTSC – Canada, US, Japan, South Korea
  PAL
  SECAM

## Slide 60: Amateur Television Signal
A 6 MHz ATV video channel with the video carrier 1.25 MHz up from the lower edge. The color subcarrier is at 3.58 MHz and the sound subcarrier at 4.5 MHz above the video carrier.
The Luminance, Chrominance and Audio carriers are visible in the spectrum plot at left

## Slide 61: T6C04 What type of transmission is indicated by the term NTSC?
  A. A Normal Transmission mode in Static Circuit
  B. A special mode for earth satellite uplink
C. A standard fast scan color television signal
  D. A frame compression scheme for TV signal

## Slide 62: T6C05 What emission mode may be used by a Technician class operator in the 219 - 220 MHz frequency range?
  A. Slow-scan television
  B. Point-to-point digital message forwarding
  C. FM voice
  D. Fast-scan television

## Slide 63: T6C05 What emission mode may be used by a Technician class operator in the 219 - 220 MHz frequency range?
  A. Slow-scan television
B. Point-to-point digital message forwarding
  C. FM voice
  D. Fast-scan television

## Slide 64: T6C06 What does the abbreviation PSK mean?
  A. Pulse Shift Keying
  B. Phase Shift Keying
  C. Packet Short Keying
  D. Phased Slide Keying

## Slide 65: T6C06 What does the abbreviation PSK mean?
  A. Pulse Shift Keying
B. Phase Shift Keying
  C. Packet Short Keying
  D. Phased Slide Keying

## Slide 66: T6C07 What is PSK31?
  A. A high-rate data transmission mode used to transmit files
  B. A method of reducing noise interference to FM signals
  C. A type of television signal
  D. A low-rate data transmission mode that works well in noisy conditions

## Slide 67: PSK31 Digital Mode
Provides VERY EFFICIENT keyboard to keyboard chat capability. PSK31 is not error-corrected.

## Slide 68: T6C07 What is PSK31?
  A. A high-rate data transmission mode used to transmit files
  B. A method of reducing noise interference to FM signals
  C. A type of television signal
D. A low-rate data transmission mode that works well in noisy conditions

## Slide 69: T6C08 What sending speed is recommended when using Morse code?
  A. Only speeds below five WPM
  B. The highest speed your keyer will operate
  C. Any speed at which you can reliably receive
  D. The highest speed at which you can control the keyer

## Slide 70: T6C08 What sending speed is recommended when using Morse code?
  A. Only speeds below five WPM
  B. The highest speed your keyer will operate
C. Any speed at which you can reliably receive
  D. The highest speed at which you can control the keyer

## Slide 71: T6C09 What is a practical reason for being able to copy CW when using repeaters?
  A. To send and receive messages others cannot overhear
  B. To conform with FCC licensing requirements
  C. To decode packet radio transmissions
  D. To recognize a repeater ID sent in Morse code

## Slide 72: T6C09 What is a practical reason for being able to copy CW when using repeaters?
  A. To send and receive messages others cannot overhear
  B. To conform with FCC licensing requirements
  C. To decode packet radio transmissions
D. To recognize a repeater ID sent in Morse code

## Slide 73: T6C10 What is the "Q" signal used to indicate that you are receiving interference from other stations?
  A. QRM
  B. QRN
  C. QTH
  D. QSB

## Slide 74: Amateur Q Signals

## Slide 75: T6C10 What is the "Q" signal used to indicate that you are receiving interference from other stations?
A. QRM
  B. QRN
  C. QTH
  D. QSB

## Slide 76: T6C11 What is the "Q" signal used to indicate that you are changing frequency?
  A. QRU
  B. QSY
  C. QSL
  D. QRZ

## Slide 77: T6C11 What is the "Q" signal used to indicate that you are changing frequency?
  A. QRU
B. QSY
  C. QSL
  D. QRZ