## Slide 1: G8 -- SIGNALS AND EMISSIONS [2 Exam Questions -- 2 Groups]
  G8A Signal information; AM; FM; single and double sideband and carrier; bandwidth; modulation envelope; deviation; overmodulation
  G8B Frequency mixing; multiplication; bandwidths; HF data communications
Notes: ELEMENT 3 - GENERAL CLASS as released by the Question Pool Committee of the National Conference of Volunteer Examiner Coordinators December 1, 2003
The questions contained within this pool must be used in all General class examinations beginning July 1, 2004, and is intended to be used up through June 30, 2007.

## Slide 2: AM and SSB Signals
Notes: The power of an Amplitude Modulated (AM) or Sideband (SSB) signal varies with the amplitude (volume) of the modulating signal. The signal quality is best and power maximized when modulation is 100% - no more no less. Speech processors in most new rigs compress the voice dynamic range so modulation can stay closer to 100% all the time. If it over modulates, the signal will be “clipped” or “flat topped” and can cause “splatter” on adjacent frequencies. Looking for a slight deflection on your ALC meter when transmitting during modulation peaks.
An Am signal consists of a carrier and two identical but inverted sidebands. If the carrier is suppressed, full power can be delivered to both sidebands. Since the sidebands are identical, if one is eliminated entirely, more power is available to the other with a dramatic decrease in bandwidth. SSB is a very efficient for of communications considering both power and spectrum usage.

## Slide 3: G8A01 What type of modulation system changes the amplitude of an RF wave for the purpose of conveying information?
  A. Frequency modulation
  B. Phase modulation
  C. Amplitude-rectification modulation
  D. Amplitude modulation

## Slide 4: G8A01 What type of modulation system changes the amplitude of an RF wave for the purpose of conveying information?
  A. Frequency modulation
  B. Phase modulation
  C. Amplitude-rectification modulation
D. Amplitude modulation

## Slide 5: G8A02 What type of modulation system changes the phase of an RF wave for the purpose of conveying information?
  A. Pulse modulation
  B. Phase modulation
  C. Phase-rectification modulation
  D. Amplitude modulation

## Slide 6: G8A02 What type of modulation system changes the phase of an RF wave for the purpose of conveying information?
  A. Pulse modulation
B. Phase modulation
  C. Phase-rectification modulation
  D. Amplitude modulation

## Slide 7: G8A03 What type of modulation system changes the frequency of an RF wave for the purpose of conveying information?
  A. Phase-rectification modulation
  B. Frequency-rectification modulation
  C. Amplitude modulation
  D. Frequency modulation

## Slide 8: G8A03 What type of modulation system changes the frequency of an RF wave for the purpose of conveying information?
  A. Phase-rectification modulation
  B. Frequency-rectification modulation
  C. Amplitude modulation
D. Frequency modulation

## Slide 9: G8A04 What emission is produced by a reactance modulator connected to an RF power amplifier?
  A. Multiplex modulation
  B. Phase modulation
  C. Amplitude modulation
  D. Pulse modulation

## Slide 10: G8A04 What emission is produced by a reactance modulator connected to an RF power amplifier?
  A. Multiplex modulation
B. Phase modulation
  C. Amplitude modulation
  D. Pulse modulation

## Slide 11: G8A05 In what emission type does the instantaneous amplitude (envelope) of the RF signal vary in accordance with the modulating audio?
  A. Frequency shift keying
  B. Pulse modulation
  C. Frequency modulation
  D. Amplitude modulation

## Slide 12: G8A05 In what emission type does the instantaneous amplitude (envelope) of the RF signal vary in accordance with the modulating audio?
  A. Frequency shift keying
  B. Pulse modulation
  C. Frequency modulation
D. Amplitude modulation

## Slide 13: G8A07 What is one advantage of carrier suppression in a double-sideband phone transmission?
  A. Only half the bandwidth is required for the same information content
  B. Greater modulation percentage is obtainable with lower distortion
  C. More power can be put into the sidebands
  D. Simpler equipment can be used to receive a double-sideband suppressed-carrier signal

## Slide 14: G8A07 What is one advantage of carrier suppression in a double-sideband phone transmission?
  A. Only half the bandwidth is required for the same information content
  B. Greater modulation percentage is obtainable with lower distortion
C. More power can be put into the sidebands
  D. Simpler equipment can be used to receive a double-sideband suppressed-carrier signal

## Slide 15: G8A08 Which popular phone emission uses the narrowest frequency bandwidth?
  A. Single-sideband
  B. Double-sideband
  C. Phase-modulated
  D. Frequency-modulated

## Slide 16: G8A08 Which popular phone emission uses the narrowest frequency bandwidth?
A. Single-sideband
  B. Double-sideband
  C. Phase-modulated
  D. Frequency-modulated

## Slide 17: G8A09 What happens to the signal of an overmodulated single-sideband or double-sideband phone transmitter?
  A. It becomes louder with no other effects
  B. It occupies less bandwidth with poor high-frequency response
  C. It has higher fidelity and improved signal-to-noise ratio
  D. It becomes distorted and occupies more bandwidth

## Slide 18: G8A09 What happens to the signal of an overmodulated single-sideband or double-sideband phone transmitter?
  A. It becomes louder with no other effects
  B. It occupies less bandwidth with poor high-frequency response
  C. It has higher fidelity and improved signal-to-noise ratio
D. It becomes distorted and occupies more bandwidth

## Slide 19: G8A10 How should the microphone gain control be adjusted on a single-sideband phone transmitter?
  A. For full deflection of the ALC meter on modulation peaks
  B. For slight movement of the ALC meter on modulation peaks
  C. For 100% frequency deviation on modulation peaks
  D. For a dip in plate current

## Slide 20: G8A10 How should the microphone gain control be adjusted on a single-sideband phone transmitter?
  A. For full deflection of the ALC meter on modulation peaks
B. For slight movement of the ALC meter on modulation peaks
  C. For 100% frequency deviation on modulation peaks
  D. For a dip in plate current

## Slide 21: G8A11 What is meant by flattopping in a single-sideband phone transmission?
  A. Signal distortion caused by insufficient collector current
  B. The transmitter's automatic level control is properly adjusted
  C. Signal distortion caused by excessive drive
  D. The transmitter's carrier is properly suppressed

## Slide 22: G8A11 What is meant by flattopping in a single-sideband phone transmission?
  A. Signal distortion caused by insufficient collector current
  B. The transmitter's automatic level control is properly adjusted
C. Signal distortion caused by excessive drive
  D. The transmitter's carrier is properly suppressed

## Slide 23: G8A12 What happens to the RF carrier signal when a modulating audio signal is applied to an FM transmitter?
  A. The carrier frequency changes proportionally to the instantaneous amplitude of the modulating signal
  B. The carrier frequency changes proportionally to the amplitude and frequency of the modulating signal
  C. The carrier amplitude changes proportionally to the instantaneous frequency of the modulating signal
  D. The carrier phase changes proportionally to the instantaneous amplitude of the modulating signal

## Slide 24: G8A12 What happens to the RF carrier signal when a modulating audio signal is applied to an FM transmitter?
A. The carrier frequency changes proportionally to the instantaneous amplitude of the modulating signal
  B. The carrier frequency changes proportionally to the amplitude and frequency of the modulating signal
  C. The carrier amplitude changes proportionally to the instantaneous frequency of the modulating signal
  D. The carrier phase changes proportionally to the instantaneous amplitude of the modulating signal

## Slide 25: G8A13 What signal(s) would be found at the output of a properly adjusted balanced modulator?
  A. Both upper and lower sidebands
  B. Either upper or lower sideband, but not both
  C. Both upper and lower sidebands and the carrier
  D. The modulating signal and the unmodulated carrier

## Slide 26: G8A13 What signal(s) would be found at the output of a properly adjusted balanced modulator?
A. Both upper and lower sidebands
  B. Either upper or lower sideband, but not both
  C. Both upper and lower sidebands and the carrier
  D. The modulating signal and the unmodulated carrier

## Slide 27: G8B01 What receiver stage combines a 14.25-MHz input signal with a 13.795-MHz oscillator signal to produce a 455-kHz intermediate frequency (IF) signal?
  A. Mixer
  B. BFO
  C. VFO
  D. Multiplier

## Slide 28: G8B01 What receiver stage combines a 14.25-MHz input signal with a 13.795-MHz oscillator signal to produce a 455-kHz intermediate frequency (IF) signal?
A. Mixer
  B. BFO
  C. VFO
  D. Multiplier

## Slide 29: G8B02 If a receiver mixes a 13.800-MHz VFO with a 14.255-MHz received signal to produce a 455-kHz intermediate frequency (IF) signal, what type of interference will a 13.345-MHz signal produce in the receiver?
  A. Local oscillator
  B. Image response
  C. Mixer interference
  D. Intermediate interference

## Slide 30: G8B02 If a receiver mixes a 13.800-MHz VFO with a 14.255-MHz received signal to produce a 455-kHz intermediate frequency (IF) signal, what type of interference will a 13.345-MHz signal produce in the receiver?
  A. Local oscillator
B. Image response
  C. Mixer interference
  D. Intermediate interference

## Slide 31: G8B03 What stage in a transmitter would change a 5.3-MHz input signal to 14.3 MHz?
  A. A mixer
  B. A beat frequency oscillator
  C. A frequency multiplier
  D. A linear translator

## Slide 32: G8B03 What stage in a transmitter would change a 5.3-MHz input signal to 14.3 MHz?
A. A mixer
  B. A beat frequency oscillator
  C. A frequency multiplier
  D. A linear translator

## Slide 33: G8B04 What is the name of the stage in a VHF FM transmitter that selects a harmonic of an HF signal to reach the desired operating frequency?
  A. Mixer
  B. Reactance modulator
  C. Preemphasis network
  D. Multiplier

## Slide 34: G8B04 What is the name of the stage in a VHF FM transmitter that selects a harmonic of an HF signal to reach the desired operating frequency?
  A. Mixer
  B. Reactance modulator
  C. Preemphasis network
D. Multiplier

## Slide 35: G8B05 Why isn't frequency modulated (FM) phone used below 29.5 MHz?
  A. The transmitter efficiency for this mode is low
  B. Harmonics could not be attenuated to practical levels
  C. The bandwidth would exceed FCC limits
  D. The frequency stability would not be adequate

## Slide 36: G8B05 Why isn't frequency modulated (FM) phone used below 29.5 MHz?
  A. The transmitter efficiency for this mode is low
  B. Harmonics could not be attenuated to practical levels
C. The bandwidth would exceed FCC limits
  D. The frequency stability would not be adequate

## Slide 37: G8B06 What is the total bandwidth of an FM-phone transmission having a 5-kHz deviation and a 3-kHz modulating frequency?
  A. 3 kHz
  B. 5 kHz
  C. 8 kHz
  D. 16 kHz

## Slide 38: G8B06 What is the total bandwidth of an FM-phone transmission having a 5-kHz deviation and a 3-kHz modulating frequency?
  A. 3 kHz
  B. 5 kHz
  C. 8 kHz
D. 16 kHz

## Slide 39: G8B07 What is the frequency deviation for a 12.21-MHz reactance-modulated oscillator in a 5-kHz deviation, 146.52-MHz FM-phone transmitter?
  A. 41.67 Hz
  B. 416.7 Hz
  C. 5 kHz
  D. 12 kHz

## Slide 40: G8B07 What is the frequency deviation for a 12.21-MHz reactance-modulated oscillator in a 5-kHz deviation, 146.52-MHz FM-phone transmitter?
  A. 41.67 Hz
B. 416.7 Hz
  C. 5 kHz
  D. 12 kHz

## Slide 41: G8B08 How is frequency shift related to keying speed in an FSK signal?
  A. The frequency shift in hertz must be at least four times the keying speed in WPM
  B. The frequency shift must not exceed 15 Hz per WPM of keying speed
  C. Greater keying speeds require greater frequency shifts
  D. Greater keying speeds require smaller frequency shifts

## Slide 42: G8B08 How is frequency shift related to keying speed in an FSK signal?
  A. The frequency shift in hertz must be at least four times the keying speed in WPM
  B. The frequency shift must not exceed 15 Hz per WPM of keying speed
C. Greater keying speeds require greater frequency shifts
  D. Greater keying speeds require smaller frequency shifts

## Slide 43: G8B09 What do RTTY, Morse code, PSK31 and packet communications have in common?
  A. They are multipath communications
  B. They are digital communications
  C. They are analog communications
  D. They are only for emergency communications

## Slide 44: G8B09 What do RTTY, Morse code, PSK31 and packet communications have in common?
  A. They are multipath communications
B. They are digital communications
  C. They are analog communications
  D. They are only for emergency communications

## Slide 45: G8B10 When sending data modes, why is it important to know the duty cycle of the mode you are using?
  A. Your connectors, feed line or antenna may be rated for intermittent amateur service
  B. To prevent damage to your transmitter's final output stage due to its inability to dissipate excess heat
  C. To prevent blowing your power supply's fuse due to its inability to dissipate excess heat
  D. All of these choices are correct

## Slide 46: G8B10 When sending data modes, why is it important to know the duty cycle of the mode you are using?
  A. Your connectors, feed line or antenna may be rated for intermittent amateur service
B. To prevent damage to your transmitter's final output stage due to its inability to dissipate excess heat
  C. To prevent blowing your power supply's fuse due to its inability to dissipate excess heat
  D. All of these choices are correct

## Slide 47: G8B11 In what segment of the 20-meter band are most PSK31 operations found?
  A. At the bottom of the slow-scan TV segment, near 14.230 MHz
  B. At the top of the SSB phone segment, near 14.325 MHz
  C. In the middle of the CW segment, near 14.100 MHz
  D. Below the RTTY segment, near 14.070 MHz

## Slide 48: G8B11 In what segment of the 20-meter band are most PSK31 operations found?
  A. At the bottom of the slow-scan TV segment, near 14.230 MHz
  B. At the top of the SSB phone segment, near 14.325 MHz
  C. In the middle of the CW segment, near 14.100 MHz
D. Below the RTTY segment, near 14.070 MHz

## Slide 49: G8B12 What is the maximum bandwidth permitted by FCC rules for amateur radio stations when operating on USB frequencies in the 60-meter band?
  A. 2.8 kHz
  B. 5.6 kHz
  C. 2.8 kHz
  D. 3 kHz

## Slide 50: G8B12 What is the maximum bandwidth permitted by FCC rules for amateur radio stations when operating on USB frequencies in the 60-meter band?
A. 2.8 kHz
  B. 5.6 kHz
  C. 2.8 kHz
  D. 3 kHz

## Slide 51: G8B13 What is another term for the mixing of two RF signals?
  A. Heterodyning
  B. Synthesizing
  C. Cancellation
  D. Multiplying

## Slide 52: G8B13 What is another term for the mixing of two RF signals?
A. Heterodyning
  B. Synthesizing
  C. Cancellation
  D. Multiplying