## Slide 1: G2 -- OPERATING PROCEDURES [6 Exam Questions -- 6 Groups]
  G2A Phone operating procedures
  G2B Operating courtesy
  G2C Emergencies, including drills and emergency communications
  G2D Amateur auxiliary to the FCC's Compliance and Information Bureau; antenna orientation to minimize interference; HF operations, including logging practices
  G2E Third-party communications; ITU Regions; VOX operation
  G2F CW operating procedures, including procedural signals, Q signals and common abbreviations; full break-in; RTTY operating procedures, including g procedural signals and common abbreviations and operating procedures for other digital modes, such as HF packet, AMTOR, PacTOR, G-TOR, Clover and PSK31
Notes: ELEMENT 3 - GENERAL CLASS as released by the Question Pool Committee of the National Conference of Volunteer Examiner Coordinators December 1, 2003
The questions contained within this pool must be used in all General class examinations beginning July 1, 2004, and is intended to be used up through June 30, 2007.

## Slide 2: Amplitude Modulation
An unmodulated RF
carrier requires narrow
bandwidth
Modulation of the carrier
creates sidebands. This
requires more bandwidth.
Transmitter power is spread across this bandwidth
Notes: This is the appearance of an AM signal on a spectrum scope. There is a carrier in the center that uses power but contains no information (it can be used for tuning). Each of the two sidebands (upper and lower) are identical but inverted. HF amateur communications are generally on a single sideband (SSB) by suppressing the carrier and opposite sideband. This is more efficient by using less bandwidth and power is not wasted transmitting a dead carrier and duplicate sideband.
Because of radio design simplicity, the convention has been to use lower sideband (LSB) below 14 MHz and upper sideband (USB) above 14 MHz.

## Slide 3: AM and SSB
The carrier contains no
audio information.
The sidebands contain
duplicate audio information
By filtering out the carrier and one sideband, we save spectrum and concentrate our RF energy into a narrower bandwidth. SSB is therefore more efficient.
EI0CL from N0OB on SSB

## Slide 4: G2A01 Which sideband is commonly used for 20-meter phone operation?
  A. Upper
  B. Lower
  C. Amplitude compandored
  D. Double

## Slide 5: G2A01 Which sideband is commonly used for 20-meter phone operation?
A. Upper
  B. Lower
  C. Amplitude compandored
  D. Double

## Slide 6: G2A02 Which sideband is commonly used on 3925-kHz for phone operation?
  A. Upper
  B. Lower
  C. Amplitude compandored
  D. Double

## Slide 7: G2A02 Which sideband is commonly used on 3925-kHz for phone operation?
  A. Upper
B. Lower
  C. Amplitude compandored
  D. Double

## Slide 8: G2A03 Which sideband is commonly used for 40-meter phone operation?
  A. Upper
  B. Lower
  C. Amplitude compandored
  D. Double

## Slide 9: G2A03 Which sideband is commonly used for 40-meter phone operation?
  A. Upper
B. Lower
  C. Amplitude compandored
  D. Double

## Slide 10: G2A04 Which sideband is commonly used for 10-meter phone operation?
  A. Double
  B. Lower
  C. Amplitude compandored
  D. Upper

## Slide 11: G2A04 Which sideband is commonly used for 10-meter phone operation?
  A. Double
  B. Lower
  C. Amplitude compandored
D. Upper

## Slide 12: G2A05 Which sideband is commonly used for 15-Meter phone operation?
  A. Upper
  B. Lower
  C. Amplitude compandored
  D. Double

## Slide 13: G2A05 Which sideband is commonly used for 15-Meter phone operation?
A. Upper
  B. Lower
  C. Amplitude compandored
  D. Double

## Slide 14: G2A06 Which sideband is commonly used for 17-Meter phone operation?
  A. Amplitude compandored
  B. Lower
  C. Upper
  D. Double

## Slide 15: G2A06 Which sideband is commonly used for 17-Meter phone operation?
  A. Amplitude compandored
  B. Lower
C. Upper
  D. Double

## Slide 16: G2A07 Which of the following modes of voice communication is most commonly used on the High Frequency Amateur bands?
  A. Frequency modulation (FM)
  B. Amplitude modulation (AM)
  C. Single sideband (SSB)
  D. Phase modulation (PM)

## Slide 17: G2A07 Which of the following modes of voice communication is most commonly used on the High Frequency Amateur bands?
  A. Frequency modulation (FM)
  B. Amplitude modulation (AM)
C. Single sideband (SSB)
  D. Phase modulation (PM)

## Slide 18: G2A08 Why is the single sideband mode of voice transmission used more frequently than Amplitude Modulation (AM) on the HF amateur bands?
  A. Single sideband transmissions use less spectrum space
  B. Single sideband transmissions are more power efficient
  C. No carrier is transmitted with a single sideband transmission
  D. All of these choices are correct

## Slide 19: G2A08 Why is the single sideband mode of voice transmission used more frequently than Amplitude Modulation (AM) on the HF amateur bands?
  A. Single sideband transmissions use less spectrum space
  B. Single sideband transmissions are more power efficient
  C. No carrier is transmitted with a single sideband transmission
D. All of these choices are correct

## Slide 20: G2A09 Which of the following statements is true of a lower sideband transmission?
  A. It is called lower sideband because the lower sideband is greatly attenuated
  B. It is called lower sideband because the lower sideband is the only sideband transmitted, since the upper sideband is suppressed
  C. The lower sideband is wider than the upper sideband
  D. The lower sideband is the only sideband that is authorized on the 160-, 75- and 40-meter amateur bands

## Slide 21: G2A09 Which of the following statements is true of a lower sideband transmission?
  A. It is called lower sideband because the lower sideband is greatly attenuated
B. It is called lower sideband because the lower sideband is the only sideband transmitted, since the upper sideband is suppressed
  C. The lower sideband is wider than the upper sideband
  D. The lower sideband is the only sideband that is authorized on the 160-, 75- and 40-meter amateur bands

## Slide 22: G2A10 Which of the following statements is true of an upper sideband transmission?
  A. Only the upper sideband is transmitted, since the lower sideband is suppressed
  B. The upper sideband is greatly attenuated as compared with the carrier
  C. The upper sideband is greatly attenuated as compared with the lower sideband
  D. Only the upper sideband may be used for phone transmissions on the amateur bands with frequencies above 14 MHz

## Slide 23: G2A10 Which of the following statements is true of an upper sideband transmission?
A. Only the upper sideband is transmitted, since the lower sideband is suppressed
  B. The upper sideband is greatly attenuated as compared with the carrier
  C. The upper sideband is greatly attenuated as compared with the lower sideband
  D. Only the upper sideband may be used for phone transmissions on the amateur bands with frequencies above 14 MHz

## Slide 24: G2A11 Why do most amateur stations use lower sideband on the 160-, 75- and 40-meter bands?
  A. The lower sideband is more efficient at these frequency bands
  B. The lower sideband is the only sideband legal on these frequency bands
  C. Because it is fully compatible with an AM detector
  D. Current amateur practice is to use lower sideband on these frequency bands

## Slide 25: G2A11 Why do most amateur stations use lower sideband on the 160-, 75- and 40-meter bands?
  A. The lower sideband is more efficient at these frequency bands
  B. The lower sideband is the only sideband legal on these frequency bands
  C. Because it is fully compatible with an AM detector
D. Current amateur practice is to use lower sideband on these frequency bands

## Slide 26: G2B01 If you are the net control station of a daily HF net, what should you do if the frequency on which you normally meet is in use just before the net begins?
  A. Reduce your output power and start the net as usual
  B. Increase your power output so that net participants will be able to hear you over the existing activity
  C. Conduct the net on a clear frequency 3 to 5-kHz away from the regular net frequency
  D. Cancel the net for that day

## Slide 27: G2B01 If you are the net control station of a daily HF net, what should you do if the frequency on which you normally meet is in use just before the net begins?
  A. Reduce your output power and start the net as usual
  B. Increase your power output so that net participants will be able to hear you over the existing activity
C. Conduct the net on a clear frequency 3 to 5-kHz away from the regular net frequency
  D. Cancel the net for that day

## Slide 28: G2B02 If a net is about to begin on a frequency which you and another station are using, what should you do?
  A. As a courtesy to the net, move to a different frequency
  B. Increase your power output to ensure that all net participants can hear you
  C. Transmit as long as possible on the frequency so that no other stations may use it
  D. Turn off your radio

## Slide 29: G2B02 If a net is about to begin on a frequency which you and another station are using, what should you do?
A. As a courtesy to the net, move to a different frequency
  B. Increase your power output to ensure that all net participants can hear you
  C. Transmit as long as possible on the frequency so that no other stations may use it
  D. Turn off your radio

## Slide 30: G2B03 If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, what should you do?
  A. Tell the interfering stations to change frequency, since you were there first
  B. Report the interference to your local Amateur Auxiliary Coordinator
  C. Move your contact to another frequency
  D. Turn on your amplifier to overcome the interference

## Slide 31: G2B03 If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, what should you do?
  A. Tell the interfering stations to change frequency, since you were there first
  B. Report the interference to your local Amateur Auxiliary Coordinator
C. Move your contact to another frequency
  D. Turn on your amplifier to overcome the interference

## Slide 32: G2B04 When selecting a CW transmitting frequency, what minimum frequency separation from a contact in progress should you allow to minimize interference?
  A. 5 to 50 Hz
  B. 150 to 500 Hz
  C. 1 to 3 kHz
  D. 3 to 6 kHz

## Slide 33: G2B04 When selecting a CW transmitting frequency, what minimum frequency separation from a contact in progress should you allow to minimize interference?
  A. 5 to 50 Hz
B. 150 to 500 Hz
  C. 1 to 3 kHz
  D. 3 to 6 kHz

## Slide 34: G2B05 When selecting a single-sideband phone transmitting frequency, what minimum frequency separation from a contact in progress should you allow (between suppressed carriers) to minimize interference?
  A. 150 to 500 Hz
  B. Approximately 3 kHz
  C. Approximately 6 kHz
  D. Approximately 10 kHz

## Slide 35: G2B05 When selecting a single-sideband phone transmitting frequency, what minimum frequency separation from a contact in progress should you allow (between suppressed carriers) to minimize interference?
  A. 150 to 500 Hz
B. Approximately 3 kHz
  C. Approximately 6 kHz
  D. Approximately 10 kHz

## Slide 36: G2B06 When selecting a RTTY transmitting frequency, what minimum frequency separation from a contact in progress should you allow (center to center) to minimize interference?
  A. 60 Hz
  B. 250 to 500 Hz
  C. Approximately 3 kHz
  D. Approximately 6 kHz

## Slide 37: G2B06 When selecting a RTTY transmitting frequency, what minimum frequency separation from a contact in progress should you allow (center to center) to minimize interference?
  A. 60 Hz
B. 250 to 500 Hz
  C. Approximately 3 kHz
  D. Approximately 6 kHz

## Slide 38: G2B07 What is a band plan?
  A. A voluntary guideline beyond the divisions established by the FCC for using different operating modes within an amateur band
  B. A guideline from the FCC for making amateur frequency band allocations
  C. A plan of operating schedules within an amateur band published by the FCC
  D. A plan devised by a club to best use a frequency band during a contest

## Slide 39: G2B07 What is a band plan?
A. A voluntary guideline beyond the divisions established by the FCC for using different operating modes within an amateur band
  B. A guideline from the FCC for making amateur frequency band allocations
  C. A plan of operating schedules within an amateur band published by the FCC
  D. A plan devised by a club to best use a frequency band during a contest

## Slide 40: G2B08 What is another name for a voluntary guideline that guides amateur activities and extends beyond the divisions established by the FCC for using different operating modes within an amateur band?
  A. A "Band Plan"
  B. A "Frequency and Solar Cycle Guide"
  C. The "Knowledgeable Operator's Guide"
  D. The "Frequency Use Guidebook"

## Slide 41: G2B08 What is another name for a voluntary guideline that guides amateur activities and extends beyond the divisions established by the FCC for using different operating modes within an amateur band?
A. A "Band Plan"
  B. A "Frequency and Solar Cycle Guide"
  C. The "Knowledgeable Operator's Guide"
  D. The "Frequency Use Guidebook"

## Slide 42: G2B09 When choosing a frequency for Slow-Scan TV (SSTV) operation, what should you do to comply with good amateur practice?
  A. Review FCC Part 97 Rules regarding permitted frequencies and emissions
  B. Follow generally accepted gentlemen's agreement band plans
  C. Before transmitting, listen to the frequency to be used to avoid interfering with an ongoing communication
  D. All of these choices

## Slide 43: G2B09 When choosing a frequency for Slow-Scan TV (SSTV) operation, what should you do to comply with good amateur practice?
  A. Review FCC Part 97 Rules regarding permitted frequencies and emissions
  B. Follow generally accepted gentlemen's agreement band plans
  C. Before transmitting, listen to the frequency to be used to avoid interfering with an ongoing communication
D. All of these choices

## Slide 44: G2B10 When choosing a frequency for radioteletype (RTTY) operation, what should you do to comply with good amateur practice?
  A. Review FCC Part 97 Rules regarding permitted frequencies and emissions
  B. Follow generally accepted gentlemen's agreement band plans
  C. Before transmitting, first listen to the frequency to be used to avoid interfering with an ongoing communication
  D. All of these choices

## Slide 45: G2B10 When choosing a frequency for radioteletype (RTTY) operation, what should you do to comply with good amateur practice?
  A. Review FCC Part 97 Rules regarding permitted frequencies and emissions
  B. Follow generally accepted gentlemen's agreement band plans
  C. Before transmitting, first listen to the frequency to be used to avoid interfering with an ongoing communication
D. All of these choices

## Slide 46: G2B11 When choosing a frequency for HF Packet operation, what should you do to comply with good amateur practice?
  A. Review FCC Part 97 Rules regarding permitted frequencies and emissions
  B. Follow generally accepted gentlemen's agreement band plans
  C. Before transmitting, first listen on the frequency to be used to avoid interfering with an ongoing communication
  D. All of these choices

## Slide 47: G2B11 When choosing a frequency for HF Packet operation, what should you do to comply with good amateur practice?
  A. Review FCC Part 97 Rules regarding permitted frequencies and emissions
  B. Follow generally accepted gentlemen's agreement band plans
  C. Before transmitting, first listen on the frequency to be used to avoid interfering with an ongoing communication
D. All of these choices

## Slide 48: G2B12 What is a considerate way to avoid harmful interference when using phone?
  A. Ask if the frequency is in use, and say your call sign
  B. Call MAYDAY to make sure that the frequency is clear
  C. Call CQ for two minutes and see if anyone responds
  D. Turn on your amplifier, then go ahead and transmit

## Slide 49: G2B12 What is a considerate way to avoid harmful interference when using phone?
A. Ask if the frequency is in use, and say your call sign
  B. Call MAYDAY to make sure that the frequency is clear
  C. Call CQ for two minutes and see if anyone responds
  D. Turn on your amplifier, then go ahead and transmit

## Slide 50: G2B13 What is a considerate way to avoid harmful interference when using Morse code or CW?
  A. Send the letter "V" 12 times and then listen for a response
  B. Call CQ for two minutes and see if anyone responds
  C. Send "QRL? de" followed by your call sign and listen for a response
  D. Turn on your amplifier, then go ahead and transmit

## Slide 51: G2B13 What is a considerate way to avoid harmful interference when using Morse code or CW?
  A. Send the letter "V" 12 times and then listen for a response
  B. Call CQ for two minutes and see if anyone responds
C. Send "QRL? de" followed by your call sign and listen for a response
  D. Turn on your amplifier, then go ahead and transmit

## Slide 52: G2C01 What means may an amateur station in distress use to attract attention, make known its condition and location, and obtain assistance?
  A. Only Morse code signals sent on internationally recognized emergency channels
  B. Any means of radiocommunication, but only on internationally recognized emergency channels
  C. Any means of radiocommunication
  D. Only those means of radiocommunication for which the station is licensed

## Slide 53: G2C01 What means may an amateur station in distress use to attract attention, make known its condition and location, and obtain assistance?
  A. Only Morse code signals sent on internationally recognized emergency channels
  B. Any means of radiocommunication, but only on internationally recognized emergency channels
C. Any means of radiocommunication
  D. Only those means of radiocommunication for which the station is licensed

## Slide 54: G2C02 During a disaster in the US, when may an amateur station make transmissions necessary to meet essential communication needs and assist relief operations?
  A. When normal communication systems are overloaded, damaged or disrupted
  B. Only when the local RACES net is activated
  C. Never; only official emergency stations may transmit in a disaster
  D. When normal communication systems are working but are not convenient

## Slide 55: G2C02 During a disaster in the US, when may an amateur station make transmissions necessary to meet essential communication needs and assist relief operations?
A. When normal communication systems are overloaded, damaged or disrupted
  B. Only when the local RACES net is activated
  C. Never; only official emergency stations may transmit in a disaster
  D. When normal communication systems are working but are not convenient

## Slide 56: G2C03 If a disaster disrupts normal communications in your area, what may the FCC do?
  A. Declare a temporary state of communication emergency
  B. Temporarily seize your equipment for use in disaster communications
  C. Order all stations across the country to stop transmitting at once
  D. Nothing until the President declares the area a disaster area

## Slide 57: G2C03 If a disaster disrupts normal communications in your area, what may the FCC do?
A. Declare a temporary state of communication emergency
  B. Temporarily seize your equipment for use in disaster communications
  C. Order all stations across the country to stop transmitting at once
  D. Nothing until the President declares the area a disaster area

## Slide 58: G2C04 If a disaster disrupts normal communications in an area what would the FCC include in any notice of a temporary state of communication emergency?
  A. Any additional test questions needed for the licensing of amateur emergency communications workers
  B. A list of organizations authorized to temporarily seize your equipment for disaster communications
  C. Any special conditions requiring the use of non-commercial power systems
  D. Any special conditions and special rules to be observed by stations during the emergency

## Slide 59: G2C04 If a disaster disrupts normal communications in an area what would the FCC include in any notice of a temporary state of communication emergency?
  A. Any additional test questions needed for the licensing of amateur emergency communications workers
  B. A list of organizations authorized to temporarily seize your equipment for disaster communications
  C. Any special conditions requiring the use of non-commercial power systems
D. Any special conditions and special rules to be observed by stations during the emergency

## Slide 60: G2C05 During an emergency, what power output limitations must be observed by a station in distress?
  A. 200 watts PEP
  B. 1500 watts PEP
  C. 1000 watts PEP during daylight hours, reduced to 200 watts PEP during the night
  D. There are no limitations during an emergency

## Slide 61: G2C05 During an emergency, what power output limitations must be observed by a station in distress?
  A. 200 watts PEP
  B. 1500 watts PEP
  C. 1000 watts PEP during daylight hours, reduced to 200 watts PEP during the night
D. There are no limitations during an emergency

## Slide 62: G2C06 During a disaster in the US, what frequencies may be used to obtain assistance?
  A. Only frequencies in the 80-meter band
  B. Only frequencies in the 40-meter band
  C. Any frequency
  D. Any United Nations approved frequency

## Slide 63: G2C06 During a disaster in the US, what frequencies may be used to obtain assistance?
  A. Only frequencies in the 80-meter band
  B. Only frequencies in the 40-meter band
C. Any frequency
  D. Any United Nations approved frequency

## Slide 64: G2C07 If you are communicating with another amateur station and hear a station in distress break in, what is the first thing you should do?
  A. Continue your communication because you were on frequency first
  B. Acknowledge the station in distress and determine its location and what assistance may be needed
  C. Change to a different frequency so the station in distress may have a clear channel to call for assistance
  D. Immediately cease all transmissions because stations in distress have emergency rights to the frequency

## Slide 65: G2C07 If you are communicating with another amateur station and hear a station in distress break in, what is the first thing you should do?
  A. Continue your communication because you were on frequency first
B. Acknowledge the station in distress and determine its location and what assistance may be needed
  C. Change to a different frequency so the station in distress may have a clear channel to call for assistance
  D. Immediately cease all transmissions because stations in distress have emergency rights to the frequency

## Slide 66: G2C08 Why do stations in the Radio Amateur Civil Emergency Service (RACES) participate in training tests and drills?
  A. To provide orderly and efficient operations for the civil defense organization they serve in the event of an emergency
  B. To ensure that members attend monthly on-the-air meetings of the civil defense organization they serve
  C. To ensure that RACES members are able to conduct tests and drills
  D. To acquaint members of RACES with other members they may meet in an emergency

## Slide 67: G2C08 Why do stations in the Radio Amateur Civil Emergency Service (RACES) participate in training tests and drills?
A. To provide orderly and efficient operations for the civil defense organization they serve in the event of an emergency
  B. To ensure that members attend monthly on-the-air meetings of the civil defense organization they serve
  C. To ensure that RACES members are able to conduct tests and drills
  D. To acquaint members of RACES with other members they may meet in an emergency

## Slide 68: G2C09 When are you prohibited from helping a station in distress?
  A. When that station is not transmitting on amateur frequencies
  B. When the station in distress offers no call sign
  C. You are not ever prohibited from helping any station in distress
  D. When the station is not another amateur station

## Slide 69: G2C09 When are you prohibited from helping a station in distress?
  A. When that station is not transmitting on amateur frequencies
  B. When the station in distress offers no call sign
C. You are not ever prohibited from helping any station in distress
  D. When the station is not another amateur station

## Slide 70: G2C10 When FCC declares a temporary state of communication emergency, what must you do?
  A. Stay off the air until 30 days after FCC lifts the emergency notice
  B. Abide by the limitations or conditions set forth in the FCC notice
  C. Only communicate with stations within 2 miles of your location
  D. Nothing; wait until the President declares a formal emergency before taking further action

## Slide 71: G2C10 When FCC declares a temporary state of communication emergency, what must you do?
  A. Stay off the air until 30 days after FCC lifts the emergency notice
B. Abide by the limitations or conditions set forth in the FCC notice
  C. Only communicate with stations within 2 miles of your location
  D. Nothing; wait until the President declares a formal emergency before taking further action

## Slide 72: G2C11 During a disaster in the US, which of the following emission modes must be used to obtain assistance?
  A. Only SSB
  B. Only SSB and CW
  C. Any mode
  D. Only CW

## Slide 73: G2C11 During a disaster in the US, which of the following emission modes must be used to obtain assistance?
  A. Only SSB
  B. Only SSB and CW
C. Any mode
  D. Only CW

## Slide 74: G2C12 What information should anyone who sends a distress transmission give to stations who answer?
  A. The ITU region and grid square locator of the emergency
  B. The location and nature of the distress
  C. The time that the emergency occurred and the names of the persons involved
  D. The agencies to notify and the name of the emergency coordinator

## Slide 75: G2C12 What information should anyone who sends a distress transmission give to stations who answer?
  A. The ITU region and grid square locator of the emergency
B. The location and nature of the distress
  C. The time that the emergency occurred and the names of the persons involved
  D. The agencies to notify and the name of the emergency coordinator

## Slide 76: G2C13 What frequency should be used to send a distress call?
  A. Whatever frequency has the best chance of communicating the distress message
  B. 3873 kHz at night or 7285 kHz during the day
  C. Only frequencies that are within your operating privileges
  D. Only frequencies used by police, fire or emergency medical services

## Slide 77: G2C13 What frequency should be used to send a distress call?
A. Whatever frequency has the best chance of communicating the distress message
  B. 3873 kHz at night or 7285 kHz during the day
  C. Only frequencies that are within your operating privileges
  D. Only frequencies used by police, fire or emergency medical services

## Slide 78: G2D01 What is the Amateur Auxiliary to the FCC's Compliance and Information Bureau?
  A. Amateur volunteers who are formally enlisted to monitor the airwaves for rules violations
  B. Amateur volunteers who conduct amateur licensing examinations
  C. Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
  D. Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency

## Slide 79: G2D01 What is the Amateur Auxiliary to the FCC's Compliance and Information Bureau?
A. Amateur volunteers who are formally enlisted to monitor the airwaves for rules violations
  B. Amateur volunteers who conduct amateur licensing examinations
  C. Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
  D. Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency

## Slide 80: G2D02 What are the objectives of the Amateur Auxiliary to the FCC's Compliance and Information Bureau?
  A. To conduct efficient and orderly amateur licensing examinations
  B. To encourage amateur self-regulation and compliance with the rules
  C. To coordinate repeaters for efficient and orderly spectrum usage
  D. To provide emergency and public safety communications

## Slide 81: G2D02 What are the objectives of the Amateur Auxiliary to the FCC's Compliance and Information Bureau?
  A. To conduct efficient and orderly amateur licensing examinations
B. To encourage amateur self-regulation and compliance with the rules
  C. To coordinate repeaters for efficient and orderly spectrum usage
  D. To provide emergency and public safety communications

## Slide 82: G2D03 Why are direction-finding "Fox Hunts" important to the Amateur Auxiliary?
  A. Fox Hunts compel amateurs to upgrade their licenses
  B. Fox Hunts provide an opportunity to practice direction-finding skills
  C. Someone always receives an FCC Notice of Apparent Liability (NAL) when a Fox Hunt is concluded
  D. Fox Hunts allow amateurs to work together with Environmental Protection Agencies

## Slide 83: G2D03 Why are direction-finding "Fox Hunts" important to the Amateur Auxiliary?
  A. Fox Hunts compel amateurs to upgrade their licenses
B. Fox Hunts provide an opportunity to practice direction-finding skills
  C. Someone always receives an FCC Notice of Apparent Liability (NAL) when a Fox Hunt is concluded
  D. Fox Hunts allow amateurs to work together with Environmental Protection Agencies

## Slide 84: Azmuthal Projection Map
Notes: An Azmuthal map is a map projection centered on a particular location, used to determine the shortest path between points on the surface of the earth. From this map, centered on Seattle, it can be seen that San Diego is 165 degrees, Hawaii about 230 degrees and Anchorage, AK will be about 325 degrees for the shortest path. These bearings will likely be different than those from a standard Mercator projection because they account for the earth’s curvature.
It is possible to hear your own voice echo when transmitting. This is from a signal propagating all the way around the world via “long path”. This “long path” signal will be from exactly the opposite bearing (180 degrees different) and because one path may have daylight, where the other doesn’t, it is often possible to make a long path contact when short path doesn’t work.

## Slide 85: G2D04 What is an azimuthal projection map?
  A. A map projection centered on the North Pole
  B. A map projection centered on a particular location, used to determine the shortest path between points on the surface of the earth
  C. A map that shows the angle at which an amateur satellite crosses the equator
  D. A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit

## Slide 86: G2D04 What is an azimuthal projection map?
  A. A map projection centered on the North Pole
B. A map projection centered on a particular location, used to determine the shortest path between points on the surface of the earth
  C. A map that shows the angle at which an amateur satellite crosses the equator
  D. A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit

## Slide 87: G2D05 What is the most useful type of map to use when orienting a directional HF antenna toward a distant station?
  A. Azimuthal projection
  B. Mercator
  C. Polar projection
  D. Topographical

## Slide 88: G2D05 What is the most useful type of map to use when orienting a directional HF antenna toward a distant station?
A. Azimuthal projection
  B. Mercator
  C. Polar projection
  D. Topographical

## Slide 89: G2D06 A directional antenna pointed in the long-path direction to another station is generally oriented how many degrees from its short-path heading?
  A. 45 degrees
  B. 90 degrees
  C. 180 degrees
  D. 270 degrees

## Slide 90: G2D06 A directional antenna pointed in the long-path direction to another station is generally oriented how many degrees from its short-path heading?
  A. 45 degrees
  B. 90 degrees
C. 180 degrees
  D. 270 degrees

## Slide 91: Station Logs
Notes: Station logs generally include just the information supplied on a QSL card: date, time, callsign, frequency/band, signal report and mode. They generally include note fields to allow entering personal data like name and location or rig type, etc. Many hams have paper logbook that go back decades. More recently, computer logging has become popular because it has the ability to automatically generate much of the QSO data (date/time/frequency), can look up the other operator callsign in the FCC database and retrieve name and address and even generate and track QSL cards. Many will also track progress toward awards such as Worked All States or DXCC (100 countries). The only issue the reliability of this computer log vs. the old paper log books.

## Slide 92: G2D07 If a visiting amateur transmits from your station on 14.325 MHz, which of these is NOT true?
  A. You must first give permission for the visiting amateur to use your station
  B. You must keep in your station log the call sign of the visiting amateur together with the time and date of transmissions
  C. The FCC may think that you were the station's control operator, unless your station records show otherwise
  D. You both are equally responsible for the proper operation of the station

## Slide 93: G2D07 If a visiting amateur transmits from your station on 14.325 MHz, which of these is NOT true?
  A. You must first give permission for the visiting amateur to use your station
B. You must keep in your station log the call sign of the visiting amateur together with the time and date of transmissions
  C. The FCC may think that you were the station's control operator, unless your station records show otherwise
  D. You both are equally responsible for the proper operation of the station

## Slide 94: G2D08 Why should I keep a log if the FCC doesn't require it?
  A. To help with your reply, if FCC requests information on who was control operator of your station for a given date and time
  B. Logs provide information (callsigns, dates & times of contacts) used for many operating contests and awards
  C. Logs are necessary to accurately verify contacts made weeks, months or years earlier, especially when completing QSL cards
  D. All of these choices

## Slide 95: G2D08 Why should I keep a log if the FCC doesn't require it?
  A. To help with your reply, if FCC requests information on who was control operator of your station for a given date and time
  B. Logs provide information (callsigns, dates & times of contacts) used for many operating contests and awards
  C. Logs are necessary to accurately verify contacts made weeks, months or years earlier, especially when completing QSL cards
D. All of these choices

## Slide 96: G2D09 What information is normally contained in a station log?
  A. Date and time of contact
  B. Band and/or frequency of the contact
  C. Call sign of station contacted and the RST signal report given
  D. All of these choices

## Slide 97: G2D09 What information is normally contained in a station log?
  A. Date and time of contact
  B. Band and/or frequency of the contact
  C. Call sign of station contacted and the RST signal report given
D. All of these choices

## Slide 98: G2D10 Which of the following is a good reason to keep a log of your station's activities?
  A. It is required by the FCC's rules
  B. It is a tradition from the earliest days of amateur radio
  C. It can aid you in resolving interference complaints
  D. It can be a source of great enjoyment when reviewed in later years

## Slide 99: G2D10 Which of the following is a good reason to keep a log of your station's activities?
  A. It is required by the FCC's rules
  B. It is a tradition from the earliest days of amateur radio
C. It can aid you in resolving interference complaints
  D. It can be a source of great enjoyment when reviewed in later years

## Slide 100: G2D11 Which HF antenna would best be used to focus your signal to minimize interference?
  A. A bidirectional antenna
  B. A horizontal antenna positioned broadside to the desired direction
  C. A unidirectional antenna
  D. An omnidirectional antenna at low power

## Slide 101: G2D11 Which HF antenna would best be used to focus your signal to minimize interference?
  A. A bidirectional antenna
  B. A horizontal antenna positioned broadside to the desired direction
C. A unidirectional antenna
  D. An omnidirectional antenna at low power

## Slide 102: G2D12 Which of the following is required by the FCC rules when operating in the 60-meter band?
  A. If you are using other than a dipole antenna, you must keep a record of the gain of your antenna
  B. You must keep a record of the date, time, frequency, power level and stations worked
  C. No records are required
  D. You must keep a record of the manufacturer of your equipment and the antenna used

## Slide 103: G2D12 Which of the following is required by the FCC rules when operating in the 60-meter band?
A. If you are using other than a dipole antenna, you must keep a record of the gain of your antenna
  B. You must keep a record of the date, time, frequency, power level and stations worked
  C. No records are required
  D. You must keep a record of the manufacturer of your equipment and the antenna used

## Slide 104: G2E01 What type of messages may be transmitted to an amateur station in a foreign country?
  A. Messages of any type
  B. Messages that are not religious, political, or patriotic in nature
  C. Messages of a technical nature or personal remarks of relative unimportance
  D. Messages of any type, but only if the foreign country has a third-party communications agreement with the US

## Slide 105: G2E01 What type of messages may be transmitted to an amateur station in a foreign country?
  A. Messages of any type
  B. Messages that are not religious, political, or patriotic in nature
C. Messages of a technical nature or personal remarks of relative unimportance
  D. Messages of any type, but only if the foreign country has a third-party communications agreement with the US

## Slide 106: VOX – Voice Operation
Notes: Voice Operated (VOX) headsets and speaker/mikes are available. These permit hands-free operation by detecting the voice of the user and automatically activating the push-to-talk (PTT). Most of these unit offer a way to switch to manual operation to eliminate falsing (inadvertent transmissions) in a noisy environment. They also generally offer some means to control the sensitivity (gain) of the VOX circuitry. Better units include VOX delay to eliminate falsing on pulse noises and anti-VOX to prevent received audio from activating the transmitter.

## Slide 107: G2E02 Which of the following statements is true of VOX operation?
  A. The received signal is more natural sounding
  B. This mode allows "Hands Free' operation
  C. Frequency spectrum is conserved
  D. The duty cycle of the transmitter is reduced

## Slide 108: G2E02 Which of the following statements is true of VOX operation?
  A. The received signal is more natural sounding
B. This mode allows "Hands Free' operation
  C. Frequency spectrum is conserved
  D. The duty cycle of the transmitter is reduced

## Slide 109: G2E03 Which of the following user adjustable controls are usually associated with VOX circuitry?
  A. Anti-VOX
  B. VOX Delay
  C. VOX Sensitivity
  D. All of these choices are correct

## Slide 110: G2E03 Which of the following user adjustable controls are usually associated with VOX circuitry?
  A. Anti-VOX
  B. VOX Delay
  C. VOX Sensitivity
D. All of these choices are correct

## Slide 111: G2E04 What is the purpose of the VOX sensitivity control?
  A. To set the timing of transmitter activation
  B. To set the audio frequency range at which the transmitter activates
  C. To set the audio level at which the transmitter activates
  D. None of these choices is correct

## Slide 112: G2E04 What is the purpose of the VOX sensitivity control?
  A. To set the timing of transmitter activation
  B. To set the audio frequency range at which the transmitter activates
C. To set the audio level at which the transmitter activates
  D. None of these choices is correct

## Slide 113: International Telegraph Union (ITU) Regions
Notes: The airwaves are a shared resource that must be coordinated worldwide. The ITU is the body that does this. It’s important to recognize that the Americas are in Region 2. Europe including Russia and Africa are Region 1 and the rest of Asia is Region 3.

## Slide 114: G2E05 In which International Telecommunication Union Region is the continental United States?
  A. Region 1
  B. Region 2
  C. Region 3
  D. Region 4

## Slide 115: G2E05 In which International Telecommunication Union Region is the continental United States?
  A. Region 1
B. Region 2
  C. Region 3
  D. Region 4

## Slide 116: G2E06 In which International Telecommunication Union Region are Europe and Africa?
  A. Region 1
  B. Region 2
  C. Region 3
  D. Region 4

## Slide 117: G2E06 In which International Telecommunication Union Region are Europe and Africa?
A. Region 1
  B. Region 2
  C. Region 3
  D. Region 4

## Slide 118: G2E07 In which International Telecommunication Union Region is Australia?
  A. Region 1
  B. Region 2
  C. Region 3
  D. Region 4

## Slide 119: G2E07 In which International Telecommunication Union Region is Australia?
  A. Region 1
  B. Region 2
C. Region 3
  D. Region 4

## Slide 120: G2E08 Which of the following organizations is responsible for international regulation of the radio spectrum?
  A. The International Regulatory Commission
  B. The International Radio Union
  C. The International Telecommunications Union
  D. The International Frequency-Spectrum Commission

## Slide 121: G2E08 Which of the following organizations is responsible for international regulation of the radio spectrum?
  A. The International Regulatory Commission
  B. The International Radio Union
C. The International Telecommunications Union
  D. The International Frequency-Spectrum Commission

## Slide 122: G2E09 What do the initials "ITU" stand for?
  A. Interstate Telecommunications Union
  B. International Telephony Union
  C. International Transmission Union
  D. International Telecommunications Union

## Slide 123: G2E09 What do the initials "ITU" stand for?
  A. Interstate Telecommunications Union
  B. International Telephony Union
  C. International Transmission Union
D. International Telecommunications Union

## Slide 124: G2E10 What is the circuit called that causes a transmitter to automatically transmit when an operator speaks into its microphone?
  A. VXO
  B. VOX
  C. VCO
  D. VFO

## Slide 125: G2E10 What is the circuit called that causes a transmitter to automatically transmit when an operator speaks into its microphone?
  A. VXO
B. VOX
  C. VCO
  D. VFO

## Slide 126: G2E11 What is the best reason to use a headset with an attached microphone and VOX control when using a mobile station?
  A. For safer, hands-free operation
  B. It allows you to make quicker transmissions
  C. To eliminate ambient noise from your transmissions
  D. To reduce outside distractions while operating

## Slide 127: G2E11 What is the best reason to use a headset with an attached microphone and VOX control when using a mobile station?
A. For safer, hands-free operation
  B. It allows you to make quicker transmissions
  C. To eliminate ambient noise from your transmissions
  D. To reduce outside distractions while operating

## Slide 128: G2E12 What function does an anti-VOX circuit perform?
  A. It prevents received audio from keying the transmitter
  B. It prevents background noise from keying the transmitter
  C. It prevents unauthorized persons from keying the transmitter
  D. It prevents activation of the transmitter during CW operation

## Slide 129: G2E12 What function does an anti-VOX circuit perform?
A. It prevents received audio from keying the transmitter
  B. It prevents background noise from keying the transmitter
  C. It prevents unauthorized persons from keying the transmitter
  D. It prevents activation of the transmitter during CW operation

## Slide 130: G2E13 Which of the following would indicate the completion of the transmitting of a formal message when using phone?
  A. The phrase, "End of message"
  B. The word "Break"
  C. The Q-signal "QSL?"
  D. The Q-signal "QRV"

## Slide 131: G2E13 Which of the following would indicate the completion of the transmitting of a formal message when using phone?
A. The phrase, "End of message"
  B. The word "Break"
  C. The Q-signal "QSL?"
  D. The Q-signal "QRV"

## Slide 132: G2F01 Which of the following describes full break-in telegraphy (QSK)?
  A. Breaking stations send the Morse code prosign BK
  B. Automatic keyers are used to send Morse code instead of hand keys
  C. An operator must activate a manual send/receive switch before and after every transmission
  D. Incoming signals are received between transmitted key pulses

## Slide 133: G2F01 Which of the following describes full break-in telegraphy (QSK)?
  A. Breaking stations send the Morse code prosign BK
  B. Automatic keyers are used to send Morse code instead of hand keys
  C. An operator must activate a manual send/receive switch before and after every transmission
D. Incoming signals are received between transmitted key pulses

## Slide 134: G2F02 In what segment of the 80-meter band do most data transmissions take place?
  A. 3580 - 3620-kHz
  B. 3500 - 3525-kHz
  C. 3700 - 3750-kHz
  D. 3775 - 3825-kHz

## Slide 135: G2F02 In what segment of the 80-meter band do most data transmissions take place?
A. 3580 - 3620-kHz
  B. 3500 - 3525-kHz
  C. 3700 - 3750-kHz
  D. 3775 - 3825-kHz

## Slide 136: G2F03 In what segment of the 20-meter band do most RTTY transmissions take place?
  A. 14.000 - 14.050 MHz
  B. 14.070 - 14.095 MHz
  C. 14.150 - 14.225 MHz
  D. 14.275 - 14.350 MHz

## Slide 137: G2F03 In what segment of the 20-meter band do most RTTY transmissions take place?
  A. 14.000 - 14.050 MHz
B. 14.070 - 14.095 MHz
  C. 14.150 - 14.225 MHz
  D. 14.275 - 14.350 MHz

## Slide 138: G2F04 Which of the following is NOT correct?
  A. ASCII is a 7-bit code, with start, stop and parity bits
  B. The benefit of using AMTOR is its error detection and correction properties
  C. Baudot is a 5-bit code, with additional start and stop bits
  D. The two major AMTOR operating modes are SELCAL and LISTEN

## Slide 139: G2F04 Which of the following is NOT correct?
  A. ASCII is a 7-bit code, with start, stop and parity bits
  B. The benefit of using AMTOR is its error detection and correction properties
  C. Baudot is a 5-bit code, with additional start and stop bits
D. The two major AMTOR operating modes are SELCAL and LISTEN

## Slide 140: G2F05 What is the most common frequency shift for RTTY emissions in the amateur HF bands?
  A. 85 Hz
  B. 170 Hz
  C. 425 Hz
  D. 850 Hz

## Slide 141: G2F05 What is the most common frequency shift for RTTY emissions in the amateur HF bands?
  A. 85 Hz
B. 170 Hz
  C. 425 Hz
  D. 850 Hz

## Slide 142: G2F06 Why are the string of letters R and Y (sent as "RYRYRYRY...") occasionally used at the beginning of RTTY or other data transmissions?
  A. This allows time to 'tune in' a station prior to the actual message being sent
  B. To keep these commonly-used keys functional
  C. These are the important mark and space keys
  D. To make sure the transmitter is functional before sending a message

## Slide 143: G2F06 Why are the string of letters R and Y (sent as "RYRYRYRY...") occasionally used at the beginning of RTTY or other data transmissions?
A. This allows time to 'tune in' a station prior to the actual message being sent
  B. To keep these commonly-used keys functional
  C. These are the important mark and space keys
  D. To make sure the transmitter is functional before sending a message

## Slide 144: G2F07 What does the abbreviation "RTTY" stand for?
  A. "Returning to you", meaning "your turn to transmit"
  B. Radioteletype
  C. A general call to all digital stations
  D. Morse code practice over the air

## Slide 145: G2F07 What does the abbreviation "RTTY" stand for?
  A. "Returning to you", meaning "your turn to transmit"
B. Radioteletype
  C. A general call to all digital stations
  D. Morse code practice over the air

## Slide 146: G2F08 What prosign is sent using CW to indicate the end of a formal message?
  A. SK - I acknowledge
  B. BK - break
  C. AR - end of message
  D. KN - called station only, go ahead

## Slide 147: G2F08 What prosign is sent using CW to indicate the end of a formal message?
  A. SK - I acknowledge
  B. BK - break
C. AR - end of message
  D. KN - called station only, go ahead

## Slide 148: G2F09 What character sequence is sent using RTTY or other data modes to indicate the end of a formal message?
  A. CZCZ
  B. KKKK
  C. XXXXX
  D. NNNN

## Slide 149: G2F09 What character sequence is sent using RTTY or other data modes to indicate the end of a formal message?
  A. CZCZ
  B. KKKK
  C. XXXXX
D. NNNN

## Slide 150: G2F10 How many data bits are sent in a single PSK31 character?
  A. The number varies
  B. 5
  C. 7
  D. 8

## Slide 151: G2F10 How many data bits are sent in a single PSK31 character?
A. The number varies
  B. 5
  C. 7
  D. 8

## Slide 152: G2F11 What part of a data packet contains the routing and handling information?
  A. Directory
  B. Preamble
  C. Header
  D. Footer

## Slide 153: G2F11 What part of a data packet contains the routing and handling information?
  A. Directory
  B. Preamble
C. Header
  D. Footer