## Slide 1: T5 – Station Setup and Operation 4 exam questions – 4 groups
  T5A Station hookup – microphone, speaker, headphones, filters, power source, connecting a computer
  T5B Operating controls
  T5C Repeaters; repeater and simplex operating techniques, offsets, selective squelch, open and closed repeaters, linked repeaters
  T5D Recognition and correction of problems, symptoms of overload and overdrive, distortion, over and under modulation, RF feedback, off frequency signals, fading and noise, problems with digital communications links
Notes: 2006 Technician Class (Element 2) Master syllabus
Released 6 February, 2006
35 Exam questions
http://www.microhams.com
Created by Scott N7SS

## Slide 2: Icom IC-7000 Transceiver
Microphone
Speaker
VFO or Tuning Knob

## Slide 3: T5A01 What does a microphone connect to in a basic amateur radio station?
  A. The receiver
  B. The transmitter
  C. The SWR Bridge
  D. The Balun

## Slide 4: T5A01 What does a microphone connect to in a basic amateur radio station?
  A. The receiver
B. The transmitter
  C. The SWR Bridge
  D. The Balun

## Slide 5: T5A02 Which piece of station equipment converts electrical signals to sound waves?
  A. Frequency coordinator
  B. Frequency discriminator
  C. Speaker
  D. Microphone

## Slide 6: T5A02 Which piece of station equipment converts electrical signals to sound waves?
  A. Frequency coordinator
  B. Frequency discriminator
C. Speaker
  D. Microphone

## Slide 7: T5A03 What is the term used to describe what happens when a microphone and speaker are too close to each other?
  A. Excessive wind noise
  B. Audio feedback
  C. Inverted signal patterns
  D. Poor electrical grounding

## Slide 8: T5A03 What is the term used to describe what happens when a microphone and speaker are too close to each other?
  A. Excessive wind noise
B. Audio feedback
  C. Inverted signal patterns
  D. Poor electrical grounding

## Slide 9: T5A04 What could you use in place of a regular speaker to help you copy signals in a noisy area?
  A. A video display
  B. A low pass filter
  C. A set of headphones
  D. A boom microphone

## Slide 10: Communications Headset
Notes: Good communications headphones are not the same as HiFi headphones. HiFi headphones are designed to cover the entire range of human hearing (20-20,000Hz) equally well. Communications headphones are only designed to reproduce the 300-300Hz voice frequencies which helps reduce non-voice noise that might come out of the receiver. This model includes a boom microphone that minimizes background noise and insures consistent voice quality. Push-to-Talk (PTT) is via a foot switch on the floor to leave the operators hands free.

## Slide 11: T5A04 What could you use in place of a regular speaker to help you copy signals in a noisy area?
  A. A video display
  B. A low pass filter
C. A set of headphones
  D. A boom microphone

## Slide 12: T5A05 What is a good reason for using a regulated power supply for communications equipment?
  A. To protect equipment from voltage fluctuations
  B. A regulated power supply has FCC approval
  C. A fuse or circuit breaker regulates the power
  D. Regulated supplies are less expensive

## Slide 13: T5A05 What is a good reason for using a regulated power supply for communications equipment?
A. To protect equipment from voltage fluctuations
  B. A regulated power supply has FCC approval
  C. A fuse or circuit breaker regulates the power
  D. Regulated supplies are less expensive

## Slide 14: Low Pass, High Pass Filters
High Pass
Frequency
Low Pass
Frequency

## Slide 15: Low Pass Filter
The low pass filter is designed to remove harmonics and spurious emissions from the transmitted signal. If these signals are coming out of your transmitter they may indicate the transmitter needs an alignment rather than a filter.
The best test is to check an antenna connected TV in your house. If you cause TVI to your own set, it’s likely your problem to resolve.
Notes: If your harmonics are causing TVI problems, an MFJ-704 could keep your neighbors happy while you have fun hamming. MFJ's Super Low Pass filter simply plugs between your rig and antenna. It suppresses TVI, RFI, telephone and other interference by reducing unwanted harmonics going to your antenna. At the same time your HF signal passes on through with low loss so you can snag rare DX. Nine Chebyshev poles, MFJ's exclusive TeflonDielectric Technology capacitors, Hi-Q inductors, ground plane shielding and an RF tight cabinet give you excellent TVI and RFI protection. These exclusive Teflon Dielectric Technology capacitors give you extremely low loss and eliminate voltage breakdown and capacitor heating -- even at full legal power with a 2:1 SWR load! The result You get the lowest possible loss, excellent harmonic attenuation and years of trouble-free and TVI-free service. Handles full legal power from 1.8 to 30 MHz. SWR below 1.3 to 30 MHz into 50 Ohms. Attenuates above 40 MHz. Measures a compact 3x3x9 inches. Handy mounting tabs.

## Slide 16: High Pass Television Interference (TVI) Filter
This filter attaches to the input of the TV set and blocks HF frequencies (5-42MHz) that might enter. It’s shown here with caps over the coax (F) connectors. It is actually about the size of a finger and runs around $25.
Technically, the TVI this device filters (receiver overload) is a fault of the TV receiver not providing sufficient internal filtering and is the TV owner’s responsibility.
Notes: MFJ's ShieldBreaker high pass filter efecctively suppresses annoying TVI! Wipe out TVI caused by two-way, broadcast, commercial, amateur and CB radios operating below 30 MHz. Use between cable/antenna and TV/VCR. For 75 Ohm cable. Type F Male and female conenctors.

## Slide 17: T5A06 Where must a filter be installed to reduce spurious emissions?
  A. At the transmitter
  B. At the receiver
  C. At the station power supply
  D. At the microphone

## Slide 18: T5A06 Where must a filter be installed to reduce spurious emissions?
A. At the transmitter
  B. At the receiver
  C. At the station power supply
  D. At the microphone

## Slide 19: Band Pass Filter
Band Pass
High Frequency
Low Frequency

## Slide 20: Notch (Band Stop) Filter
Band Stop
High Frequency
Low Frequency

## Slide 21: Figuring out which filter you may need. Single
Determine the two bands that are interfering, and draw a line between them. 1 or 2 lines?
HF
TV

## Slide 22: T5A07 What type of filter should be connected to a TV receiver as the first step in trying to prevent RF overload from a nearby 2-meter transmitter?
  A. Low-pass filter
  B. High-pass filter
  C. Band pass filter
  D. Notch filter

## Slide 23: T5A07 What type of filter should be connected to a TV receiver as the first step in trying to prevent RF overload from a nearby 2-meter transmitter?
  A. Low-pass filter
  B. High-pass filter
  C. Band pass filter
D. Notch filter

## Slide 24: T5A08 What is connected between the transceiver and computer terminal in a packet radio station?
  A. Transmatch
  B. Mixer
  C. Terminal Node Controller
  D. Antenna

## Slide 25: Terminal Node Controllers (TNC) (Radio Modems)

## Slide 26: T5A08 What is connected between the transceiver and computer terminal in a packet radio station?
  A. Transmatch
  B. Mixer
C. Terminal Node Controller
  D. Antenna

## Slide 27: T5A09 Which of these items is not required for a packet radio station?
  A. Antenna
  B. Transceiver
  C. Power source
  D. Microphone

## Slide 28: T5A09 Which of these items is not required for a packet radio station?
  A. Antenna
  B. Transceiver
  C. Power source
D. Microphone

## Slide 29: T5A10 What can be used to connect a radio with a computer for data transmission?
  A. Balun
  B. Sound Card
  C. Impedance matcher
  D. Autopatch

## Slide 30: T5A10 What can be used to connect a radio with a computer for data transmission?
  A. Balun
B. Sound Card
  C. Impedance matcher
  D. Autopatch

## Slide 31: Icom IC-7000 Multimode Transceiver
Keypad for band changes and frequency entry
Volume/Squelch Control
VFO or Tuning Knob
Noise Blanker
Up/Down Buttons
RIT
Tune Step (TS)

## Slide 32: Icom IC-T90 Tri-band Transceiver
Up/Down Buttons
Tune Step
RIT
Function (F) Button
Push to Talk (PTT)
Numeric Keypad
Duplex (Shift) Key
Duplex (Shift) Indicator
Memory Channel
Signal Strength “S-meter”
VFO Mode
Memory Mode
Microphone
Speaker

## Slide 33: T5B01 What may happen if a transmitter is operated with the microphone gain set too high?
  A. The output power will be too high
  B. It may cause the signal to become distorted and unreadable
  C. The frequency will vary
  D. The SWR will increase

## Slide 34: T5B01 What may happen if a transmitter is operated with the microphone gain set too high?
  A. The output power will be too high
B. It may cause the signal to become distorted and unreadable
  C. The frequency will vary
  D. The SWR will increase

## Slide 35: T5B02 What kind of information may a VHF/UHF transceiver be capable of storing in memory?
  A. Transmit and receive operating frequency
  B. CTCSS tone frequency
  C. Transmit power level
  D. All of these answers are correct

## Slide 36: T5B02 What kind of information may a VHF/UHF transceiver be capable of storing in memory?
  A. Transmit and receive operating frequency
  B. CTCSS tone frequency
  C. Transmit power level
D. All of these answers are correct

## Slide 37: T5B03 What is one way to select a frequency on which to operate?
  A. Use the keypad or VFO knob to enter the correct frequency
  B. Turn on the CTCSS encoder
  C. Adjust the power supply ripple frequency
  D. All of these answers are correct

## Slide 38: T5B03 What is one way to select a frequency on which to operate?
A. Use the keypad or VFO knob to enter the correct frequency
  B. Turn on the CTCSS encoder
  C. Adjust the power supply ripple frequency
  D. All of these answers are correct

## Slide 39: T5B04 What is the purpose of the squelch control on a transceiver?
  A. It is used to set the highest level of volume desired
  B. It is used to set the transmitter power level
  C. It is used to adjust the antenna polarization
  D. It is used to quiet noise when no signal is being received

## Slide 40: T5B04 What is the purpose of the squelch control on a transceiver?
  A. It is used to set the highest level of volume desired
  B. It is used to set the transmitter power level
  C. It is used to adjust the antenna polarization
D. It is used to quiet noise when no signal is being received

## Slide 41: T5B05 What is a way to enable quick access to a favorite frequency on your transceiver?
  A. Enable the CTCSS tones
  B. Store the frequency in a memory channel
  C. Disable the CTCSS tones
  D. Use the scan mode to select the desired frequency

## Slide 42: T5B05 What is a way to enable quick access to a favorite frequency on your transceiver?
  A. Enable the CTCSS tones
B. Store the frequency in a memory channel
  C. Disable the CTCSS tones
  D. Use the scan mode to select the desired frequency

## Slide 43: T5B06 What might you do to improve the situation if the station you are listening to is hard to copy because of ignition noise interference?
  A. Increase your transmitter power
  B. Decrease the squelch setting
  C. Turn on the noise blanker
  D. Use the RIT control

## Slide 44: T5B06 What might you do to improve the situation if the station you are listening to is hard to copy because of ignition noise interference?
  A. Increase your transmitter power
  B. Decrease the squelch setting
C. Turn on the noise blanker
  D. Use the RIT control

## Slide 45: T5B07 What is the purpose of the buttons labeled "up" and "down" on many microphones?
  A. To allow easy frequency or memory selection
  B. To raise or lower the internal antenna
  C. To set the battery charge rate
  D. To upload or download messages

## Slide 46: T5B07 What is the purpose of the buttons labeled "up" and "down" on many microphones?
A. To allow easy frequency or memory selection
  B. To raise or lower the internal antenna
  C. To set the battery charge rate
  D. To upload or download messages

## Slide 47: T5B08 What is the purpose of the "shift" control found on many VHF/UHF transceivers?
  A. Adjust transmitter power level
  B. Change bands
  C. Adjust the offset between transmit and receive frequency
  D. Change modes

## Slide 48: T5B08 What is the purpose of the "shift" control found on many VHF/UHF transceivers?
  A. Adjust transmitter power level
  B. Change bands
C. Adjust the offset between transmit and receive frequency
  D. Change modes

## Slide 49: T5B09 What does RIT mean?
  A. Receiver Input Tone
  B. Receiver Incremental Tuning
  C. Rectifier Inverter Test
  D. Remote Input Transmitter

## Slide 50: T5B09 What does RIT mean?
  A. Receiver Input Tone
B. Receiver Incremental Tuning
  C. Rectifier Inverter Test
  D. Remote Input Transmitter

## Slide 51: T5B10 What is the purpose of the "step" menu function found on many transceivers?
  A. It adjusts the transmitter power output level
  B. It adjusts the modulation level
  C. It sets the earphone volume
  D. It sets the tuning rate when changing frequencies

## Slide 52: T5B10 What is the purpose of the "step" menu function found on many transceivers?
  A. It adjusts the transmitter power output level
  B. It adjusts the modulation level
  C. It sets the earphone volume
D. It sets the tuning rate when changing frequencies

## Slide 53: T5B11 What is the purpose of the "function" or "F" key found on many transceivers?
  A. It turns the power on and off
  B. It selects the autopatch access code
  C. It selects an alternate action for some control buttons
  D. It controls access to the memory scrambler

## Slide 54: T5B11 What is the purpose of the "function" or "F" key found on many transceivers?
  A. It turns the power on and off
  B. It selects the autopatch access code
C. It selects an alternate action for some control buttons
  D. It controls access to the memory scrambler

## Slide 55: T5C01 What is one purpose of a repeater?
  A. To cut your power bill by using someone else's higher power system
  B. To extend the usable range of mobile and low-power stations
  C. To transmit signals for observing propagation and reception
  D. To communicate with stations in services other than amateur

## Slide 56: Repeater Operation
60+ miles
Output Freq
145.21 MHz
Input Freq
144.61 MHz
Offset
- 600 kHz

## Slide 57: K7MMI Repeater Site on Cougar Mountain
Output | Input | Tone
53.310 | 51.610 | 156.7 Hz
146.980 | - (146.380) | 156.7 Hz
224.440 | - (222.840) | 156.7 Hz
442.325 | + (447.325) | 156.7 Hz

## Slide 58: K7MMI Repeater Diagram

## Slide 59: Repeater Input/Output Offsets
Band | Offset
6 meters | 1 MHz
2 meters | 600 kHz
1.25 meters | 1.6 MHz
70 cm | 5 MHz
33 cm | 12 MHz
23 cm | 20 MHz

## Slide 60: T5C01 What is one purpose of a repeater?
  A. To cut your power bill by using someone else's higher power system
B. To extend the usable range of mobile and low-power stations
  C. To transmit signals for observing propagation and reception
  D. To communicate with stations in services other than amateur

## Slide 61: T5C02 What is a courtesy tone?
  A. A tone used to identify the repeater
  B. A tone used to indicate when a transmission is complete
  C. A tone used to indicate that a message is waiting for someone
  D. A tone used to activate a receiver in case of severe weather

## Slide 62: T5C02 What is a courtesy tone?
  A. A tone used to identify the repeater
B. A tone used to indicate when a transmission is complete
  C. A tone used to indicate that a message is waiting for someone
  D. A tone used to activate a receiver in case of severe weather

## Slide 63: T5C03 Which of the following is the most important information to know before using a repeater?
  A. The repeater input and output frequencies
  B. The repeater call sign
  C. The repeater power level
  D. Whether or not the repeater has an autopatch

## Slide 64: T5C03 Which of the following is the most important information to know before using a repeater?
A. The repeater input and output frequencies
  B. The repeater call sign
  C. The repeater power level
  D. Whether or not the repeater has an autopatch

## Slide 65: T5C04 Why should you pause briefly between transmissions when using a repeater?
  A. To let your radio cool off
  B. To reach for pencil and paper so you can take notes
  C. To listen for anyone wanting to break in
  D. To dial up the repeater's autopatch

## Slide 66: T5C04 Why should you pause briefly between transmissions when using a repeater?
  A. To let your radio cool off
  B. To reach for pencil and paper so you can take notes
C. To listen for anyone wanting to break in
  D. To dial up the repeater's autopatch

## Slide 67: T5C05 What is the most common input/output frequency offset for repeaters in the 2-meter band?
  A. 0.6 MHz
  B. 1.0 MHz
  C. 1.6 MHz
  D. 5.0 MHz

## Slide 68: T5C05 What is the most common input/output frequency offset for repeaters in the 2-meter band?
A. 0.6 MHz
  B. 1.0 MHz
  C. 1.6 MHz
  D. 5.0 MHz

## Slide 69: T5C06 What is the most common input/output frequency offset for repeaters in the 70-centimeter band?
  A. 600 kHz
  B. 1.0 MHz
  C. 1.6 MHz
  D. 5.0 MHz

## Slide 70: T5C06 What is the most common input/output frequency offset for repeaters in the 70-centimeter band?
  A. 600 kHz
  B. 1.0 MHz
  C. 1.6 MHz
D. 5.0 MHz

## Slide 71: T5C07 What is meant by the terms input and output frequency when referring to repeater operations?
  A. The repeater receives on one frequency and transmits on another
  B. The repeater offers a choice of operating frequencies
  C. One frequency is used to control the repeater and another is used to retransmit received signals
  D. The repeater must receive an access code on one frequency before it will begin transmitting

## Slide 72: T5C07 What is meant by the terms input and output frequency when referring to repeater operations?
A. The repeater receives on one frequency and transmits on another
  B. The repeater offers a choice of operating frequencies
  C. One frequency is used to control the repeater and another is used to retransmit received signals
  D. The repeater must receive an access code on one frequency before it will begin transmitting

## Slide 73: T5C08 What is the meaning of the term simplex operation?
  A. Transmitting and receiving on the same frequency
  B. Transmitting and receiving over a wide area
  C. Transmitting on one frequency and receiving on another
  D. Transmitting one-way communications

## Slide 74: T5C08 What is the meaning of the term simplex operation?
A. Transmitting and receiving on the same frequency
  B. Transmitting and receiving over a wide area
  C. Transmitting on one frequency and receiving on another
  D. Transmitting one-way communications

## Slide 75: T5C09 What is a reason to use simplex instead of a repeater?
  A. When the most reliable communications are needed
  B. To avoid tying up the repeater when direct contact is possible
  C. When an emergency telephone call is needed
  D. When you are traveling and need some local information

## Slide 76: T5C09 What is a reason to use simplex instead of a repeater?
  A. When the most reliable communications are needed
B. To avoid tying up the repeater when direct contact is possible
  C. When an emergency telephone call is needed
  D. When you are traveling and need some local information

## Slide 77: T5C10 How might you find out if you could communicate with a station using simplex instead of a repeater?
  A. Check the repeater input frequency to see if you can hear the other station
  B. Check to see if you can hear the other station on a different frequency band
  C. Check to see if you can hear a more distant repeater
  D. Check to see if a third station can hear both of you

## Slide 78: T5C10 How might you find out if you could communicate with a station using simplex instead of a repeater?
A. Check the repeater input frequency to see if you can hear the other station
  B. Check to see if you can hear the other station on a different frequency band
  C. Check to see if you can hear a more distant repeater
  D. Check to see if a third station can hear both of you

## Slide 79: T5C11 What is the term for a series of repeaters that can be connected to one another to provide users with a wider coverage?
  A. Open repeater system
  B. Closed repeater system
  C. Linked repeater system
  D. Locked repeater system

## Slide 80: T5C11 What is the term for a series of repeaters that can be connected to one another to provide users with a wider coverage?
  A. Open repeater system
  B. Closed repeater system
C. Linked repeater system
  D. Locked repeater system

## Slide 81: T5C12 What is the main reason repeaters should be approved by the local frequency coordinator before being installed?
  A. Coordination minimizes interference between repeaters and makes the most efficient use of available frequencies
  B. Coordination is required by the FCC
  C. Repeater manufacturers have exclusive territories and you could be fined for using the wrong equipment
  D. Only coordinated systems will be approved by the officers of the local radio club

## Slide 82: T5C12 What is the main reason repeaters should be approved by the local frequency coordinator before being installed?
A. Coordination minimizes interference between repeaters and makes the most efficient use of available frequencies
  B. Coordination is required by the FCC
  C. Repeater manufacturers have exclusive territories and you could be fined for using the wrong equipment
  D. Only coordinated systems will be approved by the officers of the local radio club

## Slide 83: T5C13 Which of the following statements regarding use of repeaters is true?
  A. All amateur radio operators have the right to use any repeater at any time
  B. Access to any repeater may be limited by the repeater owner
  C. Closed repeaters must be opened at the request of any amateur wishing to use it
  D. Open repeaters are required to use CTCSS tones for access

## Slide 84: T5C13 Which of the following statements regarding use of repeaters is true?
  A. All amateur radio operators have the right to use any repeater at any time
B. Access to any repeater may be limited by the repeater owner
  C. Closed repeaters must be opened at the request of any amateur wishing to use it
  D. Open repeaters are required to use CTCSS tones for access

## Slide 85: T5C14 What term is used to describe a repeater when use is restricted to the members of a club or group?
  A. A beacon station
  B. An open repeater
  C. A auxiliary station
  D. A closed repeater

## Slide 86: T5C14 What term is used to describe a repeater when use is restricted to the members of a club or group?
  A. A beacon station
  B. An open repeater
  C. A auxiliary station
D. A closed repeater

## Slide 87: T5D01 What is meant by fundamental overload in reference to a receiver?
  A. Too much voltage from the power supply
  B. Too much current from the power supply
  C. Interference caused by very strong signals from a nearby source
  D. Interference caused by turning the volume up too high

## Slide 88: T5D01 What is meant by fundamental overload in reference to a receiver?
  A. Too much voltage from the power supply
  B. Too much current from the power supply
C. Interference caused by very strong signals from a nearby source
  D. Interference caused by turning the volume up too high

## Slide 89: T5D02 Which of the following is NOT a cause of radio frequency interference?
  A. Fundamental overload
  B. Doppler shift
  C. Spurious emissions
  D. Harmonics

## Slide 90: T5D02 Which of the following is NOT a cause of radio frequency interference?
  A. Fundamental overload
B. Doppler shift
  C. Spurious emissions
  D. Harmonics

## Slide 91: T5D03 What is the most likely cause of telephone interference from a nearby transmitter?
  A. Harmonics from the transmitter
  B. The transmitter's signals are causing the telephone to act like a radio receiver
  C. Poor station grounding
  D. Improper transmitter adjustment

## Slide 92: T5D03 What is the most likely cause of telephone interference from a nearby transmitter?
  A. Harmonics from the transmitter
B. The transmitter's signals are causing the telephone to act like a radio receiver
  C. Poor station grounding
  D. Improper transmitter adjustment

## Slide 93: T5D04 What is a logical first step when attempting to cure a radio frequency interference problem in a nearby telephone?
  A. Install a low-pass filter at the transmitter
  B. Install a high-pass filter at the transmitter
  C. Install an RF filter at the telephone
  D. Improve station grounding

## Slide 94: T5D04 What is a logical first step when attempting to cure a radio frequency interference problem in a nearby telephone?
  A. Install a low-pass filter at the transmitter
  B. Install a high-pass filter at the transmitter
C. Install an RF filter at the telephone
  D. Improve station grounding

## Slide 95: T5D05 What should you do first if someone tells you that your transmissions are interfering with their TV reception?
  A. Make sure that your station is operating properly and that it does not cause interference to your own television
  B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
  C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
  D. Continue operating normally because your equipment cannot possibly cause any interference

## Slide 96: T5D05 What should you do first if someone tells you that your transmissions are interfering with their TV reception?
A. Make sure that your station is operating properly and that it does not cause interference to your own television
  B. Immediately turn off your transmitter and contact the nearest FCC office for assistance
  C. Tell them that your license gives you the right to transmit and nothing can be done to reduce the interference
  D. Continue operating normally because your equipment cannot possibly cause any interference

## Slide 97: T5D07 Which of the following may be useful in correcting a radio frequency interference problem?
  A. Snap-on ferrite chokes
  B. Low-pass and high-pass filters
  C. Notch and band-pass filters
  D. All of these answers are correct

## Slide 98: T5D07 Which of the following may be useful in correcting a radio frequency interference problem?
  A. Snap-on ferrite chokes
  B. Low-pass and high-pass filters
  C. Notch and band-pass filters
D. All of these answers are correct

## Slide 99: T5D08 What is the proper course of action to take when a neighbor reports that your radio signals are interfering with something in his home?
  A. You are not required to do anything
  B. Contact the FCC to see if other interference reports have been filed
  C. Check your station and make sure it meets the standards of good amateur practice
  D. Change your antenna polarization from vertical to horizontal

## Slide 100: T5D08 What is the proper course of action to take when a neighbor reports that your radio signals are interfering with something in his home?
  A. You are not required to do anything
  B. Contact the FCC to see if other interference reports have been filed
C. Check your station and make sure it meets the standards of good amateur practice
  D. Change your antenna polarization from vertical to horizontal

## Slide 101: T5D09 What should you do if a "Part 15" device in your neighbor’s home is causing harmful interference to your amateur station?
  A. Work with your neighbor to identify the offending device
  B. Politely inform your neighbor about the rules that require him to stop using the device if it causes interference
  C. Check your station and make sure it meets the standards of good amateur practice
  D. All of these answers are correct

## Slide 102: T5D09 What should you do if a "Part 15" device in your neighbor’s home is causing harmful interference to your amateur station?
  A. Work with your neighbor to identify the offending device
  B. Politely inform your neighbor about the rules that require him to stop using the device if it causes interference
  C. Check your station and make sure it meets the standards of good amateur practice
D. All of these answers are correct

## Slide 103: T5D10 What could be happening if another operator tells you he is hearing a variable high-pitched whine on the signals from your mobile transmitter?
  A. Your microphone is picking up noise from an open window
  B. You have the volume on your receiver set too high
  C. You need to adjust your squelch control
  D. The power wiring for your radio is picking up noise from the vehicle's electrical system

## Slide 104: T5D10 What could be happening if another operator tells you he is hearing a variable high-pitched whine on the signals from your mobile transmitter?
  A. Your microphone is picking up noise from an open window
  B. You have the volume on your receiver set too high
  C. You need to adjust your squelch control
D. The power wiring for your radio is picking up noise from the vehicle's electrical system

## Slide 105: T5D11 What may be the problem if another operator reports that your SSB signal is very garbled and breaks up?
  A. You have the noise limiter turned on
  B. The transmitter is too hot and needs to cool off
  C. RF energy may be getting into the microphone circuit and causing feedback
  D. You are operating on lower sideband

## Slide 106: T5D11 What may be the problem if another operator reports that your SSB signal is very garbled and breaks up?
  A. You have the noise limiter turned on
  B. The transmitter is too hot and needs to cool off
C. RF energy may be getting into the microphone circuit and causing feedback
  D. You are operating on lower sideband

## Slide 107: T5D12 What might be the problem if you receive a report that your signal through the repeater is distorted or weak?
  A. Your transmitter may be slightly off frequency
  B. Your batteries may be running low
  C. You could be in a bad location
  D. All of these answers are correct

## Slide 108: T5D12 What might be the problem if you receive a report that your signal through the repeater is distorted or weak?
  A. Your transmitter may be slightly off frequency
  B. Your batteries may be running low
  C. You could be in a bad location
D. All of these answers are correct

## Slide 109: T5D13 What is one of the reasons to use digital signals instead of analog signals to communicate with another station?
  A. Digital systems are less expensive than analog systems
  B. Many digital systems can automatically correct errors caused by noise and interference
  C. Digital modulation circuits are much less complicated than any other types
  D. All digital signals allow higher transmit power levels

## Slide 110: T5D13 What is one of the reasons to use digital signals instead of analog signals to communicate with another station?
  A. Digital systems are less expensive than analog systems
B. Many digital systems can automatically correct errors caused by noise and interference
  C. Digital modulation circuits are much less complicated than any other types
  D. All digital signals allow higher transmit power levels