## Slide 1: T9 – Radio Waves, Propagation and Antennas 3 exam questions – 3 groups
  T9A Antenna types – vertical, horizontal, concept of gain, common portable and mobile antennas, losses with short antennas, relationships between antenna length and frequency, dummy loads
  T9B Propagation, fading, multipath distortion, reflections, radio horizon, terrain blocking, wavelength vs. penetration, antenna orientation
  T9C Feedlines types, losses vs. frequency, SWR concepts, measuring SWR, matching and power transfer, weather protection, feedline failure modes
Notes: 2006 Technician Class (Element 2) Master syllabus
Released 6 February, 2006
35 Exam questions
http://www.microhams.com
Created by Scott N7SS

## Slide 2: Antenna Classifications
Orientation
  Horizontal – parallel to the Earth
  Vertical – perpendicular to the Earth
Directivity (Beam)
  Yagi, Log Periodic, Quad, Dish
Size
  Wavelength – λ
  ½ λ, ¼ λ, ⅝ λ, …
Notes: Antennas can be classified in any number of ways. For example their orientation, size, shape. We can also classify them by and operation parameter such as gain, directivity, impedance. We can also arrange them by physical properties line flexible, shortened, loaded, active, etc. There are lots of ways to classify them.
For the test, there are three thing we care about: Orientation, Directivity and Size.

## Slide 3: Horizontal Antennas (½ Wavelength Dipole Antenna)
Length of dipole in inches =
5600
F (MHz)
Half wavelength from formula
Open wire feeder
Solder
Spacer

## Slide 4: ½ λ Dipole Radiation
Radiation pattern for a dipole placed ½ λ
above ground looking down from above the antenna.
Looks like a doughnut around the wire in 3D space.
Pattern distorts to omnidirectional when placed low to the ground.
Notes: A dipole is a a half wavelength piece of wire connected at the center (1/4 wave on each side). If the dipole antenna was the red line, the lobes above and below show the radiation pattern at ½ wavelength above the ground. This pattern actually rotates around the wire like a donut. As the antenna is lowered below ½ wavelength, the lobes flatten until it becomes nearly omnidirectional.

## Slide 5: Vertical Antennas (Quarter Wavelength Vertical)
Length of vertical in inches =
2600
F (MHz)
Ground Plane
Ground Plane
Ground
Marconi
Radials

## Slide 6: Quarter Wave Vertical Radiation
A side view of the radiation pattern of a 1/4 wave vertical. From above the pattern is round like a doughnut. A perfect ground would be the center of a metal car roof at VHF.

Maximum Radiation Angle
Elevation
0 dB= 5.10 dBi
7.150 MHz
Perfect Ground
Average Ground

## Slide 7: Beam Antennas (Yagi Antenna)
Gain
Boom
Feedline
Reflector
Director
Driven Element
The reflector
acts like a
mirror
The director
acts like a
lens
Notes: Note the driven element with the balun attached, the smaller directors, larger reflector and the pattern with a large front lobe. The driven element is approximately a half have dipole. As parasitic elements (directors and reflectors) are added and the boom length is increased, the more gain is provided by the antenna. Reflectors are placed behind the driven element to reflect the power forward and the directors act as conductors in front of the wave. Reflectors are generally ~3% longer than the driven element and directors ~3% shorter. Five element yagis like this one yield 10-12dB gain over a dipole, based on the design of the antenna.
Antenna designers have to balance forward gain, front-to-back ratio, bandwidth and feedpoint impedance when designing an antenna. Some antennas will be optimized for maximum forward gain to improve their output and others may have better front-to-back rations to improve their noise rejection. Antenna bandwidth can be increased by using larger diameter elements. Gain is largely a function of boom length.

## Slide 8: Yagi Radiation Pattern
The yagi antenna
focuses RF energy in
one direction, giving
the appearance of
getting “free power.”
This free power or Effective Radiated Power (ERP) can be expressed as antenna Gain in Decibels (dB).

## Slide 9: T9A01 What is a beam antenna?
  A. An antenna built from metal I-beams
  B. An antenna that transmits and receives equally well in all directions
  C. An antenna that concentrates signals in one direction
  D. An antenna that reverses the phase of received signals

## Slide 10: T9A01 What is a beam antenna?
  A. An antenna built from metal I-beams
  B. An antenna that transmits and receives equally well in all directions
C. An antenna that concentrates signals in one direction
  D. An antenna that reverses the phase of received signals

## Slide 11: T9A02 What is an antenna that consists of a single element mounted perpendicular to the Earth's surface?
  A. A conical monopole
  B. A horizontal antenna
  C. A vertical antenna
  D. A traveling wave antenna

## Slide 12: T9A02 What is an antenna that consists of a single element mounted perpendicular to the Earth's surface?
  A. A conical monopole
  B. A horizontal antenna
C. A vertical antenna
  D. A traveling wave antenna

## Slide 13: T9A03 What type of antenna is a simple dipole mounted so the elements are parallel to the Earth's surface?
  A. A ground wave antenna
  B. A horizontal antenna
  C. A rhombic antenna
  D. A vertical antenna

## Slide 14: T9A03 What type of antenna is a simple dipole mounted so the elements are parallel to the Earth's surface?
  A. A ground wave antenna
B. A horizontal antenna
  C. A rhombic antenna
  D. A vertical antenna

## Slide 15: T9A04 What is a disadvantage of the "rubber duck" antenna supplied with most hand held radio transceivers?
  A. It does not transmit or receive as effectively as a full sized antenna
  B. It is much more expensive than a standard antenna
  C. If the rubber end cap is lost it will unravel very quickly
  D. It transmits a circular polarized signal

## Slide 16: T9A04 What is a disadvantage of the "rubber duck" antenna supplied with most hand held radio transceivers?
A. It does not transmit or receive as effectively as a full sized antenna
  B. It is much more expensive than a standard antenna
  C. If the rubber end cap is lost it will unravel very quickly
  D. It transmits a circular polarized signal

## Slide 17: T9A05 How does the physical size of half-wave dipole antenna change with operating frequency?
  A. It becomes longer as the frequency increases
  B. It must be made larger because it has to handle more power
  C. It becomes shorter as the frequency increases
  D. It becomes shorter as the frequency decreases

## Slide 18: T9A05 How does the physical size of half-wave dipole antenna change with operating frequency?
  A. It becomes longer as the frequency increases
  B. It must be made larger because it has to handle more power
C. It becomes shorter as the frequency increases
  D. It becomes shorter as the frequency decreases

## Slide 19: T9A06 What is the advantage of 5/8 wavelength over 1/4 wavelength vertical antennas?
  A. They are easier to match to the feed line than other types
  B. Their radiation pattern concentrates energy at lower angles
  C. They pick up less noise
  D. Their radiation pattern concentrates energy at higher angles

## Slide 20: T9A06 What is the advantage of 5/8 wavelength over 1/4 wavelength vertical antennas?
  A. They are easier to match to the feed line than other types
B. Their radiation pattern concentrates energy at lower angles
  C. They pick up less noise
  D. Their radiation pattern concentrates energy at higher angles

## Slide 21: T9A07 What is the primary purpose of a dummy load?
  A. It does not radiate interfering signals when making tests
  B. It will prevent over-modulation of your transmitter
  C. It keeps you from making mistakes while on the air
  D. It is used for close in work to prevent overloads

## Slide 22: T9A07 What is the primary purpose of a dummy load?
A. It does not radiate interfering signals when making tests
  B. It will prevent over-modulation of your transmitter
  C. It keeps you from making mistakes while on the air
  D. It is used for close in work to prevent overloads

## Slide 23: T9A08 What type of antennas are the quad, Yagi, and dish?
  A. Antennas invented after 1985
  B. Loop antennas
  C. Directional or beam antennas
  D. Antennas that are not permitted for amateur radio stations

## Slide 24: T9A08 What type of antennas are the quad, Yagi, and dish?
  A. Antennas invented after 1985
  B. Loop antennas
C. Directional or beam antennas
  D. Antennas that are not permitted for amateur radio stations

## Slide 25: T9A09 What is one type of antenna that offers good efficiency when operating mobile and can be easily installed or removed?
  A. A microwave antenna
  B. A quad antenna
  C. A traveling wave antenna
  D. A magnet mount vertical antenna

## Slide 26: T9A09 What is one type of antenna that offers good efficiency when operating mobile and can be easily installed or removed?
  A. A microwave antenna
  B. A quad antenna
  C. A traveling wave antenna
D. A magnet mount vertical antenna

## Slide 27: T9A10 What is a good reason not to use a "rubber duck" antenna inside your car?
  A. Signals can be 10 to 20 times weaker than when you are outside of the vehicle
  B. RF energy trapped inside the vehicle can distort your signal
  C. You might cause a fire in the vehicle upholstery
  D. The SWR might increase

## Slide 28: T9A10 What is a good reason not to use a "rubber duck" antenna inside your car?
A. Signals can be 10 to 20 times weaker than when you are outside of the vehicle
  B. RF energy trapped inside the vehicle can distort your signal
  C. You might cause a fire in the vehicle upholstery
  D. The SWR might increase

## Slide 29: T9A11 What is the approximate length, in inches, of a quarter-wavelength vertical antenna for 146 MHz?
  A. 112 inches
  B. 50 inches
  C. 19 inches
  D. 12 inches

## Slide 30: Calculating Vertical Antenna Length
Precisely:
2600
F (MHz)
=
2600 146
=
17.8 inches
Approximately:
146 MHz is 2m band ¼ of 2m is 0.5m 1m is 39 inches so 0.5m is 19.5 inches
Note this is based on free space wavelength. A wave traveling through wire will be slower and have a shorter wavelength.

## Slide 31: T9A11 What is the approximate length, in inches, of a quarter-wavelength vertical antenna for 146 MHz?
  A. 112 inches
  B. 50 inches
C. 19 inches
  D. 12 inches

## Slide 32: T9A12 What is the approximate length, in inches, of a 6-meter 1/2 wavelength wire dipole antenna?
  A. 6 inches
  B. 50 inches
  C. 112 inches
  D. 236 inches

## Slide 33: Calculating Dipole Antenna Length
Precisely:
5200
F (MHz)
=
5200 52
=
100 inches
Approximately:
6m band ½ of 6m is 3m 1m is 39 inches so 3m is 117 inches
Note this is based on free space wavelength. A wave traveling through wire will be slower and have a shorter wavelength.
52MHz is the middle of the 50-54Mhz 6m band

## Slide 34: T9A12 What is the approximate length, in inches, of a 6-meter 1/2 wavelength wire dipole antenna?
  A. 6 inches
  B. 50 inches
C. 112 inches
  D. 236 inches

## Slide 35: T9B01 Why are VHF/UHF signals not normally heard over long distances?
  A. They are too weak to go very far
  B. FCC regulations prohibit them from going more than 50 miles
  C. VHF and UHF signals are usually not reflected by the ionosphere
  D. They collide with trees and shrubbery and fade out

## Slide 36: T9B01 Why are VHF/UHF signals not normally heard over long distances?
  A. They are too weak to go very far
  B. FCC regulations prohibit them from going more than 50 miles
C. VHF and UHF signals are usually not reflected by the ionosphere
  D. They collide with trees and shrubbery and fade out

## Slide 37: T9B02 What might be happening when we hear a VHF signal from long distances?
  A. Signals are being reflected from outer space
  B. Someone is playing a recording to us
  C. Signals are being reflected by lightning storms in our area
  D. A possible cause is sporadic E reflection from a layer in the ionosphere

## Slide 38: T9B02 What might be happening when we hear a VHF signal from long distances?
  A. Signals are being reflected from outer space
  B. Someone is playing a recording to us
  C. Signals are being reflected by lightning storms in our area
D. A possible cause is sporadic E reflection from a layer in the ionosphere

## Slide 39: T9B03 What is the most likely cause of sudden bursts of tones or fragments of different conversations that interfere with VHF or UHF signals?
  A. The batteries in your transceiver are failing
  B. Strong signals are overloading the receiver and causing undesired signals to be heard
  C. The receiver is picking up low orbit satellites
  D. A nearby broadcast station is having transmitter problems

## Slide 40: T9B03 What is the most likely cause of sudden bursts of tones or fragments of different conversations that interfere with VHF or UHF signals?
  A. The batteries in your transceiver are failing
B. Strong signals are overloading the receiver and causing undesired signals to be heard
  C. The receiver is picking up low orbit satellites
  D. A nearby broadcast station is having transmitter problems

## Slide 41: T9B04 What is the radio horizon?
  A. The point where radio signals between two points are blocked by the curvature of the Earth
  B. The distance from the ground to a horizontally mounted antenna
  C. The farthest point you can see when standing at the base of your antenna tower
  D. The shortest distance between two points on the Earth's surface

## Slide 42: T9B04 What is the radio horizon?
A. The point where radio signals between two points are blocked by the curvature of the Earth
  B. The distance from the ground to a horizontally mounted antenna
  C. The farthest point you can see when standing at the base of your antenna tower
  D. The shortest distance between two points on the Earth's surface

## Slide 43: T9B05 What should you do if a station reports that your signals were strong just a moment ago, but now they are weak or distorted?
  A. Change the batteries in your radio to a different type
  B. Speak more slowly so he can understand your better
  C. Ask the other operator to adjust his squelch control
  D. Try moving a few feet, random reflections may be causing multi- path distortion.

## Slide 44: T9B05 What should you do if a station reports that your signals were strong just a moment ago, but now they are weak or distorted?
  A. Change the batteries in your radio to a different type
  B. Speak more slowly so he can understand your better
  C. Ask the other operator to adjust his squelch control
D. Try moving a few feet, random reflections may be causing multi- path distortion.

## Slide 45: T9B06 Why do UHF signals often work better inside of buildings than VHF signals?
  A. VHF signals lose power faster over distance
  B. The shorter wavelength of UHF signals allows them to more easily penetrate urban areas and buildings
  C. This is incorrect; VHF works better than UHF inside buildings
  D. UHF antennas are more efficient than VHF antennas

## Slide 46: T9B06 Why do UHF signals often work better inside of buildings than VHF signals?
  A. VHF signals lose power faster over distance
B. The shorter wavelength of UHF signals allows them to more easily penetrate urban areas and buildings
  C. This is incorrect; VHF works better than UHF inside buildings
  D. UHF antennas are more efficient than VHF antennas

## Slide 47: T9B07 What is a good thing to remember when using your hand-held VHF or UHF radio to reach a distant repeater?
  A. Speak as loudly as possible to help your signal go farther
  B. Keep your transmissions short to conserve battery power
  C. Keep the antenna as close to vertical as you can
  D. Turn off the CTCSS tone

## Slide 48: T9B07 What is a good thing to remember when using your hand-held VHF or UHF radio to reach a distant repeater?
  A. Speak as loudly as possible to help your signal go farther
B. Keep your transmissions short to conserve battery power
  C. Keep the antenna as close to vertical as you can
  D. Turn off the CTCSS tone

## Slide 49: T9B08 What can happen if the antennas at opposite ends of a VHF or UHF line of sight radio link are not using the same polarization?
  A. The modulation sidebands might become inverted
  B. Signals could be as much as 100 times weaker
  C. Signals have an echo effect on voices
  D. Nothing significant will happen

## Slide 50: T9B08 What can happen if the antennas at opposite ends of a VHF or UHF line of sight radio link are not using the same polarization?
  A. The modulation sidebands might become inverted
  B. Signals could be as much as 100 times weaker
C. Signals have an echo effect on voices
  D. Nothing significant will happen

## Slide 51: T9B09 What might be a way to reach a distant repeater if buildings or obstructions are blocking the direct line of sight path?
  A. Change from vertical to horizontal polarization
  B. Try using a directional antenna to find a path that reflects signals to the repeater
  C. Ask the repeater owners to repair their receiver
  D. Transmit on the repeater output frequency

## Slide 52: T9B09 What might be a way to reach a distant repeater if buildings or obstructions are blocking the direct line of sight path?
  A. Change from vertical to horizontal polarization
B. Try using a directional antenna to find a path that reflects signals to the repeater
  C. Ask the repeater owners to repair their receiver
  D. Transmit on the repeater output frequency

## Slide 53: T9B10 What term is commonly used to describe the rapid fluttering sound sometimes heard from mobile stations that are moving while transmitting?
  A. Flip-flopping
  B. Picket fencing
  C. Frequency shifting
  D. Pulsing

## Slide 54: T9B10 What term is commonly used to describe the rapid fluttering sound sometimes heard from mobile stations that are moving while transmitting?
  A. Flip-flopping
B. Picket fencing
  C. Frequency shifting
  D. Pulsing

## Slide 55: T9B11 Why do VHF and UHF Radio signals usually travel about a third farther than the visual line of sight distance between 2 stations?
  A. Radio signals move somewhat faster than the speed of light and travel farther in the same amount of time
  B. Radio waves are not blocked by dust particles
  C. The Earth seems less curved to radio waves than to light
  D. Radio waves are blocked by dust particles

## Slide 56: T9B11 Why do VHF and UHF Radio signals usually travel about a third farther than the visual line of sight distance between 2 stations?
  A. Radio signals move somewhat faster than the speed of light and travel farther in the same amount of time
  B. Radio waves are not blocked by dust particles
C. The Earth seems less curved to radio waves than to light
  D. Radio waves are blocked by dust particles

## Slide 57: T9C01 What, in general terms, is standing wave ratio (SWR)?
  A. A measure of how well a load is matched to a transmitter
  B. The ratio of high to low impedance in a feed line
  C. The transmitter efficiency ratio
  D. An indication of the quality of your station ground connection

## Slide 58: T9C01 What, in general terms, is standing wave ratio (SWR)?
A. A measure of how well a load is matched to a transmitter
  B. The ratio of high to low impedance in a feed line
  C. The transmitter efficiency ratio
  D. An indication of the quality of your station ground connection

## Slide 59: T9C02 What reading on a SWR meter indicates a perfect impedance match between the antenna and the feed line?
  A. 2 to 1
  B. 1 to 3
  C. 1 to 1
  D. 10 to 1

## Slide 60: T9C02 What reading on a SWR meter indicates a perfect impedance match between the antenna and the feed line?
  A. 2 to 1
  B. 1 to 3
C. 1 to 1
  D. 10 to 1

## Slide 61: T9C03 What might be indicated by erratic changes in SWR readings?
  A. The transmitter is being modulated
  B. A loose connection in your antenna or feedline
  C. The transmitter is being over modulated
  D. Interference from other stations is distorting your signal

## Slide 62: T9C03 What might be indicated by erratic changes in SWR readings?
  A. The transmitter is being modulated
B. A loose connection in your antenna or feedline
  C. The transmitter is being over modulated
  D. Interference from other stations is distorting your signal

## Slide 63: T9C04 What is the SWR value where the protection circuits in most solid-state transmitters begin to reduce transmitter power?
  A. 2 to 1
  B. 1 to 2
  C. 6 to 1
  D. 10 to 1

## Slide 64: T9C04 What is the SWR value where the protection circuits in most solid-state transmitters begin to reduce transmitter power?
A. 2 to 1
  B. 1 to 2
  C. 6 to 1
  D. 10 to 1

## Slide 65: T9C05 What happens to the power lost in a feed line?
  A. It increases the SWR
  B. It comes back into your transmitter and could cause damage
  C. It is converted into heat by losses in the line
  D. It can cause distortion of your signal

## Slide 66: T9C05 What happens to the power lost in a feed line?
  A. It increases the SWR
  B. It comes back into your transmitter and could cause damage
C. It is converted into heat by losses in the line
  D. It can cause distortion of your signal

## Slide 67: T9C06 What instrument other than a SWR meter could you use to determine if your feedline and antenna are properly matched?
  A. Voltmeter
  B. Ohmmeter
  C. Iambic pentameter
  D. Directional wattmeter

## Slide 68: T9C06 What instrument other than a SWR meter could you use to determine if your feedline and antenna are properly matched?
  A. Voltmeter
  B. Ohmmeter
  C. Iambic pentameter
D. Directional wattmeter

## Slide 69: T9C07 What is the most common reason for failure of coaxial cables?
  A. Moisture contamination
  B. Gamma rays
  C. End of service life
  D. Overloading

## Slide 70: T9C07 What is the most common reason for failure of coaxial cables?
A. Moisture contamination
  B. Gamma rays
  C. End of service life
  D. Overloading

## Slide 71: T9C08 Why is it important to have a low SWR in an antenna system that uses coaxial cable feedline?
  A. To reduce television interference
  B. To allow the efficient transfer of power and reduce losses
  C. To prolong antenna life
  D. To keep your signal from changing polarization

## Slide 72: T9C08 Why is it important to have a low SWR in an antenna system that uses coaxial cable feedline?
  A. To reduce television interference
B. To allow the efficient transfer of power and reduce losses
  C. To prolong antenna life
  D. To keep your signal from changing polarization

## Slide 73: T9C09 What can happen to older coaxial cables that are exposed to weather and sunlight for several years?
  A. Nothing, weather and sunlight do not affect coaxial cable
  B. The cable can shrink and break
  C. Losses can increase dramatically
  D. It will short-circuit

## Slide 74: T9C09 What can happen to older coaxial cables that are exposed to weather and sunlight for several years?
  A. Nothing, weather and sunlight do not affect coaxial cable
  B. The cable can shrink and break
C. Losses can increase dramatically
  D. It will short-circuit

## Slide 75: T9C10 Why is the outer sheath of most coaxial cables black in color?
  A. It is the cheapest color to use
  B. To see nicks and cracks in the cable
  C. Black cables have less loss
  D. Black provides protection against ultraviolet damage

## Slide 76: T9C10 Why is the outer sheath of most coaxial cables black in color?
  A. It is the cheapest color to use
  B. To see nicks and cracks in the cable
  C. Black cables have less loss
D. Black provides protection against ultraviolet damage

## Slide 77: T9C11 What is the impedance of the most commonly used coaxial cable in typical amateur radio installations?
  A. 8 Ohms
  B. 50 Ohms
  C. 600 Ohms
  D. 12 Ohms

## Slide 78: T9C11 What is the impedance of the most commonly used coaxial cable in typical amateur radio installations?
  A. 8 Ohms
B. 50 Ohms
  C. 600 Ohms
  D. 12 Ohms

## Slide 79: T9C12 Why is coaxial cable used more often than any other feed line for amateur radio antenna systems?
  A. It is easy to use and requires few special installation considerations
  B. It has less loss than any other type of feedline
  C. It can handle more power than any other type of feedline
  D. It is less expensive than any other types of line

## Slide 80: T9C12 Why is coaxial cable used more often than any other feed line for amateur radio antenna systems?
A. It is easy to use and requires few special installation considerations
  B. It has less loss than any other type of feedline
  C. It can handle more power than any other type of feedline
  D. It is less expensive than any other types of line