## Slide 1: G3 -- RADIO WAVE PROPAGATION [3 Exam Questions -- 3 Groups]
  G3A Ionospheric disturbances; sunspots and solar radiation
  G3B Maximum usable frequency; propagation "hops"
  G3C Height of ionospheric regions; critical angle and frequency; HF scatter
Notes: ELEMENT 3 - GENERAL CLASS as released by the Question Pool Committee of the National Conference of Volunteer Examiner Coordinators December 1, 2003
The questions contained within this pool must be used in all General class examinations beginning July 1, 2004, and is intended to be used up through June 30, 2007.

## Slide 2: Ionospheric Protection
The ionosphere and magnetosphere protect us from harmful radiation from the sun
Notes: RF emissions (solar flux) and particulate emissions from the sun have an enormous effect on radio propagation. RF emissions including X-ray and ultraviolet arrive at the earth in only 8 minutes. Particulate emissions including Coronal Mass Ejections (CMEs) arrive in 20-40 hours. The earth’s magnetic field captures much of this radiation near the poles and generally has an adverse effect on propagation at higher latitudes (nearer the poles). Lower frequencies are impacted by higher energy levels first and a sudden increase in activity will generally destroy propagation on the lower bands (increase the LUF) and often improve it at higher frequencies (increase the MUF).

## Slide 3: G3A01 What can be done at an amateur station to continue communications during a sudden ionospheric disturbance?
  A. Try a higher frequency
  B. Try the other sideband
  C. Try a different antenna polarization
  D. Try a different frequency shift

## Slide 4: G3A01 What can be done at an amateur station to continue communications during a sudden ionospheric disturbance?
A. Try a higher frequency
  B. Try the other sideband
  C. Try a different antenna polarization
  D. Try a different frequency shift

## Slide 5: G3A02 What effect does a sudden ionospheric disturbance have on the day-time ionospheric propagation of HF radio waves?
  A. It disrupts higher-latitude paths more than lower-latitude paths
  B. It disrupts signals on lower frequencies more than those on higher frequencies
  C. It disrupts communications via satellite more than direct communications
  D. None, only areas on the night side of the earth are affected

## Slide 6: G3A02 What effect does a sudden ionospheric disturbance have on the day-time ionospheric propagation of HF radio waves?
  A. It disrupts higher-latitude paths more than lower-latitude paths
B. It disrupts signals on lower frequencies more than those on higher frequencies
  C. It disrupts communications via satellite more than direct communications
  D. None, only areas on the night side of the earth are affected

## Slide 7: G3A03 How long does it take the increased ultraviolet and X-ray radiation from solar flares to affect radio-wave propagation on the earth?
  A. The effect is almost instantaneous
  B. 1.5 minutes
  C. 8 minutes
  D. 20 to 40 hours

## Slide 8: G3A03 How long does it take the increased ultraviolet and X-ray radiation from solar flares to affect radio-wave propagation on the earth?
  A. The effect is almost instantaneous
  B. 1.5 minutes
C. 8 minutes
  D. 20 to 40 hours

## Slide 9: G3A04 What is solar flux?
  A. The density of the sun's magnetic field
  B. The radio energy emitted by the sun
  C. The number of sunspots on the side of the sun facing the earth
  D. A measure of the tilt of the earth's ionosphere on the side toward the sun

## Slide 10: G3A04 What is solar flux?
  A. The density of the sun's magnetic field
B. The radio energy emitted by the sun
  C. The number of sunspots on the side of the sun facing the earth
  D. A measure of the tilt of the earth's ionosphere on the side toward the sun

## Slide 11: G3A05 What is the solar-flux index?
  A. A measure of solar activity that is taken annually
  B. A measure of solar activity that compares daily readings with results from the last six months
  C. Another name for the American sunspot number
  D. A measure of solar activity that is taken at a specific frequency

## Slide 12: G3A05 What is the solar-flux index?
  A. A measure of solar activity that is taken annually
  B. A measure of solar activity that compares daily readings with results from the last six months
  C. Another name for the American sunspot number
D. A measure of solar activity that is taken at a specific frequency

## Slide 13: G3A06 What is a geomagnetic disturbance?
  A. A sudden drop in the solar-flux index
  B. A shifting of the earth's magnetic pole
  C. Ripples in the ionosphere
  D. A dramatic change in the earth's magnetic field over a short period of time

## Slide 14: G3A06 What is a geomagnetic disturbance?
  A. A sudden drop in the solar-flux index
  B. A shifting of the earth's magnetic pole
  C. Ripples in the ionosphere
D. A dramatic change in the earth's magnetic field over a short period of time

## Slide 15: G3A07 At which latitudes are propagation paths more sensitive to geomagnetic disturbances?
  A. Those greater than 45 degrees latitude
  B. Those between 5 and 45 degrees latitude
  C. Those near the equator
  D. All paths are affected equally

## Slide 16: G3A07 At which latitudes are propagation paths more sensitive to geomagnetic disturbances?
A. Those greater than 45 degrees latitude
  B. Those between 5 and 45 degrees latitude
  C. Those near the equator
  D. All paths are affected equally

## Slide 17: G3A08 What can be the effect of a major geomagnetic storm on radio-wave propagation?
  A. Improved high-latitude HF propagation
  B. Degraded high-latitude HF propagation
  C. Improved ground-wave propagation
  D. Improved chances of UHF ducting

## Slide 18: G3A08 What can be the effect of a major geomagnetic storm on radio-wave propagation?
  A. Improved high-latitude HF propagation
B. Degraded high-latitude HF propagation
  C. Improved ground-wave propagation
  D. Improved chances of UHF ducting

## Slide 19: Sunspots
Sunspots peak during 11-year cycles
The higher the sunspot count, the more the atmosphere is ionized
Thus, higher sunspot counts support a higher Maximum Usable Frequency (MUF)

## Slide 20: G3A09 When sunspot numbers are high, what is the effect on radio communications?
  A. High-frequency radio signals are absorbed
  B. Frequencies above 300 MHz become usable for long-distance communication
  C. Long-distance communication in the upper HF and lower VHF range is enhanced
  D. High-frequency radio signals become weak and distorted

## Slide 21: G3A09 When sunspot numbers are high, what is the effect on radio communications?
  A. High-frequency radio signals are absorbed
  B. Frequencies above 300 MHz become usable for long-distance communication
C. Long-distance communication in the upper HF and lower VHF range is enhanced
  D. High-frequency radio signals become weak and distorted

## Slide 22: G3A10 What is the sunspot number?
  A. A daily index of sunspot activity
  B. The number of sunspots observed during one solar rotation
  C. The number of sunspots observed during a sunspot cycle
  D. The number of sunspots observed averaged over a seven day period

## Slide 23: G3A10 What is the sunspot number?
A. A daily index of sunspot activity
  B. The number of sunspots observed during one solar rotation
  C. The number of sunspots observed during a sunspot cycle
  D. The number of sunspots observed averaged over a seven day period

## Slide 24: G3A11 What is the sunspot cycle?
  A. The 9- to 11-year periods when sunspots move from the sun's pole to its equatorial region
  B. The 9- to 11-year periods when sunspots cause coronal holes to appear
  C. The approximately 11-year variation in the sunspot number
  D. The approximately 11-year periods when sunspots combine to form flares

## Slide 25: G3A11 What is the sunspot cycle?
  A. The 9- to 11-year periods when sunspots move from the sun's pole to its equatorial region
  B. The 9- to 11-year periods when sunspots cause coronal holes to appear
C. The approximately 11-year variation in the sunspot number
  D. The approximately 11-year periods when sunspots combine to form flares

## Slide 26: G3A12 What is the K-index?
  A. A linear index of solar activity
  B. A measure of geomagnetic stability
  C. An index of solar flux measured at Boulder, Colorado
  D. A daily value measured on a scale from 0 to 400 to express the range of disturbance of the geomagnetic field

## Slide 27: G3A12 What is the K-index?
  A. A linear index of solar activity
B. A measure of geomagnetic stability
  C. An index of solar flux measured at Boulder, Colorado
  D. A daily value measured on a scale from 0 to 400 to express the range of disturbance of the geomagnetic field

## Slide 28: G3A13 What is the A-index?
  A. A monthly linear index of solar activity
  B. An weekly index of solar flux measured at Boulder, Colorado
  C. A daily value measured on a scale from 0 to 400 to express the range of disturbance of the geomagnetic field
  D. An index used by NOAA to correlate the visual color wavelengths seen with Aurora Borealis (Northern Lights)

## Slide 29: G3A13 What is the A-index?
  A. A monthly linear index of solar activity
  B. An weekly index of solar flux measured at Boulder, Colorado
C. A daily value measured on a scale from 0 to 400 to express the range of disturbance of the geomagnetic field
  D. An index used by NOAA to correlate the visual color wavelengths seen with Aurora Borealis (Northern Lights)

## Slide 30: G3A14 How does solar coronal hole activity affect radio communications?
  A. The activity emits charged particles that improve HF communications
  B. The activity emits charged particles that improve VHF/UHF ducting
  C. The activity emits charged particles that usually disrupt HF communications
  D. The activity emits charged particles, but they never reach Earth's magnetosphere

## Slide 31: G3A14 How does solar coronal hole activity affect radio communications?
  A. The activity emits charged particles that improve HF communications
  B. The activity emits charged particles that improve VHF/UHF ducting
C. The activity emits charged particles that usually disrupt HF communications
  D. The activity emits charged particles, but they never reach Earth's magnetosphere

## Slide 32: G3A15 How long does it take charged particles from coronal mass ejections (CMEs) to affect radio-wave propagation on the earth?
  A. Almost instantaneously
  B. About 5 minutes
  C. About 8 minutes
  D. 20 to 40 hours

## Slide 33: G3A15 How long does it take charged particles from coronal mass ejections (CMEs) to affect radio-wave propagation on the earth?
  A. Almost instantaneously
  B. About 5 minutes
  C. About 8 minutes
D. 20 to 40 hours

## Slide 34: G3A16 What might result during periods of high geomagnetic activity?
  A. A visible aurora
  B. Excellent high-frequency radio conditions
  C. Poor 6-meter conditions
  D. F-layer absorption

## Slide 35: G3A16 What might result during periods of high geomagnetic activity?
A. A visible aurora
  B. Excellent high-frequency radio conditions
  C. Poor 6-meter conditions
  D. F-layer absorption

## Slide 36: Ionospheric Layers
Notes: The key points are the D, E and F layers. The F layer splits and becomes F1 and F2 with the additional energy from the daytime sun. The D and E layers disappear at night without the sun’s energy. The D layer absorbs most RF power, particularly at low frequencies. The other layers will reflect RF energy. The higher the layer, the further the contact possible.
Propagation conditions are a balance between the D layer absorption of lower frequencies and the reflection of the higher frequencies by the upper layers. As more of the sun’s energy (primarily electromagnetic and particle emissions) strikes the ionosphere, all the layers grown in size and density. The D layer will absorb more low frequency RF and the upper layers will reflect more high frequency RF. This creates a window of frequencies above the Lowest Usable Frequency (LUF) and Maximum Usable Frequency (MUF) that will work for long distance communications.
Sunspots provide huge amounts of energy to reflect radio waves in the ionosphere and are especially important in the upper bands. Sunspots occur in 11 cycles of high and low activity.

## Slide 37: Critical Angle
Notes: Note that the altitude and angle of reflection varies with frequency. Generally the higher frequencies will be reflected at higher altitudes and at shallower angles. If the frequency is high enough, it won’t be reflected enough to arrive back on the surface. The highest frequency that can be reflected is the “critical frequency” and generally the Maximum Usable Frequency (MUF).
If the angle if the wave is too steep, it will continue into space. The steepest angle that will be reflected back to the surface is the “critical angle”.

## Slide 38: G3B01 If the maximum usable frequency (MUF) on the path from Minnesota to France is 24 MHz, which band should offer the best chance for a successful contact?
  A. 10 meters
  B. 15 meters
  C. 20 meters
  D. 40 meters

## Slide 39: G3B01 If the maximum usable frequency (MUF) on the path from Minnesota to France is 24 MHz, which band should offer the best chance for a successful contact?
  A. 10 meters
B. 15 meters
  C. 20 meters
  D. 40 meters

## Slide 40: G3B02 If the maximum usable frequency (MUF) on the path from Ohio to Germany is 17 MHz, which band should offer the best chance for a successful contact?
  A. 80 meters
  B. 40 meters
  C. 20 meters
  D. 2 meters

## Slide 41: G3B02 If the maximum usable frequency (MUF) on the path from Ohio to Germany is 17 MHz, which band should offer the best chance for a successful contact?
  A. 80 meters
  B. 40 meters
C. 20 meters
  D. 2 meters

## Slide 42: G3B03 If the HF radio-wave propagation (skip) is generally good on the 24-MHz and 28-MHz bands for several days, when might you expect a similar condition to occur?
  A. 7 days later
  B. 14 days later
  C. 28 days later
  D. 90 days later

## Slide 43: G3B03 If the HF radio-wave propagation (skip) is generally good on the 24-MHz and 28-MHz bands for several days, when might you expect a similar condition to occur?
  A. 7 days later
  B. 14 days later
C. 28 days later
  D. 90 days later

## Slide 44: G3B04 What is one way to determine if the maximum usable frequency (MUF) is high enough to support 28-MHz propagation between your station and western Europe?
  A. Listen for signals on a 10-meter beacon frequency
  B. Listen for signals on a 20-meter beacon frequency
  C. Listen for signals on a 39-meter broadcast frequency
  D. Listen for WWVH time signals on 20 MHz

## Slide 45: G3B04 What is one way to determine if the maximum usable frequency (MUF) is high enough to support 28-MHz propagation between your station and western Europe?
A. Listen for signals on a 10-meter beacon frequency
  B. Listen for signals on a 20-meter beacon frequency
  C. Listen for signals on a 39-meter broadcast frequency
  D. Listen for WWVH time signals on 20 MHz

## Slide 46: G3B05 What usually happens to radio waves with frequencies below the maximum usable frequency (MUF) when they are sent into the ionosphere?
  A. They are bent back to the earth
  B. They pass through the ionosphere
  C. They are completely absorbed by the ionosphere
  D. They are bent and trapped in the ionosphere to circle the Earth

## Slide 47: G3B05 What usually happens to radio waves with frequencies below the maximum usable frequency (MUF) when they are sent into the ionosphere?
A. They are bent back to the earth
  B. They pass through the ionosphere
  C. They are completely absorbed by the ionosphere
  D. They are bent and trapped in the ionosphere to circle the Earth

## Slide 48: G3B06 Where would you tune to hear beacons that would help you determine propagation conditions on the 20-meter band?
  A. 28.2 MHz
  B. 21.1 MHz
  C. 14.1 MHz
  D. 18.1 MHz

## Slide 49: G3B06 Where would you tune to hear beacons that would help you determine propagation conditions on the 20-meter band?
  A. 28.2 MHz
  B. 21.1 MHz
C. 14.1 MHz
  D. 18.1 MHz

## Slide 50: G3B07 During periods of low solar activity, which frequencies are the least reliable for long-distance communication?
  A. Frequencies below 3.5 MHz
  B. Frequencies near 3.5 MHz
  C. Frequencies on or above 10 MHz
  D. Frequencies above 20 MHz

## Slide 51: G3B07 During periods of low solar activity, which frequencies are the least reliable for long-distance communication?
  A. Frequencies below 3.5 MHz
  B. Frequencies near 3.5 MHz
  C. Frequencies on or above 10 MHz
D. Frequencies above 20 MHz

## Slide 52: G3B08 At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours?
  A. At the summer solstice
  B. Only at the maximum point of the solar cycle
  C. Only at the minimum point of the solar cycle
  D. At any point in the solar cycle

## Slide 53: G3B08 At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours?
  A. At the summer solstice
  B. Only at the maximum point of the solar cycle
  C. Only at the minimum point of the solar cycle
D. At any point in the solar cycle

## Slide 54: G3B09 What is the maximum distance along the Earth's surface that is normally covered in one hop using the F2 region?
  A. 180 miles
  B. 1200 miles
  C. 2500 miles
  D. None; the F2 region does not support radio-wave propagation

## Slide 55: G3B09 What is the maximum distance along the Earth's surface that is normally covered in one hop using the F2 region?
  A. 180 miles
  B. 1200 miles
C. 2500 miles
  D. None; the F2 region does not support radio-wave propagation

## Slide 56: G3B10 What is the maximum distance along the Earth's surface that is normally covered in one hop using the E region?
  A. 180 miles
  B. 1200 miles
  C. 2500 miles
  D. None of these choices is correct

## Slide 57: G3B10 What is the maximum distance along the Earth's surface that is normally covered in one hop using the E region?
  A. 180 miles
B. 1200 miles
  C. 2500 miles
  D. None of these choices is correct

## Slide 58: G3B11 What happens to HF propagation when the lowest usable frequency (LUF) exceeds the maximum usable frequency (MUF)?
  A. No HF radio frequency will support communications along an ionospheric signal path
  B. The lowest usable frequency can never exceed the maximum usable frequency
  C. The ionospheric absorption of HF radio signals increases by 3 dB along every signal path
  D. All ionospheric propagation paths are still usable, but the signal-to-noise ratio decreases

## Slide 59: G3B11 What happens to HF propagation when the lowest usable frequency (LUF) exceeds the maximum usable frequency (MUF)?
A. No HF radio frequency will support communications along an ionospheric signal path
  B. The lowest usable frequency can never exceed the maximum usable frequency
  C. The ionospheric absorption of HF radio signals increases by 3 dB along every signal path
  D. All ionospheric propagation paths are still usable, but the signal-to-noise ratio decreases

## Slide 60: G3B12 What factors affect the maximum usable frequency (MUF)?
  A. Path distance and locations
  B. Time of day and season
  C. Solar radiation and ionospheric disturbances
  D. All of these choices are correct

## Slide 61: G3B12 What factors affect the maximum usable frequency (MUF)?
  A. Path distance and locations
  B. Time of day and season
  C. Solar radiation and ionospheric disturbances
D. All of these choices are correct

## Slide 62: G3B13 How might a skywave signal sound if it arrives at your receiver by both short path and long path propagation?
  A. Periodic fading every 10 seconds
  B. Signal strength increased by 3 dB
  C. Signal strength decreased by 3 dB
  D. A well-defined echo can be heard

## Slide 63: G3B13 How might a skywave signal sound if it arrives at your receiver by both short path and long path propagation?
  A. Periodic fading every 10 seconds
  B. Signal strength increased by 3 dB
  C. Signal strength decreased by 3 dB
D. A well-defined echo can be heard

## Slide 64: G3B14 A short distance hop on 10 meters might indicate what conditions on 6 meters?
  A. The MUF exceeds 50 MHz
  B. Absolutely no chance of a skywave 6-meter band opening
  C. 6-meter ground waves will diminish
  D. 10-meter propagation has no bearing on possible 6-meter propagation

## Slide 65: G3B14 A short distance hop on 10 meters might indicate what conditions on 6 meters?
A. The MUF exceeds 50 MHz
  B. Absolutely no chance of a skywave 6-meter band opening
  C. 6-meter ground waves will diminish
  D. 10-meter propagation has no bearing on possible 6-meter propagation

## Slide 66: G3C01 What is the average height of maximum ionization of the E region?
  A. 45 miles
  B. 70 miles
  C. 200 miles
  D. 1200 miles

## Slide 67: G3C01 What is the average height of maximum ionization of the E region?
  A. 45 miles
B. 70 miles
  C. 200 miles
  D. 1200 miles

## Slide 68: G3C02 When can the F2 region be expected to reach its maximum height at your location?
  A. At noon during the summer
  B. At midnight during the summer
  C. At dusk in the spring and fall
  D. At noon during the winter

## Slide 69: G3C02 When can the F2 region be expected to reach its maximum height at your location?
A. At noon during the summer
  B. At midnight during the summer
  C. At dusk in the spring and fall
  D. At noon during the winter

## Slide 70: G3C03 Why is the F2 region mainly responsible for the longest-distance radio-wave propagation?
  A. Because it exists only at night
  B. Because it is the lowest ionospheric region
  C. Because it is the highest ionospheric region
  D. Because it does not absorb radio waves as much as other ionospheric regions

## Slide 71: G3C03 Why is the F2 region mainly responsible for the longest-distance radio-wave propagation?
  A. Because it exists only at night
  B. Because it is the lowest ionospheric region
C. Because it is the highest ionospheric region
  D. Because it does not absorb radio waves as much as other ionospheric regions

## Slide 72: G3C04 What is the "critical angle" as used in radio-wave propagation?
  A. The lowest takeoff angle that will return a radio wave to the earth under specific ionospheric conditions
  B. The compass direction of a distant station
  C. The compass direction opposite that of a distant station
  D. The highest takeoff angle that will return a radio wave to the earth under specific ionospheric conditions

## Slide 73: G3C04 What is the "critical angle" as used in radio-wave propagation?
  A. The lowest takeoff angle that will return a radio wave to the earth under specific ionospheric conditions
  B. The compass direction of a distant station
  C. The compass direction opposite that of a distant station
D. The highest takeoff angle that will return a radio wave to the earth under specific ionospheric conditions

## Slide 74: G3C05 What is the main reason the 160-, 80- and 40-meter amateur bands tend to be useful only for short-distance communications during daylight hours?
  A. Because of a lack of activity
  B. Because of auroral propagation
  C. Because of D-region absorption
  D. Because of magnetic flux

## Slide 75: G3C05 What is the main reason the 160-, 80- and 40-meter amateur bands tend to be useful only for short-distance communications during daylight hours?
  A. Because of a lack of activity
  B. Because of auroral propagation
C. Because of D-region absorption
  D. Because of magnetic flux

## Slide 76: G3C06 What is a characteristic of HF scatter signals?
  A. High intelligibility
  B. A wavering sound
  C. Reversed modulation
  D. Reversed sidebands

## Slide 77: G3C06 What is a characteristic of HF scatter signals?
  A. High intelligibility
B. A wavering sound
  C. Reversed modulation
  D. Reversed sidebands

## Slide 78: G3C07 What makes HF scatter signals often sound distorted?
  A. Auroral activity and changes in the earth's magnetic field
  B. Propagation through ground waves that absorb much of the signal
  C. The state of the E-region at the point of refraction
  D. Energy scattered into the skip zone through several radio-wave paths

## Slide 79: G3C07 What makes HF scatter signals often sound distorted?
  A. Auroral activity and changes in the earth's magnetic field
  B. Propagation through ground waves that absorb much of the signal
  C. The state of the E-region at the point of refraction
D. Energy scattered into the skip zone through several radio-wave paths

## Slide 80: G3C08 Why are HF scatter signals usually weak?
  A. A part of the signal energy is propagated into the skip zone
  B. Auroral activity absorbs most of the signal energy
  C. Propagation through ground waves absorbs most of the signal energy
  D. The F region of the ionosphere absorbs most of the signal energy

## Slide 81: G3C08 Why are HF scatter signals usually weak?
A. A part of the signal energy is propagated into the skip zone
  B. Auroral activity absorbs most of the signal energy
  C. Propagation through ground waves absorbs most of the signal energy
  D. The F region of the ionosphere absorbs most of the signal energy

## Slide 82: G3C09 What type of radio-wave propagation allows a signal to be detected at a distance too far for ground-wave propagation but too near for normal sky-wave propagation?
  A. Ground wave
  B. Scatter
  C. Sporadic-E skip
  D. Short-path skip

## Slide 83: G3C09 What type of radio-wave propagation allows a signal to be detected at a distance too far for ground-wave propagation but too near for normal sky-wave propagation?
  A. Ground wave
B. Scatter
  C. Sporadic-E skip
  D. Short-path skip

## Slide 84: G3C10 When does scatter propagation on the HF bands most often occur?
  A. When the sunspot cycle is at a minimum and D-region absorption is high
  B. At night
  C. When the F1 and F2 regions are combined
  D. When communicating on frequencies above the maximum usable frequency (MUF)

## Slide 85: G3C10 When does scatter propagation on the HF bands most often occur?
  A. When the sunspot cycle is at a minimum and D-region absorption is high
  B. At night
  C. When the F1 and F2 regions are combined
D. When communicating on frequencies above the maximum usable frequency (MUF)

## Slide 86: G3C11 Which is true about ionospheric absorption near the maximum usable frequency (MUF)?
  A. Absorption will be minimum
  B. Absorption is independent of frequency
  C. Absorption approaches maximum
  D. There is no correlation between MUF and absorption

## Slide 87: G3C11 Which is true about ionospheric absorption near the maximum usable frequency (MUF)?
A. Absorption will be minimum
  B. Absorption is independent of frequency
  C. Absorption approaches maximum
  D. There is no correlation between MUF and absorption

## Slide 88: G3C12 Daylight fading on the 40-meter band is associated most with which ionospheric layer?
  A. The F2 layer
  B. The F1 layer
  C. The E layer
  D. The D layer

## Slide 89: G3C12 Daylight fading on the 40-meter band is associated most with which ionospheric layer?
  A. The F2 layer
  B. The F1 layer
  C. The E layer
D. The D layer