## Slide 1: G5 -- ELECTRICAL PRINCIPLES [2 Exam Questions -- 2 Groups]
  G5A Impedance, including matching; resistance, including ohm; reactance; inductance; capacitance; and metric divisions of these values
  G5B Decibel; Ohm's Law; current and voltage dividers; electrical power calculations and series and parallel components; transformers (either voltage or impedance); sine wave root-mean-square (RMS) value
Notes: ELEMENT 3 - GENERAL CLASS as released by the Question Pool Committee of the National Conference of Volunteer Examiner Coordinators December 1, 2003
The questions contained within this pool must be used in all General class examinations beginning July 1, 2004, and is intended to be used up through June 30, 2007.

## Slide 2: G5A01 What is impedance?
  A. The electric charge stored by a capacitor
  B. The opposition to the flow of AC in a circuit containing only capacitance
  C. The opposition to the flow of AC in a circuit
  D. The force of repulsion between one electric field and another with the same charge

## Slide 3: G5A01 What is impedance?
  A. The electric charge stored by a capacitor
  B. The opposition to the flow of AC in a circuit containing only capacitance
C. The opposition to the flow of AC in a circuit
  D. The force of repulsion between one electric field and another with the same charge

## Slide 4: Resonant Circuit
Notes: Inductors and Capacitors both exhibit Reactance or a resistance to AC measured in ohms. Inductive reactance (Xl) increases with frequency and capacitive reactance (Xc) decreases with frequency. When inductors and capacitors are used in the same circuit, the circuit is said to be resonant when inductive and capacitive reactance are equal.
Matching load impedance is important to insure maximum power delivery.

## Slide 5: G5A02 What is reactance?
  A. Opposition to DC caused by resistors
  B. Opposition to AC caused by inductors and capacitors
  C. A property of ideal resistors in AC circuits
  D. A large spark produced at switch contacts when an inductor is de-energized

## Slide 6: G5A02 What is reactance?
  A. Opposition to DC caused by resistors
B. Opposition to AC caused by inductors and capacitors
  C. A property of ideal resistors in AC circuits
  D. A large spark produced at switch contacts when an inductor is de-energized

## Slide 7: G5A03 In an inductor, what causes opposition to the flow of AC?
  A. Resistance
  B. Reluctance
  C. Admittance
  D. Reactance

## Slide 8: G5A03 In an inductor, what causes opposition to the flow of AC?
  A. Resistance
  B. Reluctance
  C. Admittance
D. Reactance

## Slide 9: G5A04 In a capacitor, what causes opposition to the flow of AC?
  A. Resistance
  B. Reluctance
  C. Reactance
  D. Admittance

## Slide 10: G5A04 In a capacitor, what causes opposition to the flow of AC?
  A. Resistance
  B. Reluctance
C. Reactance
  D. Admittance

## Slide 11: G5A05 How does a coil react to AC?
  A. As the frequency of the applied AC increases, the reactance decreases
  B. As the amplitude of the applied AC increases, the reactance increases
  C. As the amplitude of the applied AC increases, the reactance decreases
  D. As the frequency of the applied AC increases, the reactance increases

## Slide 12: G5A05 How does a coil react to AC?
  A. As the frequency of the applied AC increases, the reactance decreases
  B. As the amplitude of the applied AC increases, the reactance increases
  C. As the amplitude of the applied AC increases, the reactance decreases
D. As the frequency of the applied AC increases, the reactance increases

## Slide 13: G5A06 How does a capacitor react to AC?
  A. As the frequency of the applied AC increases, the reactance decreases
  B. As the frequency of the applied AC increases, the reactance increases
  C. As the amplitude of the applied AC increases, the reactance increases
  D. As the amplitude of the applied AC increases, the reactance decreases

## Slide 14: G5A06 How does a capacitor react to AC?
A. As the frequency of the applied AC increases, the reactance decreases
  B. As the frequency of the applied AC increases, the reactance increases
  C. As the amplitude of the applied AC increases, the reactance increases
  D. As the amplitude of the applied AC increases, the reactance decreases

## Slide 15: G5A07 What happens when the impedance of an electrical load is equal to the internal impedance of the power source?
  A. The source delivers minimum power to the load
  B. The electrical load is shorted
  C. No current can flow through the circuit
  D. The source delivers maximum power to the load

## Slide 16: G5A07 What happens when the impedance of an electrical load is equal to the internal impedance of the power source?
  A. The source delivers minimum power to the load
  B. The electrical load is shorted
  C. No current can flow through the circuit
D. The source delivers maximum power to the load

## Slide 17: G5A08 Why is impedance matching important?
  A. So the source can deliver maximum power to the load
  B. So the load will draw minimum power from the source
  C. To ensure that there is less resistance than reactance in the circuit
  D. To ensure that the resistance and reactance in the circuit are equal

## Slide 18: G5A08 Why is impedance matching important?
A. So the source can deliver maximum power to the load
  B. So the load will draw minimum power from the source
  C. To ensure that there is less resistance than reactance in the circuit
  D. To ensure that the resistance and reactance in the circuit are equal

## Slide 19: G5A09 What unit is used to measure reactance?
  A. Mho
  B. Ohm
  C. Ampere
  D. Siemens

## Slide 20: G5A09 What unit is used to measure reactance?
  A. Mho
B. Ohm
  C. Ampere
  D. Siemens

## Slide 21: G5A10 What unit is used to measure impedance?
  A. Volt
  B. Ohm
  C. Ampere
  D. Watt

## Slide 22: G5A10 What unit is used to measure impedance?
  A. Volt
B. Ohm
  C. Ampere
  D. Watt

## Slide 23: G5A11 Why should core saturation of a conventional impedance matching transformer be avoided?
  A. Harmonics and distortion could result from saturation
  B. Magnetic flux would increase with frequency
  C. RF susceptance would increase
  D. Temporary changes of the core permeability could result from saturation

## Slide 24: G5A11 Why should core saturation of a conventional impedance matching transformer be avoided?
A. Harmonics and distortion could result from saturation
  B. Magnetic flux would increase with frequency
  C. RF susceptance would increase
  D. Temporary changes of the core permeability could result from saturation

## Slide 25: G5B01 A two-times increase in power results in a change of how many dB?
  A. 1 dB higher
  B. 3 dB higher
  C. 6 dB higher
  D. 12 dB higher

## Slide 26: G5B01 A two-times increase in power results in a change of how many dB?
  A. 1 dB higher
B. 3 dB higher
  C. 6 dB higher
  D. 12 dB higher

## Slide 27: G5B02 In a parallel circuit with a voltage source and several branch resistors, how is the total current related to the current in the branch resistors?
  A. It equals the average of the branch current through each resistor
  B. It equals the sum of the branch current through each resistor
  C. It decreases as more parallel resistors are added to the circuit
  D. It is the sum of each resistor's voltage drop multiplied by the total number of resistors

## Slide 28: G5B02 In a parallel circuit with a voltage source and several branch resistors, how is the total current related to the current in the branch resistors?
  A. It equals the average of the branch current through each resistor
B. It equals the sum of the branch current through each resistor
  C. It decreases as more parallel resistors are added to the circuit
  D. It is the sum of each resistor's voltage drop multiplied by the total number of resistors

## Slide 29: Ohm’s Law and Power Calculations
E
I
R
P
I
E
E=Voltage (Volts)
I=Current (Amps)
R=Resistance (Ohms)
P=Power (Watts)
Notes: Ohm’s law should be familiar from the Technician exam. The new one is the power formula which states voltage in volts x current in amps = power in watts. Be sure to keep an eye on the units in these questions.

## Slide 30: G5B03 How many watts of electrical power are used if 400 VDC is supplied to an 800-ohm load?
  A. 0.5 watts
  B. 200 watts
  C. 400 watts
  D. 320,000 watts

## Slide 31: G5B03 How many watts of electrical power are used if 400 VDC is supplied to an 800-ohm load?
  A. 0.5 watts
B. 200 watts
  C. 400 watts
  D. 320,000 watts

## Slide 32: G5B04 How many watts of electrical power are used by a 12-VDC light bulb that draws 0.2 amperes?
  A. 60 watts
  B. 24 watts
  C. 6 watts
  D. 2.4 watts

## Slide 33: G5B04 How many watts of electrical power are used by a 12-VDC light bulb that draws 0.2 amperes?
  A. 60 watts
  B. 24 watts
  C. 6 watts
D. 2.4 watts

## Slide 34: G5B05 How many watts are being dissipated when 7.0 milliamperes flow through 1.25 kilohms?
  A. Approximately 61 milliwatts
  B. Approximately 39 milliwatts
  C. Approximately 11 milliwatts
  D. Approximately 9 milliwatts

## Slide 35: G5B05 How many watts are being dissipated when 7.0 milliamperes flow through 1.25 kilohms?
A. Approximately 61 milliwatts
  B. Approximately 39 milliwatts
  C. Approximately 11 milliwatts
  D. Approximately 9 milliwatts

## Slide 36: G5B06 What is the voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC?
  A. 2370 volts
  B. 540 volts
  C. 26.7 volts
  D. 5.9 volts

## Slide 37: G5B06 What is the voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC?
  A. 2370 volts
  B. 540 volts
C. 26.7 volts
  D. 5.9 volts

## Slide 38: G5B07 What is the turns ratio of a transformer to match an audio amplifier having a 600-ohm output impedance to a speaker having a 4-ohm impedance?
  A. 12.2 to 1
  B. 24.4 to 1
  C. 150 to 1
  D. 300 to 1

## Slide 39: G5B07 What is the turns ratio of a transformer to match an audio amplifier having a 600-ohm output impedance to a speaker having a 4-ohm impedance?
A. 12.2 to 1
  B. 24.4 to 1
  C. 150 to 1
  D. 300 to 1

## Slide 40: RMS, Peak and Peak to Peak Voltages
Notes: There are three key voltage measurements, RMS (Vrms), Peak (Vpk) and Peak to Peak (Vpp). The Peak voltage is relative to ground. RMS or Root Mean Square is more of an “average” voltage over the duration of the AC cycle. RMS voltage is calculated by multiplying 0.707 times the peak voltage. The Peak to Peak voltage measures from the peak of the positive swing to the peak of the negative swing.
The 120 volt AC line voltage in the wall is a peak value. That means the RMS voltage is 85 volts and Peak to Peak is 240 volts.

## Slide 41: G5B08 A DC voltage equal to what value of an applied sine-wave AC voltage would produce the same amount of heat over time in a resistive element?
  A. The peak-to-peak value
  B. The RMS value
  C. The average value
  D. The peak value

## Slide 42: G5B08 A DC voltage equal to what value of an applied sine-wave AC voltage would produce the same amount of heat over time in a resistive element?
  A. The peak-to-peak value
B. The RMS value
  C. The average value
  D. The peak value

## Slide 43: G5B09 What is the peak-to-peak voltage of a sine wave that has an RMS voltage of 120 volts?
  A. 84.8 volts
  B. 169.7 volts
  C. 204.8 volts
  D. 339.4 volts

## Slide 44: G5B09 What is the peak-to-peak voltage of a sine wave that has an RMS voltage of 120 volts?
  A. 84.8 volts
  B. 169.7 volts
  C. 204.8 volts
D. 339.4 volts

## Slide 45: G5B10 A sine wave of 17 volts peak is equivalent to how many volts RMS?
  A. 8.5 volts
  B. 12 volts
  C. 24 volts
  D. 34 volts

## Slide 46: G5B10 A sine wave of 17 volts peak is equivalent to how many volts RMS?
  A. 8.5 volts
B. 12 volts
  C. 24 volts
  D. 34 volts

## Slide 47: G5B12 What causes a voltage to appear across the secondary winding of a transformer when a voltage source is connected across its primary winding?
  A. Capacitive coupling
  B. Displacement current coupling
  C. Mutual inductance
  D. Mutual capacitance

## Slide 48: G5B12 What causes a voltage to appear across the secondary winding of a transformer when a voltage source is connected across its primary winding?
  A. Capacitive coupling
  B. Displacement current coupling
C. Mutual inductance
  D. Mutual capacitance

## Slide 49: G5B13 What would be the capacitance and voltage rating of a series circuit consisting of two equal value capacitors with equal voltage ratings?
  A. Total capacitance would be half that of each capacitor and maximum voltage would be twice that of each capacitor
  B. Total capacitance would be half that of each capacitor and maximum voltage would be the same as each capacitor
  C. Total capacitance and maximum voltage would be the same as each capacitor
  D. Total capacitance and maximum voltage would be half that of each capacitor

## Slide 50: G5B13 What would be the capacitance and voltage rating of a series circuit consisting of two equal value capacitors with equal voltage ratings?
A. Total capacitance would be half that of each capacitor and maximum voltage would be twice that of each capacitor
  B. Total capacitance would be half that of each capacitor and maximum voltage would be the same as each capacitor
  C. Total capacitance and maximum voltage would be the same as each capacitor
  D. Total capacitance and maximum voltage would be half that of each capacitor

## Slide 51: G5B14 What percentage loss would result from a transmission line loss of 1 dB?
  A. 16.6%
  B. 12.5%
  C. 14.7%
  D. 20.6%

## Slide 52: G5B14 What percentage loss would result from a transmission line loss of 1 dB?
  A. 16.6%
  B. 12.5%
  C. 14.7%
D. 20.6%

## Slide 53: G5B15 If three equal resistors in parallel produce 50-ohms of resistance and the same resistors in series produce 450-ohms, what is the value of each resistor?
  A. 1500-ohms
  B. 90-ohms
  C. 150-ohms
  D. 175-ohms

## Slide 54: G5B15 If three equal resistors in parallel produce 50-ohms of resistance and the same resistors in series produce 450-ohms, what is the value of each resistor?
  A. 1500-ohms
  B. 90-ohms
C. 150-ohms
  D. 175-ohms