## Slide 1: G9 -- ANTENNAS AND FEED-LINES [4 Exam Questions -- 4 Groups]
  G9A Yagi antennas - physical dimensions; impedance matching; radiation patterns; directivity and major lobes
  G9B Loop antennas - physical dimensions; impedance matching; radiation patterns; directivity and major lobes
  G9C Random wire antennas - physical dimensions; impedance matching; radiation patterns; directivity and major lobes; feed point impedance of 1/2-wavelength dipole and 1/4-wavelength vertical antennas
  G9D Popular antenna feed-lines - characteristic impedance and impedance matching; SWR calculations
Notes: ELEMENT 3 - GENERAL CLASS as released by the Question Pool Committee of the National Conference of Volunteer Examiner Coordinators December 1, 2003
The questions contained within this pool must be used in all General class examinations beginning July 1, 2004, and is intended to be used up through June 30, 2007.

## Slide 2: Yagi Antenna
Notes: Note the driven element with the balun attached, the smaller directors, larger reflector and the pattern with a large front lobe. The driven element is approximately a half have dipole. As parasitic elements (directors and reflectors) are added and the boom length is increased, the more gain is provided by the antenna. Reflectors are placed behind the driven element to reflect the power forward and the directors act as conductors in front of the wave. Reflectors are generally ~3% longer than the driven element and directors ~3% shorter. Five element yagis like this one yield 10-12dB gain over a dipole, based on the design of the antenna.
Antenna designers have to balance forward gain, front-to-back ratio, bandwidth and feedpoint impedance when designing an antenna. Some antennas will be optimized for maximum forward gain to improve their output and others may have better front-to-back rations to improve their noise rejection. Antenna bandwidth can be increased by using larger diameter elements.

## Slide 3: G9A01 When designing a Yagi antenna, how can the SWR bandwidth be increased?
  A. Use larger diameter elements
  B. Use closer element spacing
  C. Use traps on the elements
  D. Use tapered-diameter elements

## Slide 4: G9A01 When designing a Yagi antenna, how can the SWR bandwidth be increased?
A. Use larger diameter elements
  B. Use closer element spacing
  C. Use traps on the elements
  D. Use tapered-diameter elements

## Slide 5: G9A02 Approximately how long is the driven element of a Yagi antenna for 14.0 MHz?
  A. 17 feet
  B. 33 feet
  C. 35 feet
  D. 66 feet

## Slide 6: G9A02 Approximately how long is the driven element of a Yagi antenna for 14.0 MHz?
  A. 17 feet
B. 33 feet
  C. 35 feet
  D. 66 feet

## Slide 7: G9A03 Approximately how long is the director element of a Yagi antenna for 21.1 MHz?
  A. 42 feet
  B. 21 feet
  C. 17 feet
  D. 10.5 feet

## Slide 8: G9A03 Approximately how long is the director element of a Yagi antenna for 21.1 MHz?
  A. 42 feet
B. 21 feet
  C. 17 feet
  D. 10.5 feet

## Slide 9: G9A04 Approximately how long is the reflector element of a Yagi antenna for 28.1 MHz?
  A. 8.75 feet
  B. 16.6 feet
  C. 17.5 feet
  D. 35 feet

## Slide 10: G9A04 Approximately how long is the reflector element of a Yagi antenna for 28.1 MHz?
  A. 8.75 feet
  B. 16.6 feet
C. 17.5 feet
  D. 35 feet

## Slide 11: G9A05 Which statement about a three-element Yagi antenna is true?
  A. The reflector is normally the shortest parasitic element
  B. The director is normally the shortest parasitic element
  C. The driven element is the longest parasitic element
  D. Low feed-point impedance increases bandwidth

## Slide 12: G9A05 Which statement about a three-element Yagi antenna is true?
  A. The reflector is normally the shortest parasitic element
B. The director is normally the shortest parasitic element
  C. The driven element is the longest parasitic element
  D. Low feed-point impedance increases bandwidth

## Slide 13: G9A06 What is one effect of increasing the boom length and adding directors to a Yagi antenna?
  A. Gain increases
  B. SWR increases
  C. Weight decreases
  D. Wind load decreases

## Slide 14: G9A06 What is one effect of increasing the boom length and adding directors to a Yagi antenna?
A. Gain increases
  B. SWR increases
  C. Weight decreases
  D. Wind load decreases

## Slide 15: G9A07 Why is a Yagi antenna often used for radio communications on the 20-meter band?
  A. It provides excellent omnidirectional coverage in the horizontal Plane
  B. It is smaller, less expensive and easier to erect than a dipole or vertical antenna
  C. It helps reduce interference from other stations off to the side or behind
  D. It provides the highest possible angle of radiation for the HF bands

## Slide 16: G9A07 Why is a Yagi antenna often used for radio communications on the 20-meter band?
  A. It provides excellent omnidirectional coverage in the horizontal Plane
  B. It is smaller, less expensive and easier to erect than a dipole or vertical antenna
C. It helps reduce interference from other stations off to the side or behind
  D. It provides the highest possible angle of radiation for the HF bands

## Slide 17: G9A08 What does "antenna front-to-back ratio" mean in reference to a Yagi antenna?
  A. The number of directors versus the number of reflectors
  B. The relative position of the driven element with respect to the reflectors and directors
  C. The power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction
  D. The power radiated in the major radiation lobe compared to the power radiated 90 degrees away from that direction

## Slide 18: G9A08 What does "antenna front-to-back ratio" mean in reference to a Yagi antenna?
  A. The number of directors versus the number of reflectors
  B. The relative position of the driven element with respect to the reflectors and directors
C. The power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction
  D. The power radiated in the major radiation lobe compared to the power radiated 90 degrees away from that direction

## Slide 19: G9A09 What is the "main lobe" of a Yagi antenna radiation pattern?
  A. The direction of least radiation from the antenna
  B. The point of maximum current in a radiating antenna element
  C. The maximum voltage standing wave point on a radiating element
  D. The direction of maximum radiated field strength from the antenna

## Slide 20: G9A09 What is the "main lobe" of a Yagi antenna radiation pattern?
  A. The direction of least radiation from the antenna
  B. The point of maximum current in a radiating antenna element
  C. The maximum voltage standing wave point on a radiating element
D. The direction of maximum radiated field strength from the antenna

## Slide 21: G9A10 What is a good way to get maximum performance from a Yagi antenna?
  A. Optimize the lengths and spacing of the elements
  B. Use RG-58 feed-line
  C. Use a reactance bridge to measure the antenna performance from each direction around the antenna
  D. Avoid using towers higher than 30 feet above the ground

## Slide 22: G9A10 What is a good way to get maximum performance from a Yagi antenna?
A. Optimize the lengths and spacing of the elements
  B. Use RG-58 feed-line
  C. Use a reactance bridge to measure the antenna performance from each direction around the antenna
  D. Avoid using towers higher than 30 feet above the ground

## Slide 23: G9A11 Which of the following is NOT a Yagi antenna design variable that should be considered to optimize the forward gain, front-to-rear ratio and SWR bandwidth?
  A. The physical length of the boom
  B. The number of elements on the boom
  C. The spacing of each element along the boom
  D. The polarization of the antenna elements

## Slide 24: G9A11 Which of the following is NOT a Yagi antenna design variable that should be considered to optimize the forward gain, front-to-rear ratio and SWR bandwidth?
  A. The physical length of the boom
  B. The number of elements on the boom
  C. The spacing of each element along the boom
D. The polarization of the antenna elements

## Slide 25: Quad antenna
Notes: The driven element of a quad is a full wave loop, so each side is quarter wave. In this picture the feed is along the bottom, horizontal wire. This means the polarization of this antenna is horizontal. If the antenna were rotated 90 degrees so the feed were on a vertical side, the polarization would be vertical. Like the Yagi, reflector elements are ~3% larger and director elements are ~3% smaller than driven elements.

## Slide 26: G9B01 Approximately how long is each side of a cubical-quad antenna driven element for 21.4 MHz?
  A. 1.17 feet
  B. 11.7 feet
  C. 47 feet
  D. 469 feet

## Slide 27: G9B01 Approximately how long is each side of a cubical-quad antenna driven element for 21.4 MHz?
  A. 1.17 feet
B. 11.7 feet
  C. 47 feet
  D. 469 feet

## Slide 28: G9B02 Approximately how long is each side of a cubical-quad antenna driven element for 14.3 MHz?
  A. 17.6 feet
  B. 23.4 feet
  C. 70.3 feet
  D. 175 feet

## Slide 29: G9B02 Approximately how long is each side of a cubical-quad antenna driven element for 14.3 MHz?
A. 17.6 feet
  B. 23.4 feet
  C. 70.3 feet
  D. 175 feet

## Slide 30: G9B03 Approximately how long is each side of a cubical-quad antenna reflector element for 29.6 MHz?
  A. 8.23 feet
  B. 8.7 feet
  C. 9.7 feet
  D. 34.8 feet

## Slide 31: G9B03 Approximately how long is each side of a cubical-quad antenna reflector element for 29.6 MHz?
  A. 8.23 feet
B. 8.7 feet
  C. 9.7 feet
  D. 34.8 feet

## Slide 32: Delta Loop
Notes: Delta loop antennas also have full wave elements and offer performance similar to quad antennas. Because of the large elements, 2 element quads and deltas offer similar performance to a 3 element yagi. In reference to the test questions, quads and deltas have nearly identical characteristics to yagis, just a bit more gain.

## Slide 33: G9B04 Approximately how long is each leg of a symmetrical delta-loop antenna driven element for 28.7 MHz?
  A. 8.75 feet
  B. 11.7 feet
  C. 23.4 feet
  D. 35 feet

## Slide 34: G9B04 Approximately how long is each leg of a symmetrical delta-loop antenna driven element for 28.7 MHz?
  A. 8.75 feet
B. 11.7 feet
  C. 23.4 feet
  D. 35 feet

## Slide 35: G9B05 Approximately how long is each leg of a symmetrical delta-loop antenna driven element for 24.9 MHz?
  A. 10.99 feet
  B. 12.95 feet
  C. 13.45 feet
  D. 40.36 feet

## Slide 36: G9B05 Approximately how long is each leg of a symmetrical delta-loop antenna driven element for 24.9 MHz?
  A. 10.99 feet
  B. 12.95 feet
C. 13.45 feet
  D. 40.36 feet

## Slide 37: G9B06 Approximately how long is each leg of a symmetrical delta-loop antenna reflector element for 14.1 MHz?
  A. 18.26 feet
  B. 23.76 feet
  C. 24.35 feet
  D. 73.05 feet

## Slide 38: G9B06 Approximately how long is each leg of a symmetrical delta-loop antenna reflector element for 14.1 MHz?
  A. 18.26 feet
  B. 23.76 feet
C. 24.35 feet
  D. 73.05 feet

## Slide 39: G9B07 Which statement about two-element quad antennas is true?
  A. They compare favorably with a three-element Yagi
  B. They perform poorly above HF
  C. They perform very well only at HF
  D. They are effective only when constructed using insulated wire

## Slide 40: G9B07 Which statement about two-element quad antennas is true?
A. They compare favorably with a three-element Yagi
  B. They perform poorly above HF
  C. They perform very well only at HF
  D. They are effective only when constructed using insulated wire

## Slide 41: G9B08 Compared to a dipole antenna, what are the directional radiation characteristics of a cubical-quad antenna?
  A. The quad has more directivity in the horizontal plane but less directivity in the vertical plane
  B. The quad has less directivity in the horizontal plane but more directivity in the vertical plane
  C. The quad has less directivity in both horizontal and vertical planes
  D. The quad has more directivity in both horizontal and vertical planes

## Slide 42: G9B08 Compared to a dipole antenna, what are the directional radiation characteristics of a cubical-quad antenna?
  A. The quad has more directivity in the horizontal plane but less directivity in the vertical plane
  B. The quad has less directivity in the horizontal plane but more directivity in the vertical plane
  C. The quad has less directivity in both horizontal and vertical planes
D. The quad has more directivity in both horizontal and vertical planes

## Slide 43: G9B09 Moving the feed point of a multielement quad antenna from a side parallel to the ground to a side perpendicular to the ground will have what effect?
  A. It will significantly increase the antenna feed-point impedance
  B. It will significantly decrease the antenna feed-point impedance
  C. It will change the antenna polarization from vertical to horizontal
  D. It will change the antenna polarization from horizontal to vertical

## Slide 44: G9B09 Moving the feed point of a multielement quad antenna from a side parallel to the ground to a side perpendicular to the ground will have what effect?
  A. It will significantly increase the antenna feed-point impedance
  B. It will significantly decrease the antenna feed-point impedance
  C. It will change the antenna polarization from vertical to horizontal
D. It will change the antenna polarization from horizontal to vertical

## Slide 45: G9B10 What does the term "antenna front-to-back ratio" mean in reference to a cubical-quad antenna?
  A. The number of directors versus the number of reflectors
  B. The relative position of the driven element with respect to the reflectors and directors
  C. The power radiated in the major radiation lobe compared to the power radiated 90 degrees away from that direction
  D. The power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction

## Slide 46: G9B10 What does the term "antenna front-to-back ratio" mean in reference to a cubical-quad antenna?
  A. The number of directors versus the number of reflectors
  B. The relative position of the driven element with respect to the reflectors and directors
  C. The power radiated in the major radiation lobe compared to the power radiated 90 degrees away from that direction
D. The power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction

## Slide 47: G9B11 What is the "main lobe" of a cubical-quad antenna radiation pattern?
  A. The direction of least radiation from an antenna
  B. The point of maximum current in a radiating antenna element
  C. The direction of maximum radiated field strength from the antenna
  D. The maximum voltage standing wave point on a radiating element

## Slide 48: G9B11 What is the "main lobe" of a cubical-quad antenna radiation pattern?
  A. The direction of least radiation from an antenna
  B. The point of maximum current in a radiating antenna element
C. The direction of maximum radiated field strength from the antenna
  D. The maximum voltage standing wave point on a radiating element

## Slide 49: G9C01 What type of multiband transmitting antenna does NOT require a feed-line?
  A. An end-fed random-wire antenna
  B. A triband Yagi antenna
  C. A delta-loop antenna
  D. A Beverage antenna

## Slide 50: G9C01 What type of multiband transmitting antenna does NOT require a feed-line?
A. An end-fed random-wire antenna
  B. A triband Yagi antenna
  C. A delta-loop antenna
  D. A Beverage antenna

## Slide 51: G9C02 What is one advantage of using a random-wire antenna?
  A. It is more efficient than any other kind of antenna
  B. It will keep RF energy out of your station
  C. It doesn't need an impedance matching network
  D. It is a multiband antenna

## Slide 52: G9C02 What is one advantage of using a random-wire antenna?
  A. It is more efficient than any other kind of antenna
  B. It will keep RF energy out of your station
  C. It doesn't need an impedance matching network
D. It is a multiband antenna

## Slide 53: G9C03 What is one disadvantage of a random-wire antenna?
  A. It must be longer than 1 wavelength
  B. You may experience RF feedback in your station
  C. It usually produces vertically polarized radiation
  D. You must use an inverted-T matching network for multiband operation

## Slide 54: G9C03 What is one disadvantage of a random-wire antenna?
  A. It must be longer than 1 wavelength
B. You may experience RF feedback in your station
  C. It usually produces vertically polarized radiation
  D. You must use an inverted-T matching network for multiband operation

## Slide 55: Vertical Antenna
  Standard ¼ wave vertical has a feedpoint impedance of ~35 ohms
  Sloping ground radials downward raises feedpoint impedance
Notes: If the vertical is ground mounted, the radials should be on or near the surface of the ground.

## Slide 56: G9C04 What is an advantage of downward sloping radials on a ground-plane antenna?
  A. It lowers the radiation angle
  B. It brings the feed-point impedance closer to 300 ohms
  C. It increases the radiation angle
  D. It brings the feed-point impedance closer to 50 ohms

## Slide 57: G9C04 What is an advantage of downward sloping radials on a ground-plane antenna?
  A. It lowers the radiation angle
  B. It brings the feed-point impedance closer to 300 ohms
  C. It increases the radiation angle
D. It brings the feed-point impedance closer to 50 ohms

## Slide 58: G9C05 What happens to the feed-point impedance of a ground-plane antenna when its radials are changed from horizontal to downward-sloping?
  A. It decreases
  B. It increases
  C. It stays the same
  D. It approaches zero

## Slide 59: G9C05 What happens to the feed-point impedance of a ground-plane antenna when its radials are changed from horizontal to downward-sloping?
  A. It decreases
B. It increases
  C. It stays the same
  D. It approaches zero

## Slide 60: Dipole Radiation
Notes: If the dipole antenna was the red line, the lobes above and below show the radiation pattern at ½ wavelength above the ground. This pattern actually rotates around the wire like a donut. As the antenna is lowered below ½ wavelength, the lobes flatten until it becomes nearly omnidirectional.

## Slide 61: G9C06 What is the low-angle radiation pattern of an ideal half-wavelength dipole HF antenna installed a half-wavelength high, parallel to the earth?
  A. It is a figure-eight at right angles to the antenna
  B. It is a figure-eight off both ends of the antenna
  C. It is a circle (equal radiation in all directions)
  D. It is two smaller lobes on one side of the antenna, and one larger lobe on the other side

## Slide 62: G9C06 What is the low-angle radiation pattern of an ideal half-wavelength dipole HF antenna installed a half-wavelength high, parallel to the earth?
A. It is a figure-eight at right angles to the antenna
  B. It is a figure-eight off both ends of the antenna
  C. It is a circle (equal radiation in all directions)
  D. It is two smaller lobes on one side of the antenna, and one larger lobe on the other side

## Slide 63: G9C07 How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna?
  A. If the antenna is too high, the pattern becomes unpredictable
  B. Antenna height has no effect on the pattern
  C. If the antenna is less than one-half wavelength high, the azimuthal pattern is almost omnidirectional
  D. If the antenna is less than one-half wavelength high, radiation off the ends of the wire is eliminated

## Slide 64: G9C07 How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna?
  A. If the antenna is too high, the pattern becomes unpredictable
  B. Antenna height has no effect on the pattern
C. If the antenna is less than one-half wavelength high, the azimuthal pattern is almost omnidirectional
  D. If the antenna is less than one-half wavelength high, radiation off the ends of the wire is eliminated

## Slide 65: G9C08 If the horizontal radiation pattern of an antenna shows a major lobe at 0 degrees and a minor lobe at 180 degrees, how would you describe the radiation pattern of this antenna?
  A. Most of the signal would be radiated towards 180 degrees and a smaller amount would be radiated towards 0 degrees
  B. Almost no signal would be radiated towards 0 degrees and a small amount would be radiated towards 180 degrees
  C. Almost all the signal would be radiated equally towards 0 degrees and 180 degrees
  D. Most of the signal would be radiated towards 0 degrees and a smaller amount would be radiated towards 180 degrees

## Slide 66: G9C08 If the horizontal radiation pattern of an antenna shows a major lobe at 0 degrees and a minor lobe at 180 degrees, how would you describe the radiation pattern of this antenna?
  A. Most of the signal would be radiated towards 180 degrees and a smaller amount would be radiated towards 0 degrees
  B. Almost no signal would be radiated towards 0 degrees and a small amount would be radiated towards 180 degrees
  C. Almost all the signal would be radiated equally towards 0 degrees and 180 degrees
D. Most of the signal would be radiated towards 0 degrees and a smaller amount would be radiated towards 180 degrees

## Slide 67: G9C09 If a slightly shorter parasitic element is placed 0.1 wavelength away and parallel to an HF dipole antenna mounted above ground, what effect will this have on the antenna's radiation pattern?
  A. The radiation pattern will not be affected
  B. A major lobe will develop in the horizontal plane, parallel to the two elements
  C. A major lobe will develop in the vertical plane, away from the ground
  D. A major lobe will develop in the horizontal plane, toward the parasitic element

## Slide 68: G9C09 If a slightly shorter parasitic element is placed 0.1 wavelength away and parallel to an HF dipole antenna mounted above ground, what effect will this have on the antenna's radiation pattern?
  A. The radiation pattern will not be affected
  B. A major lobe will develop in the horizontal plane, parallel to the two elements
  C. A major lobe will develop in the vertical plane, away from the ground
D. A major lobe will develop in the horizontal plane, toward the parasitic element

## Slide 69: G9C10 If a slightly longer parasitic element is placed 0.1 wavelength away and parallel to an HF dipole antenna mounted above ground, what effect will this have on the antenna's radiation pattern?
  A. The radiation pattern will not be affected
  B. A major lobe will develop in the horizontal plane, away from the parasitic element, toward the dipole
  C. A major lobe will develop in the vertical plane, away from the ground
  D. A major lobe will develop in the horizontal plane, parallel to the two elements

## Slide 70: G9C10 If a slightly longer parasitic element is placed 0.1 wavelength away and parallel to an HF dipole antenna mounted above ground, what effect will this have on the antenna's radiation pattern?
  A. The radiation pattern will not be affected
B. A major lobe will develop in the horizontal plane, away from the parasitic element, toward the dipole
  C. A major lobe will develop in the vertical plane, away from the ground
  D. A major lobe will develop in the horizontal plane, parallel to the two elements

## Slide 71: G9C11 Where should the radial wires of a ground-mounted vertical antenna system be placed?
  A. As high as possible above the ground
  B. Parallel to the antenna element
  C. On the surface or buried a few inches below the ground
  D. At the top of the antenna

## Slide 72: G9C11 Where should the radial wires of a ground-mounted vertical antenna system be placed?
  A. As high as possible above the ground
  B. Parallel to the antenna element
C. On the surface or buried a few inches below the ground
  D. At the top of the antenna

## Slide 73: Feedlines
Notes: Impedance of feedlines is generally determines by the distance between conductors and their size. Amateur antenna are generally fed with 50 ohm coax or 450 ohm ladder/window line. Occasionally TV-style 300 ohm twin lead or 75 ohm coax is used for certain antenna types. Ultimately, these feedlines must all be matched to the typical 50 ohm input on the radio to insure proper power transfer to the antenna. Many dipole style antennas use a balun (BALanced to UNbalanced) to match the balanced antenna feedpoint to an unbalanced 50 ohm coaxial feed.

## Slide 74: G9D01 Which of the following factors help determine the characteristic impedance of a parallel-conductor antenna feed-line?
  A. The distance between the centers of the conductors and the radius of the conductors
  B. The distance between the centers of the conductors and the length of the line
  C. The radius of the conductors and the frequency of the signal
  D. The frequency of the signal and the length of the line

## Slide 75: G9D01 Which of the following factors help determine the characteristic impedance of a parallel-conductor antenna feed-line?
A. The distance between the centers of the conductors and the radius of the conductors
  B. The distance between the centers of the conductors and the length of the line
  C. The radius of the conductors and the frequency of the signal
  D. The frequency of the signal and the length of the line

## Slide 76: G9D02 What is the typical characteristic impedance of coaxial cables used for antenna feed-lines at amateur stations?
  A. 25 and 30 ohms
  B. 50 and 75 ohms
  C. 80 and 100 ohms
  D. 500 and 750 ohms

## Slide 77: G9D02 What is the typical characteristic impedance of coaxial cables used for antenna feed-lines at amateur stations?
  A. 25 and 30 ohms
B. 50 and 75 ohms
  C. 80 and 100 ohms
  D. 500 and 750 ohms

## Slide 78: G9D03 What is the characteristic impedance of flat-ribbon TV-type twin-lead?
  A. 50 ohms
  B. 75 ohms
  C. 100 ohms
  D. 300 ohms

## Slide 79: G9D03 What is the characteristic impedance of flat-ribbon TV-type twin-lead?
  A. 50 ohms
  B. 75 ohms
  C. 100 ohms
D. 300 ohms

## Slide 80: G9D04 What is the typical cause of power being reflected back down an antenna feed-line?
  A. Operating an antenna at its resonant frequency
  B. Using more transmitter power than the antenna can handle
  C. A difference between feed line impedance and antenna feed-point impedance
  D. Feeding the antenna with unbalanced feed-line

## Slide 81: G9D04 What is the typical cause of power being reflected back down an antenna feed-line?
  A. Operating an antenna at its resonant frequency
  B. Using more transmitter power than the antenna can handle
C. A difference between feed line impedance and antenna feed-point impedance
  D. Feeding the antenna with unbalanced feed-line

## Slide 82: G9D05 What must be done to prevent standing waves of voltage and current on an antenna feed-line?
  A. The antenna feed point must be at DC ground potential
  B. The feed line must be cut to an odd number of electrical quarter-wavelengths long
  C. The feed line must be cut to an even number of physical half wavelengths long
  D. The antenna feed-point impedance must be matched to the characteristic impedance of the feed-line

## Slide 83: G9D05 What must be done to prevent standing waves of voltage and current on an antenna feed-line?
  A. The antenna feed point must be at DC ground potential
  B. The feed line must be cut to an odd number of electrical quarter-wavelengths long
  C. The feed line must be cut to an even number of physical half wavelengths long
D. The antenna feed-point impedance must be matched to the characteristic impedance of the feed-line

## Slide 84: G9D06 Under what conditions would you use an inductively coupled matching network with a dipole antenna fed with parallel-conductor feed line?
  A. It would not normally be used with parallel-conductor feed lines
  B. It would be used to increase the SWR to an acceptable level
  C. It would be used to match the unbalanced transmitter output to the balanced parallel-conductor feed line
  D. It would be used at the antenna feed point to tune out the radiation resistance

## Slide 85: G9D06 Under what conditions would you use an inductively coupled matching network with a dipole antenna fed with parallel-conductor feed line?
  A. It would not normally be used with parallel-conductor feed lines
  B. It would be used to increase the SWR to an acceptable level
C. It would be used to match the unbalanced transmitter output to the balanced parallel-conductor feed line
  D. It would be used at the antenna feed point to tune out the radiation resistance

## Slide 86
Coax Cable Signal Loss (Attenuation) in dB per 100ft |  |  |  |  |  |  |  | 
Loss | RG-174 | RG-58 | RG-8X | RG-213 | RG-6 | RG-11 | 9913 | LMR-400
1MHz | 1.9dB | 0.4dB | 0.5dB | 0.2dB | 0.2dB | 0.2dB | 0.2dB | 0.3dB
10MHz | 3.3dB | 1.4dB | 1.0dB | 0.6dB | 0.6dB | 0.4dB | 0.4dB | 0.5dB
50MHz | 6.6dB | 3.3dB | 2.5dB | 1.6dB | 1.4dB | 1.0dB | 0.9dB | 0.9dB
100MHz | 8.9dB | 4.9dB | 3.6dB | 2.2dB | 2.0dB | 1.6dB | 1.4dB | 1.4dB
200MHz | 11.9dB | 7.3dB | 5.4dB | 3.3dB | 2.8dB | 2.3dB | 1.8dB | 1.8dB
400MHz | 17.3dB | 11.2dB | 7.9dB | 4.8dB | 4.3dB | 3.5dB | 2.6dB | 2.6dB
700MHz | 26.0dB | 16.9dB | 11.0dB | 6.6dB | 5.6dB | 4.7dB | 3.6dB | 3.5dB
900MHz | 27.9dB | 20.1dB | 12.6dB | 7.7dB | 6.0dB | 5.4dB | 4.2dB | 3.9dB
1GHz | 32.0dB | 21.5dB | 13.5dB | 8.3dB | 6.1dB | 5.6dB | 4.5dB | 4.1dB
Imped | 50ohm | 50ohm | 50ohm | 50ohm | 75ohm | 75ohm | 50ohm | 50ohm
Notes: Notice how losses go up as frequency increases for each coax type. Coax losses shown above are for 100 feet lengths. Loss is a length multiplier, so a 200 ft length would have twice the loss shown above and a 50 ft length would have half the loss. This multiplier factor is why you should keep cable installation lengths between radios and antennas as short as practical!

## Slide 87: G9D07 If a 160-meter signal and a 2-meter signal pass through the same coaxial cable, how will the attenuation of the two signals compare?
  A. It will be greater at 2 meters
  B. It will be less at 2 meters
  C. It will be the same at both frequencies
  D. It will depend on the emission type in use

## Slide 88: G9D07 If a 160-meter signal and a 2-meter signal pass through the same coaxial cable, how will the attenuation of the two signals compare?
A. It will be greater at 2 meters
  B. It will be less at 2 meters
  C. It will be the same at both frequencies
  D. It will depend on the emission type in use

## Slide 89: G9D08 In what values are RF feed line losses usually expressed?
  A. Bels/1000 ft
  B. dB/1000 ft
  C. Bels/100 ft
  D. dB/100 ft

## Slide 90: G9D08 In what values are RF feed line losses usually expressed?
  A. Bels/1000 ft
  B. dB/1000 ft
  C. Bels/100 ft
D. dB/100 ft

## Slide 91: G9D09 What standing-wave-ratio will result from the connection of a 50-ohm feed line to a resonant antenna having a 200-ohm feed-point impedance?
  A. 4:1
  B. 1:4
  C. 2:1
  D. 1:2

## Slide 92: G9D09 What standing-wave-ratio will result from the connection of a 50-ohm feed line to a resonant antenna having a 200-ohm feed-point impedance?
A. 4:1
  B. 1:4
  C. 2:1
  D. 1:2

## Slide 93: G9D10 What standing-wave-ratio will result from the connection of a 50-ohm feed line to a resonant antenna having a 10-ohm feed-point impedance?
  A. 2:1
  B. 50:1
  C. 1:5
  D. 5:1

## Slide 94: G9D10 What standing-wave-ratio will result from the connection of a 50-ohm feed line to a resonant antenna having a 10-ohm feed-point impedance?
  A. 2:1
  B. 50:1
  C. 1:5
D. 5:1

## Slide 95: G9D11 What standing-wave-ratio will result from the connection of a 50-ohm feed line to a resonant antenna having a 50-ohm feed-point impedance?
  A. 2:1
  B. 1:1
  C. 50:50
  D. 0:0

## Slide 96: G9D11 What standing-wave-ratio will result from the connection of a 50-ohm feed line to a resonant antenna having a 50-ohm feed-point impedance?
  A. 2:1
B. 1:1
  C. 50:50
  D. 0:0

## Slide 97: G9D12 What physical aspects of an air-insulated parallel-conductor transmission line determine its characteristic impedance?
  A. The RF resistance of the conductors and the length of the conductors
  B. The diameter of the conductors and the distance between their centers
  C. The RF resistance of the conductors and the dielectric constant of the insulation
  D. The resistance of each wire to RF ground and the antenna's impedance

## Slide 98: G9D12 What physical aspects of an air-insulated parallel-conductor transmission line determine its characteristic impedance?
  A. The RF resistance of the conductors and the length of the conductors
B. The diameter of the conductors and the distance between their centers
  C. The RF resistance of the conductors and the dielectric constant of the insulation
  D. The resistance of each wire to RF ground and the antenna's impedance

## Slide 99: G9D13 What would be the SWR if you feed a vertical antenna that has a 25-ohm feed-point impedance with 50-ohm coaxial cable?
  A. 2:1
  B. 2.5:1
  C. 1.25:1
  D. You cannot determine SWR from impedance values

## Slide 100: G9D13 What would be the SWR if you feed a vertical antenna that has a 25-ohm feed-point impedance with 50-ohm coaxial cable?
A. 2:1
  B. 2.5:1
  C. 1.25:1
  D. You cannot determine SWR from impedance values

## Slide 101: G9D14 What would be the SWR if you feed a folded dipole antenna that has a 300-ohm feed-point impedance with 50-ohm coaxial cable?
  A. 1.5:1
  B. 3:1
  C. 6:1
  D. You cannot determine SWR from impedance values

## Slide 102: G9D14 What would be the SWR if you feed a folded dipole antenna that has a 300-ohm feed-point impedance with 50-ohm coaxial cable?
  A. 1.5:1
  B. 3:1
C. 6:1
  D. You cannot determine SWR from impedance values