## Slide 1: T3 – Operating Practices 4 exam questions – 4 groups
  T3A Choosing an operating frequency, calling CQ, calling another station, test transmissions
  T3B Use of minimum power, band plans, repeater coordination, mode restricted sub-bands
  T3C Courtesy and respect for others, sensitive subject areas, obscene and indecent language
  T3D Interference to and from consumer devices, public relations, intentional and unintentional interference
Notes: 2006 Technician Class (Element 2) Master syllabus
Released 6 February, 2006
35 Exam questions
http://www.microhams.com
Created by Scott N7SS

## Slide 2: Basic Voice (Phone) Communication Rules
Be Polite
  Do not interrupt other operators
  Do not hog the channel
Listen before you talk
  If someone else is using the frequency, let them have it, move to another frequency
Keep it Simple
  Speak Clearly
  Do not rush or slur
  Use terms people understand, avoid colloquialisms
Use the ITU Phonetic Alphabet to Spell Words/Callsigns
Use Common Abbreviations and TLA (Three Letter Acronyms)
Use the Correct Sideband
  >9MHz - Use Upper Side Band
Always Identify Yourself

## Slide 3: Starting a Conversation (QSO)
Open Call – I will talk to anybody (CQ)
  Listen / Check – Is this frequency in use?
    This is KD7PSV
  Place the call
    CQ CQ calling CQ. This is KD7PSV, Kilo Delta Seven Papa Sierra Victor, KD7PSV calling CQ and standing by.
  To Answer
    KD7PSV, this is N7SS, November 7 Sierra Sierra, N7SS over
Direct Call – I know who I want to talk to
  Listen / Check – Is this frequency in use?
    This is KD7PSV
  Place the call
    KD7PSV calling N7SS, Kilo Delta Seven Papa Sierra Victor calling November Seven Sierra Sierra, KD7PSV calling N7SS
  Answering a call
    KD7PSV this is N7SS, over
Ending the Conversation
    This is KD7PSV clear
    This is N7SS clear

## Slide 4: T3A01 Which of the following should you do when selecting a frequency on which to transmit?
  A. Call CQ to see if anyone is listening
  B. Listen to determine if the frequency is busy
  C. Transmit on a frequency that allows your signals to be heard
  D. Check for maximum power output

## Slide 5: T3A01 Which of the following should you do when selecting a frequency on which to transmit?
  A. Call CQ to see if anyone is listening
B. Listen to determine if the frequency is busy
  C. Transmit on a frequency that allows your signals to be heard
  D. Check for maximum power output

## Slide 6: T3A02 How do you call another station on a repeater if you know the station's call sign?
  A. Say "break, break" then say the station's call sign
  B. Say the station's call sign then identify your own station
  C. Say "CQ" three times then the other station's call sign
  D. Wait for the station to call "CQ" then answer it

## Slide 7: T3A02 How do you call another station on a repeater if you know the station's call sign?
  A. Say "break, break" then say the station's call sign
B. Say the station's call sign then identify your own station
  C. Say "CQ" three times then the other station's call sign
  D. Wait for the station to call "CQ" then answer it

## Slide 8: T3A03 How do you indicate you are looking for any station with which to make contact?
  A. CQ followed by your callsign
  B. RST followed by your callsign
  C. QST followed by your callsign
  D. SK followed by your callsign

## Slide 9: T3A03 How do you indicate you are looking for any station with which to make contact?
A. CQ followed by your callsign
  B. RST followed by your callsign
  C. QST followed by your callsign
  D. SK followed by your callsign

## Slide 10: Common Abbreviations
CQ Call Any Station
RST Readability, Signal Strength, Tone
DX Distance, foreign country
73 Best Regards
DE From, this is
PTT Push To Talk
VOX Voice Activated Switch

## Slide 11: T3A04 What should you transmit when responding to a call of CQ?
  A. Your own CQ followed by the other station’s callsign
  B. Your callsign followed by the other station’s callsign
  C. The other station’s callsign followed by your callsign
  D. A signal report followed by your callsign

## Slide 12: T3A04 What should you transmit when responding to a call of CQ?
  A. Your own CQ followed by the other station’s callsign
  B. Your callsign followed by the other station’s callsign
C. The other station’s callsign followed by your callsign
  D. A signal report followed by your callsign

## Slide 13: T3A05 What term describes a brief test transmission that does not include any station identification?
  A. A test emission with no identification required
  B. An illegal un-modulated transmission
  C. An illegal unidentified transmission
  D. A non-voice ID transmission

## Slide 14: T3A05 What term describes a brief test transmission that does not include any station identification?
  A. A test emission with no identification required
  B. An illegal un-modulated transmission
C. An illegal unidentified transmission
  D. A non-voice ID transmission

## Slide 15: T3A06 What must an amateur do when making a transmission to test equipment or antennas?
  A. Properly identify the station
  B. Make test transmissions only after 10:00 PM local time
  C. Notify the FCC of the test transmission
  D. State the purpose of the test during the test procedure

## Slide 16: T3A06 What must an amateur do when making a transmission to test equipment or antennas?
A. Properly identify the station
  B. Make test transmissions only after 10:00 PM local time
  C. Notify the FCC of the test transmission
  D. State the purpose of the test during the test procedure

## Slide 17: T3A07 Which of the following is true when making a test transmission?
  A. Station identification is not required if the transmission is less than 15 seconds
  B. Station identification is not required if the transmission is less than 1 watt
  C. Station identification is required only if your station can be heard
  D. Station identification is required at least every ten minutes and at the end of every transmission.

## Slide 18: T3A07 Which of the following is true when making a test transmission?
  A. Station identification is not required if the transmission is less than 15 seconds
  B. Station identification is not required if the transmission is less than 1 watt
  C. Station identification is required only if your station can be heard
D. Station identification is required at least every ten minutes and at the end of every transmission.

## Slide 19: T3A08 What is the meaning of the procedural signal "CQ"?
  A. Call on the quarter hour
  B. New antenna is being tested (no station should answer)
  C. Only the called station should transmit
  D. Calling any station

## Slide 20: T3A08 What is the meaning of the procedural signal "CQ"?
  A. Call on the quarter hour
  B. New antenna is being tested (no station should answer)
  C. Only the called station should transmit
D. Calling any station

## Slide 21: T3A09 Why should you avoid using cute phrases or word combinations to identify your station?
  A. They are not easily understood by some operators
  B. They might offend some operators
  C. They do not meet FCC identification requirements
  D. They might be interpreted as codes or ciphers intended to obscure your identification

## Slide 22: T3A09 Why should you avoid using cute phrases or word combinations to identify your station?
A. They are not easily understood by some operators
  B. They might offend some operators
  C. They do not meet FCC identification requirements
  D. They might be interpreted as codes or ciphers intended to obscure your identification

## Slide 23: T3A10 What brief statement is often used in place of "CQ" to indicate that you are listening for calls on a repeater?
  A. Say "Hello test" followed by your call sign
  B. Say your call sign
  C. Say the repeater call sign followed by your call sign
  D. Say the letters "QSY" followed by your call sign

## Slide 24: T3A10 What brief statement is often used in place of "CQ" to indicate that you are listening for calls on a repeater?
  A. Say "Hello test" followed by your call sign
B. Say your call sign
  C. Say the repeater call sign followed by your call sign
  D. Say the letters "QSY" followed by your call sign

## Slide 25: T3A11 Why should you use the International Telecommunication Union (ITU) phonetic alphabet when identifying your station?
  A. The words are internationally recognized substitutes for letters
  B. There is no advantage
  C. The words have been chosen to represent amateur radio terms
  D. It preserves traditions begun in the early days of amateur radio

## Slide 26: ITU Phonetic Alphabet
Agreed upon words to represent the letters of the “roman alphabet”.
The boldfaced syllables are emphasized. The pronunciations shown in this table were designed for those who speak any of the international languages. The pronunciations given for “Oscar”, “Papa” and “Victor” may seem awkward to English-speaking people in the US.
A Alfa AL FAH
B Bravo BRAH VOH
C Charlie CHAR LEE
D Delta DELL TAH
E Echo ECK OH
F Foxtrot FOKS TROT
G Golf GOLF
H Hotel HOH TELL
I India IN DEE AH
J Juliett JEW LEE ETT
K Kilo KEY LOH
L Lima LEE MAH
M Mike MIKE
N November NO VEM BER
O Oscar OSS CAH
P Papa PAH PAH
Q Quebec KEH BECK
R Romeo ROW ME OH
S Sierra SEE AIR RAH
T Tango TANG GO
U Uniform YOU NEE FORM
V Victor VIK TAH
W Whiskey WISS KEY
X X-Ray ECKS RAY
Y Yankee YANG KEY
Z Zulu ZOO LOO

## Slide 27: T3A11 Why should you use the International Telecommunication Union (ITU) phonetic alphabet when identifying your station?
A. The words are internationally recognized substitutes for letters
  B. There is no advantage
  C. The words have been chosen to represent amateur radio terms
  D. It preserves traditions begun in the early days of amateur radio

## Slide 28: T3B01 What is a band plan?
  A. A voluntary guideline, beyond the divisions established by the FCC for using different operating modes within an amateur band
  B. A guideline from the FCC for making amateur frequency band allocations
  C. A guideline for operating schedules within an amateur band published by the FCC
  D. A plan devised by a local group

## Slide 29: T3B01 What is a band plan?
A. A voluntary guideline, beyond the divisions established by the FCC for using different operating modes within an amateur band
  B. A guideline from the FCC for making amateur frequency band allocations
  C. A guideline for operating schedules within an amateur band published by the FCC
  D. A plan devised by a local group

## Slide 30
23cm
33cm
70cm
1.25m
2m
6m
2300 2310 2390 2450
1240 1300
902 928
420 430 435 438 450
Not Available North of Line A |  | Satellite | 
219 220 222 225
144 144.1 148
CW | 
50 50.1 54
 No Code Technicians Have All Privileges On The Above Bands 
13cm
Point to Point Digital Links |  | 
CW | 
70cm - 5 MHz repeater frequency separation (Split)
2m - 600 kHz repeater frequency separation (Split)
Notes: The FCC has mandated the areas colored (other than blue) to specific purposes. The remaining areas are divided by the amateur community into a band plan to insure most effective use of the spectrum and minimize interference. This band plan is not law but voluntary. If the FCC does get involved in a dispute, they will use the local band plan as a means to resolve the dispute.

## Slide 31: T3B02 Which of the following statements is true of band plans?
  A. They are mandated by the FCC to regulate spectrum use
  B. They are mandated by the ITU
  C. They are voluntary guidelines for efficient use of the radio spectrum
  D. They are mandatory only in the US

## Slide 32: T3B02 Which of the following statements is true of band plans?
  A. They are mandated by the FCC to regulate spectrum use
  B. They are mandated by the ITU
C. They are voluntary guidelines for efficient use of the radio spectrum
  D. They are mandatory only in the US

## Slide 33: T3B03 Who developed the band plans used by amateur radio operators?
  A. The US Congress
  B. The FCC
  C. The amateur community
  D. The Interstate Commerce Commission

## Slide 34: T3B03 Who developed the band plans used by amateur radio operators?
  A. The US Congress
  B. The FCC
C. The amateur community
  D. The Interstate Commerce Commission

## Slide 35: T3B04 Who is in charge of the repeater frequency band plan in your local area?
  A. The local FCC field office
  B. RACES and FEMA
  C. The recognized frequency coordination body
  D. Repeater Council of America

## Slide 36: T3B04 Who is in charge of the repeater frequency band plan in your local area?
  A. The local FCC field office
  B. RACES and FEMA
C. The recognized frequency coordination body
  D. Repeater Council of America
Notes: Locally this is the Western Washington Amateur Repeater Association (WWARA)

## Slide 37: T3B05 What is the main purpose of repeater coordination?
  A. To reduce interference and promote proper use of spectrum
  B. To coordinate as many repeaters as possible in a small area
  C. To coordinate all possible frequencies available for repeater use
  D. To promote and encourage use of simplex frequencies

## Slide 38: T3B05 What is the main purpose of repeater coordination?
A. To reduce interference and promote proper use of spectrum
  B. To coordinate as many repeaters as possible in a small area
  C. To coordinate all possible frequencies available for repeater use
  D. To promote and encourage use of simplex frequencies

## Slide 39: T3B06 Who is accountable if a repeater station inadvertently retransmits communications that violate FCC rules?
  A. The repeater trustee
  B. The repeater control operator
  C. The transmitting station
  D. All of these answers are correct

## Slide 40: T3B06 Who is accountable if a repeater station inadvertently retransmits communications that violate FCC rules?
  A. The repeater trustee
  B. The repeater control operator
C. The transmitting station
  D. All of these answers are correct

## Slide 41: T3B07 Which of these statements is true about legal power levels on the amateur bands?
  A. Always use the maximum power allowed to ensure that you complete the contact
  B. An amateur may use no more than 200 Watts PEP to make an amateur contact
  C. An amateur may use up to 1500 Watts PEP on any amateur frequency
  D. An amateur must use the minimum transmitter power necessary to carry out the desired communication

## Slide 42: T3B07 Which of these statements is true about legal power levels on the amateur bands?
  A. Always use the maximum power allowed to ensure that you complete the contact
  B. An amateur may use no more than 200 Watts PEP to make an amateur contact
  C. An amateur may use up to 1500 Watts PEP on any amateur frequency
D. An amateur must use the minimum transmitter power necessary to carry out the desired communication

## Slide 43: T3B08 Which of the bands available to Technician class licensees have mode restricted sub-bands?
  A. The 6-meter, 2-meter, and 70-centimeter bands
  B. The 2-meter and 13-centimeter bands
  C. The 6-meter, 2-meter, and 1 1/4-meter bands
  D. The 2-meter and 70-centimeter bands

## Slide 44: T3B08 Which of the bands available to Technician class licensees have mode restricted sub-bands?
  A. The 6-meter, 2-meter, and 70-centimeter bands
  B. The 2-meter and 13-centimeter bands
C. The 6-meter, 2-meter, and 1 1/4-meter bands
  D. The 2-meter and 70-centimeter bands
Notes: These sub-bands are restricted in use by the FCC. 6m and 2m both have FCC designated areas for CW operations. 1.25m has the 219-220 sub-band that is reserved for point to point digital links. These are represented by different colors on the band plan graphic slide and handout.

## Slide 45: T3B09 What emission modes are permitted in the restricted sub-band at 50.0-50.1 MHz?
  A. CW only
  B. CW and RTTY
  C. SSB only
  D. CW and SSB

## Slide 46: T3B09 What emission modes are permitted in the restricted sub-band at 50.0-50.1 MHz?
A. CW only
  B. CW and RTTY
  C. SSB only
  D. CW and SSB

## Slide 47: T3B10 What emission modes are permitted in the restricted sub-band at 144.0-144.1 MHz?
  A. CW only
  B. CW and RTTY
  C. SSB only
  D. CW and SSB

## Slide 48: T3B10 What emission modes are permitted in the restricted sub-band at 144.0-144.1 MHz?
A. CW only
  B. CW and RTTY
  C. SSB only
  D. CW and SSB

## Slide 49: T3C01 What is the proper way to break into a conversation between two stations that are using the frequency?
  A. Say your call sign between their transmissions
  B. Wait for them to finish and then call CQ
  C. Say "Break-break" between their transmissions
  D. Call one of the operators on the telephone to interrupt the conversation

## Slide 50: T3C01 What is the proper way to break into a conversation between two stations that are using the frequency?
A. Say your call sign between their transmissions
  B. Wait for them to finish and then call CQ
  C. Say "Break-break" between their transmissions
  D. Call one of the operators on the telephone to interrupt the conversation

## Slide 51: T3C02 What is considered to be proper repeater operating practice?
  A. Monitor before transmitting and keep transmissions short
  B. Identify legally
  C. Use the minimum amount of transmitter power necessary
  D. All of these answers are correct

## Slide 52: T3C02 What is considered to be proper repeater operating practice?
  A. Monitor before transmitting and keep transmissions short
  B. Identify legally
  C. Use the minimum amount of transmitter power necessary
D. All of these answers are correct

## Slide 53: T3C03 What should you do before responding to another stations call?
  A. Make sure you are operating on a permissible frequency for your license class
  B. Adjust your transmitter for maximum power output
  C. Ask the station to send their signal report and location
  D. Verify the other station’s license class

## Slide 54: T3C03 What should you do before responding to another stations call?
A. Make sure you are operating on a permissible frequency for your license class
  B. Adjust your transmitter for maximum power output
  C. Ask the station to send their signal report and location
  D. Verify the other station’s license class

## Slide 55: T3C04 What rule applies if two amateur stations want to use the same frequency?
  A. The station operator with a lesser class of license must yield the frequency to a higher-class licensee
  B. The station operator with a lower power output must yield the frequency to the station with a higher power output
  C. No frequency will be assigned for the exclusive use of any station and neither has priority
  D. Station operators in ITU Regions 1 and 3 must yield the frequency to stations in ITU Region 2

## Slide 56: T3C04 What rule applies if two amateur stations want to use the same frequency?
  A. The station operator with a lesser class of license must yield the frequency to a higher-class licensee
  B. The station operator with a lower power output must yield the frequency to the station with a higher power output
C. No frequency will be assigned for the exclusive use of any station and neither has priority
  D. Station operators in ITU Regions 1 and 3 must yield the frequency to stations in ITU Region 2

## Slide 57: T3C05 Why is indecent and obscene language prohibited in the Amateur Service?
  A. Because it is offensive to some individuals
  B. Because young children may intercept amateur communications with readily available receiving equipment
  C. Because such language is specifically prohibited by FCC Rules
  D. All of these choices are correct

## Slide 58: T3C05 Why is indecent and obscene language prohibited in the Amateur Service?
  A. Because it is offensive to some individuals
  B. Because young children may intercept amateur communications with readily available receiving equipment
  C. Because such language is specifically prohibited by FCC Rules
D. All of these choices are correct

## Slide 59: T3C06 Why should amateur radio operators avoid the use of racial or ethnic slurs when talking to other stations?
  A. Such language is prohibited by the FCC
  B. It is offensive to some people and reflects a poor public image on all amateur radio operators
  C. Some of the terms used may be unfamiliar to other operators
  D. You transmissions might be recorded for use in court

## Slide 60: T3C06 Why should amateur radio operators avoid the use of racial or ethnic slurs when talking to other stations?
  A. Such language is prohibited by the FCC
B. It is offensive to some people and reflects a poor public image on all amateur radio operators
  C. Some of the terms used may be unfamiliar to other operators
  D. You transmissions might be recorded for use in court

## Slide 61: T3C07 What should you do if you hear a newly licensed operator that is having trouble with their station?
  A. Tell them to get off the air until they learn how operate properly
  B. Report them to the FCC
  C. Contact them and offer to help with the problem
  D. Move to another frequency

## Slide 62: T3C07 What should you do if you hear a newly licensed operator that is having trouble with their station?
  A. Tell them to get off the air until they learn how operate properly
  B. Report them to the FCC
C. Contact them and offer to help with the problem
  D. Move to another frequency

## Slide 63: T3C08 Where can an official list be found of prohibited obscene and indecent words that should not be used in amateur radio?
  A. On the FCC web site
  B. There is no official list of prohibited obscene and indecent words
  C. On the Department of Commerce web site
  D. The official list is in public domain and found in all amateur study guides

## Slide 64: T3C08 Where can an official list be found of prohibited obscene and indecent words that should not be used in amateur radio?
  A. On the FCC web site
B. There is no official list of prohibited obscene and indecent words
  C. On the Department of Commerce web site
  D. The official list is in public domain and found in all amateur study guides

## Slide 65: T3C09 What type of subjects are not prohibited communications while using amateur radio?
  A. Political discussions
  B. Jokes and stories
  C. Religious preferences
  D. All of these answers are correct

## Slide 66: T3C09 What type of subjects are not prohibited communications while using amateur radio?
  A. Political discussions
  B. Jokes and stories
  C. Religious preferences
D. All of these answers are correct

## Slide 67: T3C10 When circumstances are not specifically covered by FCC rules, what general operating standard must be applied to amateur station operation?
  A. Designated operator control
  B. Politically correct control
  C. Good engineering and amateur practices
  D. Reasonable operator control

## Slide 68: T3C10 When circumstances are not specifically covered by FCC rules, what general operating standard must be applied to amateur station operation?
  A. Designated operator control
  B. Politically correct control
C. Good engineering and amateur practices
  D. Reasonable operator control

## Slide 69: Low Pass Filter
A low-pass filter
goes between your
transmitter and
antenna. It removes
harmonic radiation
from your signals.
It will pass the low frequency (HF) ham bands while blocking their harmonics (cutoff frequency 50 MHz). Your neighbors’ TV sets will thank you.

## Slide 70: T3D01 What should you do if you receive a report that your transmissions are causing splatter or interference on nearby frequencies?
  A. Increase transmit power
  B. Change mode of transmission
  C. Report the interference to the equipment manufacturer
  D. Check transmitter for off frequency operation or spurious emissions

## Slide 71: T3D01 What should you do if you receive a report that your transmissions are causing splatter or interference on nearby frequencies?
  A. Increase transmit power
  B. Change mode of transmission
  C. Report the interference to the equipment manufacturer
D. Check transmitter for off frequency operation or spurious emissions

## Slide 72: T3D02 Who is responsible for taking care of the interference if signals from your transmitter are causing front end overload in your neighbor's television receiver?
  A. You alone are responsible, since your transmitter is causing the problem
  B. Both you and the owner of the television receiver share the responsibility
  C. The FCC must decide if you or the owner of the television receiver is responsible
  D. The owner of the television receiver is responsible

## Slide 73: T3D02 Who is responsible for taking care of the interference if signals from your transmitter are causing front end overload in your neighbor's television receiver?
  A. You alone are responsible, since your transmitter is causing the problem
  B. Both you and the owner of the television receiver share the responsibility
  C. The FCC must decide if you or the owner of the television receiver is responsible
D. The owner of the television receiver is responsible

## Slide 74: T3D03 What is the major cause of telephone interference?
  A. The telephone wiring is inadequate
  B. Tropospheric ducting at UHF frequencies
  C. The telephone was not equipped with adequate interference protection when manufactured.
  D. Improper location of the telephone in the home

## Slide 75: Telephone Filter
http://www.ky-filters.com
Notes: From http://www.ky-filters.com/rfchoke.htm

## Slide 76: T3D03 What is the major cause of telephone interference?
  A. The telephone wiring is inadequate
  B. Tropospheric ducting at UHF frequencies
C. The telephone was not equipped with adequate interference protection when manufactured.
  D. Improper location of the telephone in the home

## Slide 77: T3D04 What is the proper course of action if you unintentionally interfere with another station?
  A. Rotate your antenna slightly
  B. Properly identify your station and move to a different frequency
  C. Increase power
  D. Change antenna polarization

## Slide 78: T3D04 What is the proper course of action if you unintentionally interfere with another station?
  A. Rotate your antenna slightly
B. Properly identify your station and move to a different frequency
  C. Increase power
  D. Change antenna polarization

## Slide 79: T3D05 When may you deliberately interfere with another station's communications?
  A. Only if the station is operating illegally
  B. Only if the station begins transmitting on a frequency you are using
  C. Never
  D. You may cause deliberate interference because it can't be helped during crowded band conditions

## Slide 80: T3D05 When may you deliberately interfere with another station's communications?
  A. Only if the station is operating illegally
  B. Only if the station begins transmitting on a frequency you are using
C. Never
  D. You may cause deliberate interference because it can't be helped during crowded band conditions

## Slide 81: T3D06 Who has exclusive use of a specific frequency when the FCC has not declared a communication emergency?
  A. Any net station that has traffic
  B. The station first occupying the frequency
  C. Individuals passing health and welfare communications
  D. No station has exclusive use of any frequency

## Slide 82: T3D06 Who has exclusive use of a specific frequency when the FCC has not declared a communication emergency?
  A. Any net station that has traffic
  B. The station first occupying the frequency
  C. Individuals passing health and welfare communications
D. No station has exclusive use of any frequency

## Slide 83: T3D07 What effect might a break in a cable television transmission line have on amateur communications?
  A. A break cannot affect amateur communications
  B. Harmonic radiation from the TV may cause the amateur transmitter to transmit off-frequency
  C. TV interference may result when the amateur station is transmitting, or interference may occur to the amateur receiver
  D. The broken cable may pick up very high voltages when the amateur station is transmitting

## Slide 84: T3D07 What effect might a break in a cable television transmission line have on amateur communications?
  A. A break cannot affect amateur communications
  B. Harmonic radiation from the TV may cause the amateur transmitter to transmit off-frequency
C. TV interference may result when the amateur station is transmitting, or interference may occur to the amateur receiver
  D. The broken cable may pick up very high voltages when the amateur station is transmitting

## Slide 85: T3D08 What is the best way to reduce on the air interference when testing your transmitter?
  A. Use a short indoor antenna when testing
  B. Use upper side band when testing
  C. Use a dummy load when testing
  D. Use a simplex frequency instead of a repeater frequency

## Slide 86: T3D08 What is the best way to reduce on the air interference when testing your transmitter?
  A. Use a short indoor antenna when testing
  B. Use upper side band when testing
C. Use a dummy load when testing
  D. Use a simplex frequency instead of a repeater frequency

## Slide 87: T3D09 What rules apply to your station when using amateur radio at the request of public service officials or at the scene of an emergency?
  A. RACES
  B. ARES
  C. FCC
  D. FEMA

## Slide 88: T3D09 What rules apply to your station when using amateur radio at the request of public service officials or at the scene of an emergency?
  A. RACES
  B. ARES
C. FCC
  D. FEMA

## Slide 89: T3D10 What do RACES and ARES have in common?
  A. They represent the two largest ham clubs in the United States
  B. One handles road traffic, the other weather traffic
  C. Neither may handle emergency traffic
  D. Both organizations provide communications during emergencies

## Slide 90: T3D10 What do RACES and ARES have in common?
  A. They represent the two largest ham clubs in the United States
  B. One handles road traffic, the other weather traffic
  C. Neither may handle emergency traffic
D. Both organizations provide communications during emergencies

## Slide 91: T3D11 What is meant by receiver front-end overload?
  A. Too much voltage from the power supply
  B. Too much current from the power supply
  C. Interference caused by strong signals from a nearby source
  D. Interference caused by turning the volume up too high

## Slide 92: T3D11 What is meant by receiver front-end overload?
  A. Too much voltage from the power supply
  B. Too much current from the power supply
C. Interference caused by strong signals from a nearby source
  D. Interference caused by turning the volume up too high