## Slide 1: T0 – Electrical and RF Safety 3 exam questions – 3 groups
  T0A AC power circuits, hazardous voltages, fuses and circuit breakers, grounding, lightning protection, battery safety, electrical code compliance
  T0B Antenna installation, tower safety, overhead power lines
  T0C RF hazards, radiation exposure, RF heating hazards, proximity to antennas, recognized safe power levels, hand held safety, exposure to others
Notes: 2006 Technician Class (Element 2) Master syllabus
Released 6 February, 2006
35 Exam questions
http://www.microhams.com
Created by Scott N7SS

## Slide 2: T0A01 What is a commonly accepted value for the lowest voltage that can cause a dangerous electric shock?
  A. 12 volts
  B. 30 volts
  C. 120 volts
  D. 300 volts

## Slide 3: T0A01 What is a commonly accepted value for the lowest voltage that can cause a dangerous electric shock?
  A. 12 volts
B. 30 volts
  C. 120 volts
  D. 300 volts

## Slide 4: T0A02 What is the lowest amount of electrical current flowing through the human body that is likely to cause death?
  A. 10 microamperes
  B. 100 milliamperes
  C. 10 amperes
  D. 100 amperes

## Slide 5: T0A02 What is the lowest amount of electrical current flowing through the human body that is likely to cause death?
  A. 10 microamperes
B. 100 milliamperes
  C. 10 amperes
  D. 100 amperes

## Slide 6: T0A03 What is connected to the green wire in a three-wire electrical plug?
  A. Neutral
  B. Hot
  C. Ground
  D. The white wire

## Slide 7: T0A03 What is connected to the green wire in a three-wire electrical plug?
  A. Neutral
  B. Hot
C. Ground
  D. The white wire

## Slide 8: T0A04 What is the purpose of a fuse in an electrical circuit?
  A. To make sure enough power reaches the circuit
  B. To interrupt power in case of overload
  C. To prevent television interference
  D. To prevent shocks

## Slide 9: T0A04 What is the purpose of a fuse in an electrical circuit?
  A. To make sure enough power reaches the circuit
B. To interrupt power in case of overload
  C. To prevent television interference
  D. To prevent shocks

## Slide 10: T0A05 What might happen if you install a 20-ampere fuse in your transceiver in the place of a 5-ampere fuse?
  A. The larger fuse would better protect your transceiver from using too much current
  B. The transceiver will run cooler
  C. Excessive current could cause a fire
  D. The transceiver would not be able to produce as much RF output

## Slide 11: T0A05 What might happen if you install a 20-ampere fuse in your transceiver in the place of a 5-ampere fuse?
  A. The larger fuse would better protect your transceiver from using too much current
  B. The transceiver will run cooler
C. Excessive current could cause a fire
  D. The transceiver would not be able to produce as much RF output

## Slide 12: T0A06 What is a good way to guard against electrical shock at your station?
  A. Use 3-wire cords and plugs for all AC powered equipment
  B. Connect all AC powered station equipment to a common ground
  C. Use a ground-fault interrupter at each electrical outlet
  D. All of these answers are correct

## Slide 13: T0A06 What is a good way to guard against electrical shock at your station?
  A. Use 3-wire cords and plugs for all AC powered equipment
  B. Connect all AC powered station equipment to a common ground
  C. Use a ground-fault interrupter at each electrical outlet
D. All of these answers are correct

## Slide 14: T0A07 What is the most important thing to consider when installing an emergency disconnect switch at your station?
  A. It must always be as near to the operator as possible
  B. It must always be as far away from the operator as possible
  C. Everyone should know where it is and how to use it
  D. It should be installed in a metal box to prevent tampering

## Slide 15: T0A07 What is the most important thing to consider when installing an emergency disconnect switch at your station?
  A. It must always be as near to the operator as possible
  B. It must always be as far away from the operator as possible
C. Everyone should know where it is and how to use it
  D. It should be installed in a metal box to prevent tampering

## Slide 16: T0A08 What precautions should be taken when a lightning storm is expected?
  A. Disconnect the antenna cables from your station and move them away from your radio equipment
  B. Unplug all power cords from AC outlets
  C. Stop using your radio equipment and move to another room until the storm passes
  D. All of these answers are correct

## Slide 17: T0A08 What precautions should be taken when a lightning storm is expected?
  A. Disconnect the antenna cables from your station and move them away from your radio equipment
  B. Unplug all power cords from AC outlets
  C. Stop using your radio equipment and move to another room until the storm passes
D. All of these answers are correct

## Slide 18: T0A09 What is one way to recharge a 12-volt battery if the commercial power is out?
  A. You cannot recharge a battery unless the power is back on
  B. Add water to the battery
  C. Connect the battery to a car's battery and run the engine
  D. Take your battery to the utility company for a recharge

## Slide 19: T0A09 What is one way to recharge a 12-volt battery if the commercial power is out?
  A. You cannot recharge a battery unless the power is back on
  B. Add water to the battery
C. Connect the battery to a car's battery and run the engine
  D. Take your battery to the utility company for a recharge

## Slide 20: T0A10 What kind of hazard is presented by a conventional 12-volt storage battery?
  A. It contains dangerous acid that can spill and cause injury
  B. Short circuits can damage wiring and possibly cause a fire
  C. Explosive gas can collect if not properly vented
  D. All of these answers are correct

## Slide 21: Battery Explosion
Notes: The facility was formerly a large computer/data center with battery room and emergency generators in Sacramento, CA. The company vacated the building, moved out the computer equipment but left the battery backup system behind.
The ventilation for the battery room appeared to be tied to a hydrogen monitoring system (which is pretty common). The Hydrogen sensor was in alarm upon emergency responders arriving at the scene (post-explosion). 911 callers reporting the explosion also reported hearing an alarm for 3 days prior to the explosion. This appears to have been a local alarm as it was not relayed to the Fire Department. Given how slowly batteries generate hydrogen gas, it appears the batteries were charging for a long period of time with no ventilation - the detector was alarming and hydrogen gas continued to build up until it found an ignition source. The best guess is the ignition occurred at or near a grounding strap on the battery racks but in a room full of batteries and electrical equipment, ignition sources are plentiful...especially when considering the sensitivity of hydrogen.
The lesson to pass on is that ventilation is CRITICAL with lead acid batteries. Great care should be taken to insure ventilation is adequate or even better that the batteries can NOT be charged without the ventilation system properly working.

## Slide 22: T0A10 What kind of hazard is presented by a conventional 12-volt storage battery?
  A. It contains dangerous acid that can spill and cause injury
  B. Short circuits can damage wiring and possibly cause a fire
  C. Explosive gas can collect if not properly vented
D. All of these answers are correct

## Slide 23: T0A11 What can happen if a storage battery is charged or discharged too quickly?
  A. The battery could overheat and give off dangerous gas or explode
  B. The terminal voltage will oscillate rapidly
  C. The warranty will be voided
  D. The voltage will be reversed

## Slide 24: T0A11 What can happen if a storage battery is charged or discharged too quickly?
A. The battery could overheat and give off dangerous gas or explode
  B. The terminal voltage will oscillate rapidly
  C. The warranty will be voided
  D. The voltage will be reversed

## Slide 25: T0A12 What is the most important reason to have a lightning protection system for your amateur radio station?
  A. Lower insurance rates
  B. Improved reception
  C. Fire prevention
  D. Noise reduction

## Slide 26: T0A12 What is the most important reason to have a lightning protection system for your amateur radio station?
  A. Lower insurance rates
  B. Improved reception
C. Fire prevention
  D. Noise reduction

## Slide 27: T0A13 What kind of hazard might exist in a power supply when it is turned off and disconnected?
  A. Static electricity could damage the grounding system
  B. Circulating currents inside the transformer might cause damage
  C. The fuse might blow if you remove the cover
  D. You might receive an electric shock from stored charge in large capacitors

## Slide 28: T0A13 What kind of hazard might exist in a power supply when it is turned off and disconnected?
  A. Static electricity could damage the grounding system
  B. Circulating currents inside the transformer might cause damage
  C. The fuse might blow if you remove the cover
D. You might receive an electric shock from stored charge in large capacitors

## Slide 29: T0B01 Why should you wear a hard hat and safety glasses if you are on the ground helping someone work on an antenna tower?
  A. It is required by FCC rules
  B. To keep RF energy away from your head during antenna testing
  C. To protect your head and eyes in case something accidentally falls from the tower
  D. It is required by the electrical code

## Slide 30: T0B01 Why should you wear a hard hat and safety glasses if you are on the ground helping someone work on an antenna tower?
  A. It is required by FCC rules
  B. To keep RF energy away from your head during antenna testing
C. To protect your head and eyes in case something accidentally falls from the tower
  D. It is required by the electrical code

## Slide 31: T0B02 What is a good precaution to observe before climbing an antenna tower?
  A. Turn on all radio transmitters
  B. Remove all tower grounding connections
  C. Put on your safety belt and safety glasses
  D. Inform the FAA and the FCC that you are working on a tower

## Slide 32: T0B02 What is a good precaution to observe before climbing an antenna tower?
  A. Turn on all radio transmitters
  B. Remove all tower grounding connections
C. Put on your safety belt and safety glasses
  D. Inform the FAA and the FCC that you are working on a tower

## Slide 33: T0B03 What should you do before you climb a tower?
  A. Arrange for a helper or observer
  B. Inspect the tower for damage or loose hardware
  C. Make sure there are no electrical storms nearby
  D. All of these answers are correct

## Slide 34: T0B03 What should you do before you climb a tower?
  A. Arrange for a helper or observer
  B. Inspect the tower for damage or loose hardware
  C. Make sure there are no electrical storms nearby
D. All of these answers are correct

## Slide 35: T0B04 What is an important consideration when putting up an antenna?
  A. Carefully tune it for a low SWR
  B. Make sure people cannot accidentally come into contact with it
  C. Make sure you discard all packing material in a safe place
  D. Make sure birds can see it so they don’t fly into it

## Slide 36: T0B04 What is an important consideration when putting up an antenna?
  A. Carefully tune it for a low SWR
B. Make sure people cannot accidentally come into contact with it
  C. Make sure you discard all packing material in a safe place
  D. Make sure birds can see it so they don’t fly into it

## Slide 37: T0B05 What must be considered when erecting an antenna near an airport?
  A. The maximum allowed height with regard to nearby airports
  B. The possibility of interference to aircraft radios
  C. The radiation angle of the signals it produces
  D. The polarization of signal to be radiated

## Slide 38: T0B05 What must be considered when erecting an antenna near an airport?
A. The maximum allowed height with regard to nearby airports
  B. The possibility of interference to aircraft radios
  C. The radiation angle of the signals it produces
  D. The polarization of signal to be radiated

## Slide 39: T0B06 What is the most important safety precaution to observe when putting up an antenna tower?
  A. Install steps on the tower for safe climbing
  B. Insulate the base of the tower to avoid lightning strikes
  C. Ground the base of the tower to prevent lightning strikes
  D. Look for and stay clear of any overhead electrical wires

## Slide 40: T0B06 What is the most important safety precaution to observe when putting up an antenna tower?
  A. Install steps on the tower for safe climbing
  B. Insulate the base of the tower to avoid lightning strikes
  C. Ground the base of the tower to prevent lightning strikes
D. Look for and stay clear of any overhead electrical wires

## Slide 41: T0B07 How should the guy wires for an antenna tower be installed?
  A. So each guy wire anchor point has an even number of wires
  B. So that no guy wire is more than 25 feet long
  C. Each guy wire must be pulled as tight as possible
  D. In accordance with the tower manufacturer's instructions

## Slide 42: T0B07 How should the guy wires for an antenna tower be installed?
  A. So each guy wire anchor point has an even number of wires
  B. So that no guy wire is more than 25 feet long
  C. Each guy wire must be pulled as tight as possible
D. In accordance with the tower manufacturer's instructions

## Slide 43: T0B08 What is a safe distance from a power line to allow when installing an antenna?
  A. Half the width of your property unless the wires are at least 23 feet high
  B. 12.5 feet in most metropolitan areas
  C. 36 meters plus 1/2 wavelength at the operating frequency
  D. So that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires

## Slide 44: T0B08 What is a safe distance from a power line to allow when installing an antenna?
  A. Half the width of your property unless the wires are at least 23 feet high
  B. 12.5 feet in most metropolitan areas
  C. 36 meters plus 1/2 wavelength at the operating frequency
D. So that if the antenna falls unexpectedly, no part of it can come closer than 10 feet to the power wires

## Slide 45: T0B09 What is the most important safety rule to remember when using a crank-up tower?
  A. This type of tower must never be painted
  B. Crank up towers must be raised and lowered frequently to keep them properly lubricated
  C. Winch cables must be specially rated for use on this type of tower
  D. A crank-up tower should never be climbed unless it is in the fully lowered position

## Slide 46: T0B09 What is the most important safety rule to remember when using a crank-up tower?
  A. This type of tower must never be painted
  B. Crank up towers must be raised and lowered frequently to keep them properly lubricated
  C. Winch cables must be specially rated for use on this type of tower
D. A crank-up tower should never be climbed unless it is in the fully lowered position

## Slide 47: T0B10 Why is stainless steel hardware used on many antennas instead of other metals?
  A. Stainless steel is a better electrical conductor
  B. Stainless steel weighs less than other metals
  C. Stainless steel parts are much less likely to corrode
  D. Stainless steel costs less than other metals

## Slide 48: T0B10 Why is stainless steel hardware used on many antennas instead of other metals?
  A. Stainless steel is a better electrical conductor
  B. Stainless steel weighs less than other metals
C. Stainless steel parts are much less likely to corrode
  D. Stainless steel costs less than other metals

## Slide 49: T0B11 What is considered to be an adequate ground for a tower?
  A. A single 4 foot ground rod, driven into the earth no more than 12 inches from the base
  B. A screen of 120 radial wires
  C. Separate 8 foot long ground rods for each tower leg, bonded to the tower and each other
  D. A connection between the tower base and a cold water pipe

## Slide 50: T0B11 What is considered to be an adequate ground for a tower?
  A. A single 4 foot ground rod, driven into the earth no more than 12 inches from the base
  B. A screen of 120 radial wires
C. Separate 8 foot long ground rods for each tower leg, bonded to the tower and each other
  D. A connection between the tower base and a cold water pipe

## Slide 51: T0C01 What type of radiation are VHF and UHF radio signals?
  A. Gamma radiation
  B. Ionizing radiation
  C. Alpha radiation
  D. Non-ionizing radiation

## Slide 52: T0C01 What type of radiation are VHF and UHF radio signals?
  A. Gamma radiation
  B. Ionizing radiation
  C. Alpha radiation
D. Non-ionizing radiation

## Slide 53: T0C02 When can radio waves cause injury to the human body?
  A. Only when the frequency is below 30 MHz
  B. Only if the combination of signal strength and frequency cause excessive power to be absorbed
  C. Only when the frequency is greater than 30 MHz
  D. Only when transmitter power exceeds 50 watts

## Slide 54: T0C02 When can radio waves cause injury to the human body?
  A. Only when the frequency is below 30 MHz
B. Only if the combination of signal strength and frequency cause excessive power to be absorbed
  C. Only when the frequency is greater than 30 MHz
  D. Only when transmitter power exceeds 50 watts

## Slide 55: T0C03 What is the maximum power level that an amateur radio station may use at frequencies above 30 MHz before an RF exposure evaluation is required?
  A. 1500 watts PEP transmitter output
  B. 1 watt forward power
  C. 50 watts PEP at the antenna
  D. 50 watts PEP reflected power

## Slide 56: T0C03 What is the maximum power level that an amateur radio station may use at frequencies above 30 MHz before an RF exposure evaluation is required?
  A. 1500 watts PEP transmitter output
  B. 1 watt forward power
C. 50 watts PEP at the antenna
  D. 50 watts PEP reflected power

## Slide 57: T0C04 What factors affect the RF exposure of people near an amateur transmitter?
  A. Frequency and power level of the RF field
  B. Distance from the antenna to a person
  C. Radiation pattern of the antenna
  D. All of these answers are correct

## Slide 58: T0C04 What factors affect the RF exposure of people near an amateur transmitter?
  A. Frequency and power level of the RF field
  B. Distance from the antenna to a person
  C. Radiation pattern of the antenna
D. All of these answers are correct

## Slide 59: T0C05 Why must the frequency of an RF source be considered when evaluating RF radiation exposure?
  A. Lower frequency RF fields have more energy than higher frequency fields
  B. Lower frequency RF fields do not penetrate the human body
  C. Higher frequency RF fields are transient in nature and do not affect the human body
  D. The human body absorbs more RF energy at some frequencies than others

## Slide 60: T0C05 Why must the frequency of an RF source be considered when evaluating RF radiation exposure?
  A. Lower frequency RF fields have more energy than higher frequency fields
  B. Lower frequency RF fields do not penetrate the human body
  C. Higher frequency RF fields are transient in nature and do not affect the human body
D. The human body absorbs more RF energy at some frequencies than others

## Slide 61: T0C06 How can you determine that your station complies with FCC RF exposure regulations?
  A. By calculation based on FCC OET Bulletin 65
  B. By calculation based on computer modeling
  C. By measurement of field strength using calibrated equipment
  D. All of these choices are correct

## Slide 62: T0C06 How can you determine that your station complies with FCC RF exposure regulations?
  A. By calculation based on FCC OET Bulletin 65
  B. By calculation based on computer modeling
  C. By measurement of field strength using calibrated equipment
D. All of these choices are correct

## Slide 63: T0C07 What could happen if a person accidentally touched your antenna while you were transmitting?
  A. Touching the antenna could cause television interference
  B. They might receive a painful RF burn injury
  C. They would be able to hear what you are saying
  D. Nothing

## Slide 64: T0C07 What could happen if a person accidentally touched your antenna while you were transmitting?
  A. Touching the antenna could cause television interference
B. They might receive a painful RF burn injury
  C. They would be able to hear what you are saying
  D. Nothing

## Slide 65: T0C08 What action might amateur operators take to prevent exposure to RF radiation in excess of FCC supplied limits?
  A. Alter antenna patterns
  B. Relocate antennas
  C. Change station parameters such as frequency or power
  D. All of these answers are correct

## Slide 66: T0C08 What action might amateur operators take to prevent exposure to RF radiation in excess of FCC supplied limits?
  A. Alter antenna patterns
  B. Relocate antennas
  C. Change station parameters such as frequency or power
D. All of these answers are correct

## Slide 67: T0C09 How can you make sure your station stays in compliance with RF safety regulations?
  A. Compliance is not necessary
  B. By re-evaluating the station whenever an item of equipment is changed
  C. By making sure your antennas have a low SWR
  D. By installing a low pass filter

## Slide 68: T0C09 How can you make sure your station stays in compliance with RF safety regulations?
  A. Compliance is not necessary
B. By re-evaluating the station whenever an item of equipment is changed
  C. By making sure your antennas have a low SWR
  D. By installing a low pass filter

## Slide 69: T0C10 Which of the following units of measurement is used to measure RF radiation exposure?
  A. Milliwatts per square centimeter
  B. Megohms per square meter
  C. Microfarads per foot
  D. Megahertz per second

## Slide 70: T0C10 Which of the following units of measurement is used to measure RF radiation exposure?
A. Milliwatts per square centimeter
  B. Megohms per square meter
  C. Microfarads per foot
  D. Megahertz per second

## Slide 71: T0C11 Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
  A. It takes into account the amount of time the transmitter is operating
  B. It takes into account the transmitter power supply rating
  C. It takes into account the antenna feed line loss
  D. It takes into account the thermal effects of the final amplifier

## Slide 72: T0C11 Why is duty cycle one of the factors used to determine safe RF radiation exposure levels?
A. It takes into account the amount of time the transmitter is operating
  B. It takes into account the transmitter power supply rating
  C. It takes into account the antenna feed line loss
  D. It takes into account the thermal effects of the final amplifier