## Slide 1: G6 -- CIRCUIT COMPONENTS [1 exam question -- 1 group]
  G6A Resistors; capacitors; inductors; rectifiers and transistors; etc.
Notes: ELEMENT 3 - GENERAL CLASS as released by the Question Pool Committee of the National Conference of Volunteer Examiner Coordinators December 1, 2003
The questions contained within this pool must be used in all General class examinations beginning July 1, 2004, and is intended to be used up through June 30, 2007.

## Slide 2: Resistor Ratings
Notes: Here are some wire-wound resistors. They have better power handling capabilities than other types of resistors. All resistors have published tolerances. As their temperature changes, their resistance changes. The amount they change can be anticipated using their Temperature Coefficient (less than or equal to 100 parts per million/degree Celsius above).

## Slide 3: G6A01 If a carbon resistor's temperature is increased, what will happen to the resistance?
  A. It will increase by 20% for every 10 degrees centigrade
  B. It will stay the same
  C. It will change depending on the resistor's temperature coefficient rating
  D. It will become time dependent

## Slide 4: G6A01 If a carbon resistor's temperature is increased, what will happen to the resistance?
  A. It will increase by 20% for every 10 degrees centigrade
  B. It will stay the same
C. It will change depending on the resistor's temperature coefficient rating
  D. It will become time dependent

## Slide 5: Half Wave Rectifier
Notes: The AC voltage on the primary windings of the transformer (Ep) create a magnetic field that is converted to an AC voltage on the secondary windings (Es). Since the diode will only pass current one direction, it cuts off half (180 degrees) of every AC cycle. This method is a very simple way to supply DC power but most electronic devices can’t handle the voltage swings. It is commonly used in car battery chargers.
It would be possible to place a large electrolytic capacitor parallel to the load to eliminate the large voltage swings and smaller disc or tantalum capacitor to smooth the remaining ripple. Suppressor capacitors can also be places across the transformers secondary windings to absorb voltage transients.
When the diode is chosen, it must be able to handle the current required at the load and the Peak Inverse Voltage (PIV) rating must be higher than the peak voltage it will be exposed to in the circuit.

## Slide 6: G6A02 What type of capacitor is often used in power-supply circuits to filter the rectified AC?
  A. Disc ceramic
  B. Vacuum variable
  C. Mica
  D. Electrolytic

## Slide 7: G6A02 What type of capacitor is often used in power-supply circuits to filter the rectified AC?
  A. Disc ceramic
  B. Vacuum variable
  C. Mica
D. Electrolytic

## Slide 8: G6A03 What function does a capacitor serve if it is used in a power-supply circuit to filter transient voltage spikes across the transformer's secondary winding?
  A. Clipper capacitor
  B. Trimmer capacitor
  C. Feedback capacitor
  D. Suppressor capacitor

## Slide 9: G6A03 What function does a capacitor serve if it is used in a power-supply circuit to filter transient voltage spikes across the transformer's secondary winding?
  A. Clipper capacitor
  B. Trimmer capacitor
  C. Feedback capacitor
D. Suppressor capacitor

## Slide 10: G6A04 Where is the source of energy connected in a transformer?
  A. To the secondary winding
  B. To the primary winding
  C. To the core
  D. To the plates

## Slide 11: G6A04 Where is the source of energy connected in a transformer?
  A. To the secondary winding
B. To the primary winding
  C. To the core
  D. To the plates

## Slide 12: G6A05 If no load is attached to the secondary winding of a transformer, what is current in the primary winding called?
  A. Magnetizing current
  B. Direct current
  C. Excitation current
  D. Stabilizing current

## Slide 13: G6A05 If no load is attached to the secondary winding of a transformer, what is current in the primary winding called?
A. Magnetizing current
  B. Direct current
  C. Excitation current
  D. Stabilizing current

## Slide 14: G6A06 What is the peak-inverse-voltage rating of a power-supply rectifier?
  A. The maximum transient voltage the rectifier will handle in the conducting direction
  B. 1.4 times the AC frequency
  C. The maximum voltage the rectifier will handle in the non-conducting direction
  D. 2.8 times the AC frequency

## Slide 15: G6A06 What is the peak-inverse-voltage rating of a power-supply rectifier?
  A. The maximum transient voltage the rectifier will handle in the conducting direction
  B. 1.4 times the AC frequency
C. The maximum voltage the rectifier will handle in the non-conducting direction
  D. 2.8 times the AC frequency

## Slide 16: G6A07 What are the two major ratings that must not be exceeded for silicon-diode rectifiers used in power-supply circuits?
  A. Peak inverse voltage; average forward current
  B. Average power; average voltage
  C. Capacitive reactance; avalanche voltage
  D. Peak load impedance; peak voltage

## Slide 17: G6A07 What are the two major ratings that must not be exceeded for silicon-diode rectifiers used in power-supply circuits?
A. Peak inverse voltage; average forward current
  B. Average power; average voltage
  C. Capacitive reactance; avalanche voltage
  D. Peak load impedance; peak voltage

## Slide 18: G6A08 What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
  A. A series of pulses at twice the frequency of the AC input
  B. A series of pulses at the same frequency as the AC input
  C. A sine wave at half the frequency of the AC input
  D. A steady DC voltage

## Slide 19: G6A08 What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load?
A. A series of pulses at twice the frequency of the AC input
  B. A series of pulses at the same frequency as the AC input
  C. A sine wave at half the frequency of the AC input
  D. A steady DC voltage

## Slide 20: G6A09 A half-wave rectifier conducts during how many degrees of each cycle?
  A. 90 degrees
  B. 180 degrees
  C. 270 degrees
  D. 360 degrees

## Slide 21: G6A09 A half-wave rectifier conducts during how many degrees of each cycle?
  A. 90 degrees
B. 180 degrees
  C. 270 degrees
  D. 360 degrees

## Slide 22: G6A10 A full-wave rectifier conducts during how many degrees of each cycle?
  A. 90 degrees
  B. 180 degrees
  C. 270 degrees
  D. 360 degrees

## Slide 23: G6A10 A full-wave rectifier conducts during how many degrees of each cycle?
  A. 90 degrees
  B. 180 degrees
  C. 270 degrees
D. 360 degrees

## Slide 24: G6A11 When two or more diodes are connected in parallel to increase the current-handling capacity of a power supply, what is the purpose of the resistor connected in series with each diode?
  A. The resistors ensure the thermal stability of the power supply
  B. The resistors regulate the power supply output voltage
  C. The resistors ensure that one diode doesn't take most of the current
  D. The resistors act as swamping resistors in the circuit

## Slide 25: G6A11 When two or more diodes are connected in parallel to increase the current-handling capacity of a power supply, what is the purpose of the resistor connected in series with each diode?
  A. The resistors ensure the thermal stability of the power supply
  B. The resistors regulate the power supply output voltage
C. The resistors ensure that one diode doesn't take most of the current
  D. The resistors act as swamping resistors in the circuit

## Slide 26: G6A12 Why would it not be a good idea to use a wire-wound resistor in a resonant circuit?
  A. The resistor's tolerance value would not be adequate for such a circuit
  B. The resistor's inductance would detune the circuit
  C. The resistor would overheat
  D. The resistor's internal capacitance would detune the circuit

## Slide 27: G6A12 Why would it not be a good idea to use a wire-wound resistor in a resonant circuit?
  A. The resistor's tolerance value would not be adequate for such a circuit
B. The resistor's inductance would detune the circuit
  C. The resistor would overheat
  D. The resistor's internal capacitance would detune the circuit

## Slide 28: G6A13 What is an advantage of ferrite toroidal inductors?
  A. Large values of inductance may be obtained
  B. The inductor may be used in applications where core saturation is desirable
  C. Most of the magnetic field is contained in the core
  D. All of these choices are correct

## Slide 29: G6A13 What is an advantage of ferrite toroidal inductors?
  A. Large values of inductance may be obtained
  B. The inductor may be used in applications where core saturation is desirable
  C. Most of the magnetic field is contained in the core
D. All of these choices are correct

## Slide 30: G6A14 Where would be the stable operating points for a bipolar transistor that is used as a switch in a logic circuit?
  A. In its saturation and cut-off regions
  B. In its active region (between cut-off and saturation regions)
  C. Between its peak and valley current points
  D. Between its enhancement and deletion modes

## Slide 31: G6A14 Where would be the stable operating points for a bipolar transistor that is used as a switch in a logic circuit?
A. In its saturation and cut-off regions
  B. In its active region (between cut-off and saturation regions)
  C. Between its peak and valley current points
  D. Between its enhancement and deletion modes

## Slide 32: G6A15 How should two solenoid inductors be placed so as to minimize their mutual inductance?
  A. In line with their winding axis
  B. With their winding axis parallel to each other
  C. At right angles to their winding axis
  D. Within the same shielded enclosure

## Slide 33: G6A15 How should two solenoid inductors be placed so as to minimize their mutual inductance?
  A. In line with their winding axis
  B. With their winding axis parallel to each other
C. At right angles to their winding axis
  D. Within the same shielded enclosure