## Slide 1: G4 -- AMATEUR RADIO PRACTICES [5 Exam Questions -- 5 Groups]
  G4A Two-tone test; electronic TR switch; amplifier neutralization
  G4B Test equipment: oscilloscope; signal tracer; antenna noise bridge; monitoring oscilloscope; field-strength meters
  G4C Audio rectification in consumer electronics; RF ground
  G4D Speech processors; PEP calculations; wire sizes and fuses
  G4E Common connectors used in amateur stations: types; when to use; fastening methods; precautions when using; HF mobile radio installations; emergency power systems; generators; battery storage devices and charging sources including solar; wind generation
Notes: ELEMENT 3 - GENERAL CLASS as released by the Question Pool Committee of the National Conference of Volunteer Examiner Coordinators December 1, 2003
The questions contained within this pool must be used in all General class examinations beginning July 1, 2004, and is intended to be used up through June 30, 2007.

## Slide 2: Oscilloscope
Notes: This is a current model Tektronix oscilloscope. It has four signal inputs along the lower right edge and can display the waveforms from those inputs. There are three main sections to the right of the screen; vertical, horizontal and trigger. The horizontal and vertical controls adjust how the waveform appears on the screen by adjusting the horizontal and vertical amplifiers. The trigger controls allow the oscilloscope to synchronize to external events.
Newer oscilloscopes are digital and can record data to the floppy seen here on the left or send to other external devices. By connecting the RF output of a transmitter (through appropriate connections) to the vertical input of the scope, the quality of a transmitted signal can be seen on the display.

## Slide 3: Audio Distortion
Notes: Two tone audio tests are used on an oscilloscope to test proper linearity. The pure tones fed in will give you a stable picture on the scope if the amplifier is properly adjusted. The lower image shows a signal with some noise that it also overdriven (overmodulated) and is clipping or flattopping. Any two audio tones may be used, but they must be within the transmitter audio passband, and should not be harmonically related.
Speech Processors are used to keep input audio close to a perfect level for 100% modulation. If they are not adjusted properly, they can cause the distortion seen here. Overdriving causes very distorted audio and no additional power output.

## Slide 4: G4A01 What kind of input signal is used to test the amplitude linearity of a single-sideband phone transmitter while viewing the output on an oscilloscope?
  A. Normal speech
  B. An audio-frequency sine wave
  C. Two audio-frequency sine waves
  D. An audio-frequency square wave

## Slide 5: G4A01 What kind of input signal is used to test the amplitude linearity of a single-sideband phone transmitter while viewing the output on an oscilloscope?
  A. Normal speech
  B. An audio-frequency sine wave
C. Two audio-frequency sine waves
  D. An audio-frequency square wave

## Slide 6: G4A02 When testing the amplitude linearity of a single-sideband transmitter, what kind of audio tones are fed into the microphone input and on what kind of instrument is the transmitter output observed?
  A. Two harmonically related tones are fed in, and the output is observed on an oscilloscope
  B. Two harmonically related tones are fed in, and the output is observed on a distortion analyzer
  C. Two non-harmonically related tones are fed in, and the output is observed on an oscilloscope
  D. Two non-harmonically related tones are fed in, and the output is observed on a distortion analyzer

## Slide 7: G4A02 When testing the amplitude linearity of a single-sideband transmitter, what kind of audio tones are fed into the microphone input and on what kind of instrument is the transmitter output observed?
  A. Two harmonically related tones are fed in, and the output is observed on an oscilloscope
  B. Two harmonically related tones are fed in, and the output is observed on a distortion analyzer
C. Two non-harmonically related tones are fed in, and the output is observed on an oscilloscope
  D. Two non-harmonically related tones are fed in, and the output is observed on a distortion analyzer

## Slide 8: G4A03 What audio frequencies are used in a two-tone test of the linearity of a single-sideband phone transmitter?
  A. 20 Hz and 20 kHz tones must be used
  B. 1200 Hz and 2400 Hz tones must be used
  C. Any two audio tones may be used, but they must be within the transmitter audio passband, and must be harmonically related
  D. Any two audio tones may be used, but they must be within the transmitter audio passband, and should not be harmonically related

## Slide 9: G4A03 What audio frequencies are used in a two-tone test of the linearity of a single-sideband phone transmitter?
  A. 20 Hz and 20 kHz tones must be used
  B. 1200 Hz and 2400 Hz tones must be used
  C. Any two audio tones may be used, but they must be within the transmitter audio passband, and must be harmonically related
D. Any two audio tones may be used, but they must be within the transmitter audio passband, and should not be harmonically related

## Slide 10: TR (Transmit/Receive) Switch
Transmitter
Receiver
TR Switch
Low Pass Filter
Antenna Match
Notes: The TR switch is placed after the transmitter/receiver stages and before the low pass filter to minimize harmonics on transmit and reduce out of band noise on receive. The TR switch in a modern transceiver is often solid state because it allows very fast switching between transmit and receive.

## Slide 11: G4A04 At what point in an HF transceiver block diagram would an electronic TR switch normally appear?
  A. Between the transmitter and low-pass filter
  B. Between the low-pass filter and antenna
  C. At the antenna feed point
  D. At the power supply feed point

## Slide 12: G4A04 At what point in an HF transceiver block diagram would an electronic TR switch normally appear?
A. Between the transmitter and low-pass filter
  B. Between the low-pass filter and antenna
  C. At the antenna feed point
  D. At the power supply feed point

## Slide 13: G4A05 Why is an electronic TR switch preferable to a mechanical one?
  A. It allows greater receiver sensitivity
  B. Its circuitry is simpler
  C. It has a higher operating speed
  D. It allows cleaner output signals

## Slide 14: G4A05 Why is an electronic TR switch preferable to a mechanical one?
  A. It allows greater receiver sensitivity
  B. Its circuitry is simpler
C. It has a higher operating speed
  D. It allows cleaner output signals

## Slide 15: Linear Amplifier
Notes: This is a Tokyo Hy-Power 1.5kW linear amplifier using two 3-500Z tubes. The meter on the left is plate current and the right is grid current. It is necessary to neutralize the tubes in an amplifier to prevent internal (self) oscillation caused by interelectrode capacitance. The best indicator of a neutralized amplifier is a minimum change in grid current as the output circuit is changed. A negative signal is used to cancel the effects of positive feedback.

## Slide 16: G4A06 As a power amplifier is tuned, what reading on its grid-current meter indicates the best neutralization?
  A. A minimum change in grid current as the output circuit is changed
  B. A maximum change in grid current as the output circuit is changed
  C. Minimum grid current
  D. Maximum grid current

## Slide 17: G4A06 As a power amplifier is tuned, what reading on its grid-current meter indicates the best neutralization?
A. A minimum change in grid current as the output circuit is changed
  B. A maximum change in grid current as the output circuit is changed
  C. Minimum grid current
  D. Maximum grid current

## Slide 18: G4A07 Why is neutralization necessary for some vacuum-tube amplifiers?
  A. To reduce the limits of loaded Q
  B. To reduce grid-to-cathode leakage
  C. To cancel AC hum from the filament transformer
  D. To cancel oscillation caused by the effects of interelectrode capacitance

## Slide 19: G4A07 Why is neutralization necessary for some vacuum-tube amplifiers?
  A. To reduce the limits of loaded Q
  B. To reduce grid-to-cathode leakage
  C. To cancel AC hum from the filament transformer
D. To cancel oscillation caused by the effects of interelectrode capacitance

## Slide 20: G4A08 In a properly neutralized RF amplifier, what type of feedback is used?
  A. 5%
  B. 10%
  C. Negative
  D. Positive

## Slide 21: G4A08 In a properly neutralized RF amplifier, what type of feedback is used?
  A. 5%
  B. 10%
C. Negative
  D. Positive

## Slide 22: G4A09 What does a neutralizing circuit do in an RF amplifier?
  A. It controls differential gain
  B. It cancels the effects of positive feedback
  C. It eliminates AC hum from the power supply
  D. It reduces incidental grid modulation

## Slide 23: G4A09 What does a neutralizing circuit do in an RF amplifier?
  A. It controls differential gain
B. It cancels the effects of positive feedback
  C. It eliminates AC hum from the power supply
  D. It reduces incidental grid modulation

## Slide 24: G4A10 What is the reason for neutralizing the final amplifier stage of a transmitter?
  A. To limit the modulation index
  B. To eliminate self oscillations
  C. To cut off the final amplifier during standby periods
  D. To keep the carrier on frequency

## Slide 25: G4A10 What is the reason for neutralizing the final amplifier stage of a transmitter?
  A. To limit the modulation index
B. To eliminate self oscillations
  C. To cut off the final amplifier during standby periods
  D. To keep the carrier on frequency

## Slide 26: G4A11 What type of transmitter performance does a two-tone test analyze?
  A. Linearity
  B. Carrier and undesired sideband suppression
  C. Percentage of frequency modulation
  D. Percentage of carrier phase shift

## Slide 27: G4A11 What type of transmitter performance does a two-tone test analyze?
A. Linearity
  B. Carrier and undesired sideband suppression
  C. Percentage of frequency modulation
  D. Percentage of carrier phase shift

## Slide 28: G4A12 What type of signals are used to conduct a two-tone test?
  A. Two audio signals of the same frequency, but shifted 90-degrees and are within the transmitter's modulation bandpass
  B. Two non-harmonically related audio signals that are within the modulation bandpass of a transmitter
  C. Any two audio frequency signals as long as they are within the transmitter's modulation bandpass
  D. Two audio frequency range square wave signals of equal amplitude that are within the transmitter's modulation bandpass

## Slide 29: G4A12 What type of signals are used to conduct a two-tone test?
  A. Two audio signals of the same frequency, but shifted 90-degrees and are within the transmitter's modulation bandpass
B. Two non-harmonically related audio signals that are within the modulation bandpass of a transmitter
  C. Any two audio frequency signals as long as they are within the transmitter's modulation bandpass
  D. Two audio frequency range square wave signals of equal amplitude that are within the transmitter's modulation bandpass

## Slide 30: G4A13 In what way is a diode like a switch?
  A. It permits current flow at bias voltages less than its zener voltage and blocks current at bias voltages greater than its zener voltage
  B. It permits current flow when reverse biased and blocks current when forward biased
  C. The voltage drop across it increases as forward bias increases and decreases as reverse bias decreases
  D. It permits current flow when forward biased and blocks current when reverse biased

## Slide 31: G4A13 In what way is a diode like a switch?
  A. It permits current flow at bias voltages less than its zener voltage and blocks current at bias voltages greater than its zener voltage
  B. It permits current flow when reverse biased and blocks current when forward biased
  C. The voltage drop across it increases as forward bias increases and decreases as reverse bias decreases
D. It permits current flow when forward biased and blocks current when reverse biased

## Slide 32: G4B01 What item of test equipment contains horizontal- and vertical-channel amplifiers?
  A. An ohmmeter
  B. A signal generator
  C. An ammeter
  D. An oscilloscope

## Slide 33: G4B01 What item of test equipment contains horizontal- and vertical-channel amplifiers?
  A. An ohmmeter
  B. A signal generator
  C. An ammeter
D. An oscilloscope

## Slide 34: G4B02 What is a digital oscilloscope?
  A. An oscilloscope used only for signal tracing in digital circuits
  B. An oscilloscope used only for troubleshooting computers
  C. An oscilloscope used only for troubleshooting switching power supply circuits
  D. An oscilloscope designed around digital technology rather than analog technology

## Slide 35: G4B02 What is a digital oscilloscope?
  A. An oscilloscope used only for signal tracing in digital circuits
  B. An oscilloscope used only for troubleshooting computers
  C. An oscilloscope used only for troubleshooting switching power supply circuits
D. An oscilloscope designed around digital technology rather than analog technology

## Slide 36: G4B03 How would a signal tracer normally be used?
  A. To identify the source of radio transmissions
  B. To make exact drawings of signal waveforms
  C. To show standing wave patterns on open-wire feed-lines
  D. To identify an inoperative stage in a receiver

## Slide 37: G4B03 How would a signal tracer normally be used?
  A. To identify the source of radio transmissions
  B. To make exact drawings of signal waveforms
  C. To show standing wave patterns on open-wire feed-lines
D. To identify an inoperative stage in a receiver

## Slide 38: G4B04 How is a noise bridge normally used?
  A. It is connected at an antenna's feed point and reads the antenna's noise figure
  B. It is connected between a transmitter and an antenna and is tuned for minimum SWR
  C. It is connected between a receiver and an antenna of unknown impedance and is tuned for minimum noise
  D. It is connected between an antenna and ground and is tuned for minimum SWR

## Slide 39: G4B04 How is a noise bridge normally used?
  A. It is connected at an antenna's feed point and reads the antenna's noise figure
  B. It is connected between a transmitter and an antenna and is tuned for minimum SWR
C. It is connected between a receiver and an antenna of unknown impedance and is tuned for minimum noise
  D. It is connected between an antenna and ground and is tuned for minimum SWR

## Slide 40: G4B05 What is the best instrument to use to check the signal quality of a CW or single-sideband phone transmitter?
  A. A monitoring oscilloscope
  B. A field-strength meter
  C. A sidetone monitor
  D. A signal tracer and an audio amplifier

## Slide 41: G4B05 What is the best instrument to use to check the signal quality of a CW or single-sideband phone transmitter?
A. A monitoring oscilloscope
  B. A field-strength meter
  C. A sidetone monitor
  D. A signal tracer and an audio amplifier

## Slide 42: G4B06 What signal source is connected to the vertical input of a monitoring oscilloscope when checking the quality of a transmitted signal?
  A. The IF output of a monitoring receiver
  B. The audio input of the transmitter
  C. The RF signals of a nearby receiving antenna
  D. The RF output of the transmitter

## Slide 43: G4B06 What signal source is connected to the vertical input of a monitoring oscilloscope when checking the quality of a transmitted signal?
  A. The IF output of a monitoring receiver
  B. The audio input of the transmitter
  C. The RF signals of a nearby receiving antenna
D. The RF output of the transmitter

## Slide 44: Field Strength Meter
Notes: Here are two digital Field Strength Meter models. Some SWR meters and frequency counters can also be used as field strength meters. Field Strength Meters are used to test the density of an RF field. This allows testing of antenna patterns and ambient RF levels at repeater and home sites to insure safe levels.

## Slide 45: G4B07 What is the purpose of a field-strength meter?
  A. To determine the standing-wave ratio on a transmission line
  B. To check the output modulation of a transmitter
  C. To monitor relative RF output
  D. To increase average transmitter output

## Slide 46: G4B07 What is the purpose of a field-strength meter?
  A. To determine the standing-wave ratio on a transmission line
  B. To check the output modulation of a transmitter
C. To monitor relative RF output
  D. To increase average transmitter output

## Slide 47: G4B08 What simple instrument may be used to monitor relative RF output during antenna and transmitter adjustments?
  A. A field-strength meter
  B. An antenna noise bridge
  C. A multimeter
  D. A metronome

## Slide 48: G4B08 What simple instrument may be used to monitor relative RF output during antenna and transmitter adjustments?
A. A field-strength meter
  B. An antenna noise bridge
  C. A multimeter
  D. A metronome

## Slide 49: Decibel Multipliers
Notes: The Decibel scale is logarithmic. 3dB represents a 2-fold increase in power, 6dB is 4 fold, 10dB is 10-fold, 20dB is 100-fold. The S-Unit scale on a receiver meter is not an absolute scale and can vary from radio to radio. Although these meters are not calibrated, they can be useful for verifying antenna performance. One “S-Unit” represents a 4-fold change in power or 6dB.

## Slide 50: G4B09 In order to raise the S-meter reading on a receiver from S8 to S9, how much must the power output of a transmitter be increased?
  A. Approximately 2 times
  B. Approximately 3 times
  C. Approximately 4 times
  D. Approximately 5 times

## Slide 51: G4B09 In order to raise the S-meter reading on a receiver from S8 to S9, how much must the power output of a transmitter be increased?
  A. Approximately 2 times
  B. Approximately 3 times
C. Approximately 4 times
  D. Approximately 5 times

## Slide 52: G4B10 What type of information does a field strength meter provide?
  A. The gain in dBi of an antenna
  B. The field pattern of an antenna
  C. The presence and amount of phase distortion of a transmitter
  D. The presence and amount of amplitude distortion of a transmitter

## Slide 53: G4B10 What type of information does a field strength meter provide?
  A. The gain in dBi of an antenna
B. The field pattern of an antenna
  C. The presence and amount of phase distortion of a transmitter
  D. The presence and amount of amplitude distortion of a transmitter

## Slide 54: G4B11 For which of the following applications might you use a field strength meter?
  A. Close-in RDF work
  B. A modulation monitor for a frequency or phase modulation transmitter
  C. An overmodulation indicator for a SSB transmitter
  D. A keying indicator for a RTTY or packet transmitter

## Slide 55: G4B11 For which of the following applications might you use a field strength meter?
A. Close-in RDF work
  B. A modulation monitor for a frequency or phase modulation transmitter
  C. An overmodulation indicator for a SSB transmitter
  D. A keying indicator for a RTTY or packet transmitter

## Slide 56: G4B12 What is one way a noise bridge might be used?
  A. Determining an antenna's gain in dBi
  B. Pre-tuning an antenna tuner
  C. Determining the directivity of an antenna
  D. Determining the line loss of the antenna system

## Slide 57: G4B12 What is one way a noise bridge might be used?
  A. Determining an antenna's gain in dBi
B. Pre-tuning an antenna tuner
  C. Determining the directivity of an antenna
  D. Determining the line loss of the antenna system

## Slide 58: G4B13 What information could a noise bridge directly provide about an unknown length and type of transmission line?
  A. Its characteristic impedance
  B. Its velocity factor
  C. Its loss in dB per 100-feet
  D. Its reflection coefficient

## Slide 59: G4B13 What information could a noise bridge directly provide about an unknown length and type of transmission line?
A. Its characteristic impedance
  B. Its velocity factor
  C. Its loss in dB per 100-feet
  D. Its reflection coefficient

## Slide 60: G4B14 How would you connect an oscilloscope to an AM or SSB transmitter to check transmitter modulation using double trapezoidal patterns?
  A. Couple the detected RF output signal to the vertical plates; set the internal sweep to twice the modulating frequency
  B. Couple the RF output signal to the vertical plates and external trigger; set the internal sweep to twice the modulating frequency
  C. Couple the RF output signal to the vertical plates; apply the unmodulated RF drive signal to the horizontal plates
  D. Couple the detected RF output signal to the vertical plates; apply a constant DC signal to the horizontal plates

## Slide 61: G4B14 How would you connect an oscilloscope to an AM or SSB transmitter to check transmitter modulation using double trapezoidal patterns?
  A. Couple the detected RF output signal to the vertical plates; set the internal sweep to twice the modulating frequency
B. Couple the RF output signal to the vertical plates and external trigger; set the internal sweep to twice the modulating frequency
  C. Couple the RF output signal to the vertical plates; apply the unmodulated RF drive signal to the horizontal plates
  D. Couple the detected RF output signal to the vertical plates; apply a constant DC signal to the horizontal plates

## Slide 62: G4C01 What devices would you install in home-entertainment systems to reduce or eliminate audio-frequency interference?
  A. Bypass inductors
  B. Bypass capacitors
  C. Metal-oxide varistors
  D. Bypass resistors

## Slide 63: G4C01 What devices would you install in home-entertainment systems to reduce or eliminate audio-frequency interference?
  A. Bypass inductors
B. Bypass capacitors
  C. Metal-oxide varistors
  D. Bypass resistors

## Slide 64: Telephone Line Filter
Notes: Occasionally, the RF transmitted from a station will be picked up in the telephone lines and will be audible on the phone. This is very common near AM broadcast stations. The telephone line filter shown here can be used to eliminate RF being picked up in the telephone line by simply plugging it in line with the phone (there’s a jack on the end of the boxy part). Some phones (poorly designed ones) will actually pick up the RF inside the phone. There is no effective solution for these phones, short of replacement.
It is also possible for RF to be picked up by PA or stereo systems. Sideband voice signals will often sound very distorted and CW can cause a buzzing or clicking. A solid ground on the transmitter and the PA or stereo system can often correct this.

## Slide 65: G4C02 What should be done if a properly operating amateur station is the cause of interference to a nearby telephone?
  A. Make internal adjustments to the telephone equipment
  B. Install RFI filters at the affected telephone
  C. Stop transmitting whenever the telephone is in use
  D. Ground and shield the local telephone distribution amplifier

## Slide 66: G4C02 What should be done if a properly operating amateur station is the cause of interference to a nearby telephone?
  A. Make internal adjustments to the telephone equipment
B. Install RFI filters at the affected telephone
  C. Stop transmitting whenever the telephone is in use
  D. Ground and shield the local telephone distribution amplifier

## Slide 67: G4C03 What sound is heard from a public-address system if audio rectification of a nearby single-sideband phone transmission occurs?
  A. A steady hum whenever the transmitter's carrier is on the air
  B. On-and-off humming or clicking
  C. Distorted speech from the transmitter's signals
  D. Clearly audible speech from the transmitter's signals

## Slide 68: G4C03 What sound is heard from a public-address system if audio rectification of a nearby single-sideband phone transmission occurs?
  A. A steady hum whenever the transmitter's carrier is on the air
  B. On-and-off humming or clicking
C. Distorted speech from the transmitter's signals
  D. Clearly audible speech from the transmitter's signals

## Slide 69: G4C04 What sound is heard from a public-address system if audio rectification of a nearby CW transmission occurs?
  A. On-and-off humming or clicking
  B. Audible, possibly distorted speech
  C. Muffled, severely distorted speech
  D. A steady whistling

## Slide 70: G4C04 What sound is heard from a public-address system if audio rectification of a nearby CW transmission occurs?
A. On-and-off humming or clicking
  B. Audible, possibly distorted speech
  C. Muffled, severely distorted speech
  D. A steady whistling

## Slide 71: Station Grounding
Notes: For a proper RF ground, it’s important to use a heavy gauge copper (not aluminum) braid or foil and keep the run length to a minimum. Standard wire, even heavy gauge, or long runs can cause your ground lead to act as an antenna and resonate. A good ground will reduce RFI to other equipment, minimize the risk of shock and reduce electrical interference. At a minimum a ground rod should be 8 feet long. This can be difficult to achieve in some locations and multiple shorter rods tied together can be used.

## Slide 72: G4C05 If your third-floor amateur station has a ground wire running 33 feet down to a ground rod, why might you get an RF burn if you touch the front panel of your HF transceiver?
  A. Because the ground rod is not making good contact with moist earth
  B. Because the transceiver's heat-sensing circuit is not working to start the cooling fan
  C. Because of a bad antenna connection, allowing the RF energy to take an easier path out of the transceiver through you
  D. Because the ground wire is a resonant length on several HF bands and acts more like an antenna than an RF ground connection

## Slide 73: G4C05 If your third-floor amateur station has a ground wire running 33 feet down to a ground rod, why might you get an RF burn if you touch the front panel of your HF transceiver?
  A. Because the ground rod is not making good contact with moist earth
  B. Because the transceiver's heat-sensing circuit is not working to start the cooling fan
  C. Because of a bad antenna connection, allowing the RF energy to take an easier path out of the transceiver through you
D. Because the ground wire is a resonant length on several HF bands and acts more like an antenna than an RF ground connection

## Slide 74: G4C06 Which of the following is NOT an important reason to have a good station ground?
  A. To reduce the cost of operating a station
  B. To reduce electrical noise
  C. To reduce interference
  D. To reduce the possibility of electric shock

## Slide 75: G4C06 Which of the following is NOT an important reason to have a good station ground?
A. To reduce the cost of operating a station
  B. To reduce electrical noise
  C. To reduce interference
  D. To reduce the possibility of electric shock

## Slide 76: G4C07 What is one good way to avoid stray RF energy in your amateur station?
  A. Keep the station's ground wire as short as possible
  B. Use a beryllium ground wire for best conductivity
  C. Drive the ground rod at least 14 feet into the ground
  D. Make a couple of loops in the ground wire where it connects to your station

## Slide 77: G4C07 What is one good way to avoid stray RF energy in your amateur station?
A. Keep the station's ground wire as short as possible
  B. Use a beryllium ground wire for best conductivity
  C. Drive the ground rod at least 14 feet into the ground
  D. Make a couple of loops in the ground wire where it connects to your station

## Slide 78: G4C08 Which of the following statements about station grounding is NOT true?
  A. Braid from RG-213 coaxial cable makes a good conductor to tie station equipment together into a station ground
  B. Only transceivers and power amplifiers need to be tied into a station ground
  C. According to the National Electrical Code, there should be only one grounding system in a building
  D. The minimum length for a good ground rod is 8 feet

## Slide 79: G4C08 Which of the following statements about station grounding is NOT true?
  A. Braid from RG-213 coaxial cable makes a good conductor to tie station equipment together into a station ground
B. Only transceivers and power amplifiers need to be tied into a station ground
  C. According to the National Electrical Code, there should be only one grounding system in a building
  D. The minimum length for a good ground rod is 8 feet

## Slide 80: G4C09 Which of the following statements about station grounding is true?
  A. The chassis of each piece of station equipment should be tied together with high-impedance conductors
  B. If the chassis of all station equipment is connected with a good conductor, there is no need to tie them to an earth ground
  C. RF hot spots can occur in a station located above the ground floor if the equipment is grounded by a long ground wire
  D. A ground loop is an effective way to ground station equipment

## Slide 81: G4C09 Which of the following statements about station grounding is true?
  A. The chassis of each piece of station equipment should be tied together with high-impedance conductors
  B. If the chassis of all station equipment is connected with a good conductor, there is no need to tie them to an earth ground
C. RF hot spots can occur in a station located above the ground floor if the equipment is grounded by a long ground wire
  D. A ground loop is an effective way to ground station equipment

## Slide 82: G4C10 Which of the following is NOT covered in the National Electrical Code?
  A. Minimum conductor sizes for different lengths of amateur antennas
  B. The size and composition of grounding conductors
  C. Electrical safety inside the ham shack
  D. The RF exposure limits of the human body

## Slide 83: G4C10 Which of the following is NOT covered in the National Electrical Code?
  A. Minimum conductor sizes for different lengths of amateur antennas
  B. The size and composition of grounding conductors
  C. Electrical safety inside the ham shack
D. The RF exposure limits of the human body

## Slide 84: G4C11 What can cause the unintended rectification of an RF signal?
  A. Induced currents in conductors that are in poor electrical contact
  B. Induced voltages in conductors that are in good electrical contact
  C. Capacitive coupling of the RF signal to ground
  D. Excessive standing wave ratio (SWR) of the transmission line system

## Slide 85: G4C11 What can cause the unintended rectification of an RF signal?
A. Induced currents in conductors that are in poor electrical contact
  B. Induced voltages in conductors that are in good electrical contact
  C. Capacitive coupling of the RF signal to ground
  D. Excessive standing wave ratio (SWR) of the transmission line system

## Slide 86: G4C12 What is one cause of severe, broadband radio frequency noise at an amateur radio station?
  A. Not using a balun or line isolator to feed balanced antennas
  B. Lack of rectification of the transmitter's signal in power conductors
  C. An intermittent RF ground
  D. The use of horizontal, rather than vertical antennas

## Slide 87: G4C12 What is one cause of severe, broadband radio frequency noise at an amateur radio station?
  A. Not using a balun or line isolator to feed balanced antennas
  B. Lack of rectification of the transmitter's signal in power conductors
C. An intermittent RF ground
  D. The use of horizontal, rather than vertical antennas

## Slide 88: G4C13 How can a ground loop be avoided?
  A. Series connect ("daisy chain") all ground conductors
  B. Connect the AC neutral conductor to the ground wire
  C. Avoid using lockwashers and star washers in making ground connections
  D. Connect all ground conductors to a single point

## Slide 89: G4C13 How can a ground loop be avoided?
  A. Series connect ("daisy chain") all ground conductors
  B. Connect the AC neutral conductor to the ground wire
  C. Avoid using lockwashers and star washers in making ground connections
D. Connect all ground conductors to a single point

## Slide 90: G4D01 What is the reason for using a properly adjusted speech processor with a single-sideband phone transmitter?
  A. It reduces average transmitter power requirements
  B. It reduces unwanted noise pickup from the microphone
  C. It improves voice-frequency fidelity
  D. It improves signal intelligibility at the receiver

## Slide 91: G4D01 What is the reason for using a properly adjusted speech processor with a single-sideband phone transmitter?
  A. It reduces average transmitter power requirements
  B. It reduces unwanted noise pickup from the microphone
  C. It improves voice-frequency fidelity
D. It improves signal intelligibility at the receiver

## Slide 92: G4D02 If a single-sideband phone transmitter is 100% modulated, what will a speech processor do to the transmitter's power?
  A. It will increase the output PEP
  B. It will add nothing to the output PEP
  C. It will decrease the peak power output
  D. It will decrease the average power output

## Slide 93: G4D02 If a single-sideband phone transmitter is 100% modulated, what will a speech processor do to the transmitter's power?
  A. It will increase the output PEP
B. It will add nothing to the output PEP
  C. It will decrease the peak power output
  D. It will decrease the average power output

## Slide 94: RMS, Peak and Peak to Peak Voltages
Notes: There are three key voltage measurements, RMS (Vrms), Peak (Vpk) and Peak to Peak (Vpp). The Peak voltage is relative to ground. RMS or Root Mean Square is more of an “average” voltage over the duration of the AC cycle. RMS voltage is calculated by multiplying 0.707 times the peak voltage. The Peak to Peak voltage measures from the peak of the positive swing to the peak of the negative swing.
The 120 volt AC line voltage in the wall is a peak value. That means the RMS voltage is 85 volts and Peak to Peak is 240 volts.

## Slide 95: G4D03 What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
  A. 100 watts
  B. 200 watts
  C. 400 watts
  D. 1000 watts

## Slide 96: G4D03 What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
A. 100 watts
  B. 200 watts
  C. 400 watts
  D. 1000 watts

## Slide 97: G4D04 What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
  A. 500 watts
  B. 625 watts
  C. 1250 watts
  D. 2500 watts

## Slide 98: G4D04 What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50-ohm resistor connected to the transmitter output?
  A. 500 watts
B. 625 watts
  C. 1250 watts
  D. 2500 watts

## Slide 99: G4D05 What is the output PEP of an unmodulated carrier transmitter if an average-reading wattmeter connected to the transmitter output indicates 1060 watts?
  A. 530 watts
  B. 1060 watts
  C. 1500 watts
  D. 2120 watts

## Slide 100: G4D05 What is the output PEP of an unmodulated carrier transmitter if an average-reading wattmeter connected to the transmitter output indicates 1060 watts?
  A. 530 watts
B. 1060 watts
  C. 1500 watts
  D. 2120 watts

## Slide 101: 240 Volt House Power
Notes: Homes in the US are generally supplied with 240 volts. This is split into two 120 volt halves to supply outlets and lights throughout the house. There are two places that are commonly wired with 240: a dryer and range. This is a range plug. Some larger appliances such as air compressors and large amplifiers also require 240 volts to allow for the use of smaller wire to support their current draw.
Note the Red, Black, White and bare wire. Red and Black are the two “hot leads”. The white is “common” or “neutral” and the bare wire is the ground. Hot leads must always be fuse or breaker protected.

## Slide 102: G4D06 Which wires in a four-conductor line cord should be attached to fuses in a 240-VAC primary (single phase) power supply?
  A. Only the "hot" (black and red) wires
  B. Only the "neutral" (white) wire
  C. Only the ground (bare) wire
  D. All wires

## Slide 103: G4D06 Which wires in a four-conductor line cord should be attached to fuses in a 240-VAC primary (single phase) power supply?
A. Only the "hot" (black and red) wires
  B. Only the "neutral" (white) wire
  C. Only the ground (bare) wire
  D. All wires

## Slide 104: AWG Wire Gauges vs. Current Capacity
Continuous-Duty
Current Capacity (Amps)
AWG Single Bundled
Gauge Wire Wire
8 73 46
10 55 33
12 41 23
14 32 17
16 22 13
18 16 10
Notes: This shows various wire sizes and their maximum current capacity. Single conductor wire has a higher capacity the multiconductor bundled wire because it has less ability to heat up (melt through) its jacket. The important point here is the two common wire sizes in household wiring are 12 and 14 gauge. They receive 20 amp and 15 amp fuses or circuit breakers respectively. The table above shows their maximum capacity in a multiconductor cable is just over this amount – not enough headroom to support the next larger fuse or breaker.

## Slide 105: G4D07 What size wire is normally used on a 20-ampere, 120-VAC household appliance circuit?
  A. AWG number 20
  B. AWG number 16
  C. AWG number 14
  D. AWG number 12

## Slide 106: G4D07 What size wire is normally used on a 20-ampere, 120-VAC household appliance circuit?
  A. AWG number 20
  B. AWG number 16
  C. AWG number 14
D. AWG number 12

## Slide 107: G4D08 What maximum size fuse or circuit breaker should be used in a household appliance circuit using AWG number 12 wiring?
  A. 100 amperes
  B. 60 amperes
  C. 30 amperes
  D. 20 amperes

## Slide 108: G4D08 What maximum size fuse or circuit breaker should be used in a household appliance circuit using AWG number 12 wiring?
  A. 100 amperes
  B. 60 amperes
  C. 30 amperes
D. 20 amperes

## Slide 109: G4D09 What operating benefit does properly adjusted speech clipping provide?
  A. It removes any distortion in the audio waveform
  B. Deep clipping restores the natural sound of the audio
  C. It prevents overdriving the transmitter's modulator stage
  D. It removes any AC hum and noise that might be in the audio

## Slide 110: G4D09 What operating benefit does properly adjusted speech clipping provide?
  A. It removes any distortion in the audio waveform
  B. Deep clipping restores the natural sound of the audio
C. It prevents overdriving the transmitter's modulator stage
  D. It removes any AC hum and noise that might be in the audio

## Slide 111: G4D10 What would be the voltage across a 50-ohm dummy load dissipating 1200 watts?
  A. 173 volts
  B. 245 volts
  C. 346 volts
  D. 692 volts

## Slide 112: G4D10 What would be the voltage across a 50-ohm dummy load dissipating 1200 watts?
  A. 173 volts
B. 245 volts
  C. 346 volts
  D. 692 volts

## Slide 113: Typical Ham RF Connectors
From Left to Right:
N male, N female, PL-259, BNC male, SMA male, SMA female (on HT), BNC female (on lower radio), SO-238 (on upper radio)
Notes: Note the PL-259 is a Plug and is therefore male. The SO-238 is the corresponding chassis mount Socket. The PL-259 is by far the most common connector in amateur use. It’s simple to install and cheap. Unfortunately, its impedance isn’t stable – especially at high frequencies. For lower power work, BNCs and SMAs are more common because of their compact size.
N connectors are used by hams at higher (UHF) frequencies because they handle high power levels and match coax perfectly into the GHz range. N Connectors are also used by the military because they are gasketed making them water and dust-proof.

## Slide 114: G4E01 Which of the following connectors is NOT designed for RF transmission lines?
  A. PL-259
  B. DB-25
  C. Type N
  D. BNC

## Slide 115: G4E01 Which of the following connectors is NOT designed for RF transmission lines?
  A. PL-259
B. DB-25
  C. Type N
  D. BNC

## Slide 116: G4E02 When installing a power plug on a line cord, which of the following should you do?
  A. Twist the wire strands neatly and fasten them so they don't cause a short circuit
  B. Observe the correct wire color conventions for plug terminals
  C. Use proper grounding techniques
  D. All of these choices

## Slide 117: G4E02 When installing a power plug on a line cord, which of the following should you do?
  A. Twist the wire strands neatly and fasten them so they don't cause a short circuit
  B. Observe the correct wire color conventions for plug terminals
  C. Use proper grounding techniques
D. All of these choices

## Slide 118: Mobile Radio Installation
Notes: This is an ideal mobile installation. The power is wired directly to the battery via a fuse on each power lead. There is a relay that turns the radio off when the ignition is turned off and the antenna is mounted on the roof for best performance and shielding for the occupants.
Using large wires directly to the battery insures there is sufficient power available with minimal voltage drop and noise. Where a 50 watt VHF transceiver may draw up to 10 amps, an HF transceiver can draw over 20 amps. Most auto wiring is not designed for this load, particularly cigarette lighters.

## Slide 119: G4E03 Which of the following power connections would be the best for a 100-watt HF mobile installation?
  A. A direct, fused connection to the battery using heavy gauge wire
  B. A connection to the fuse-protected accessory terminal strip or distribution panel
  C. A connection to the cigarette lighter
  D. A direct connection to the alternator or generator

## Slide 120: G4E03 Which of the following power connections would be the best for a 100-watt HF mobile installation?
A. A direct, fused connection to the battery using heavy gauge wire
  B. A connection to the fuse-protected accessory terminal strip or distribution panel
  C. A connection to the cigarette lighter
  D. A direct connection to the alternator or generator

## Slide 121: G4E04 Why is it best NOT to draw the DC power for a 100-watt HF transceiver from an automobile's cigarette lighter socket?
  A. The socket is not wired with an RF-shielded power cable
  B. The socket's wiring may not be adequate for the current being drawn by the transceiver
  C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
  D. The power from the socket is never adequately filtered for HF transceiver operation

## Slide 122: G4E04 Why is it best NOT to draw the DC power for a 100-watt HF transceiver from an automobile's cigarette lighter socket?
  A. The socket is not wired with an RF-shielded power cable
B. The socket's wiring may not be adequate for the current being drawn by the transceiver
  C. The DC polarity of the socket is reversed from the polarity of modern HF transceivers
  D. The power from the socket is never adequately filtered for HF transceiver operation

## Slide 123: G4E05 Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band?
  A. The vehicle's electrical system wiring
  B. The wire gauge of the DC power line to the transceiver
  C. The HF mobile antenna system
  D. The rating of the vehicle's alternator or generator

## Slide 124: G4E05 Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band?
  A. The vehicle's electrical system wiring
  B. The wire gauge of the DC power line to the transceiver
C. The HF mobile antenna system
  D. The rating of the vehicle's alternator or generator

## Slide 125: G4E06 Which of the following is true of both a permanent or temporary emergency generator installation?
  A. The generator should be located in a well ventilated area
  B. The installation should be grounded
  C. Extra fuel supplies, especially gasoline, should not be stored in an inhabited area
  D. All of these choices

## Slide 126: G4E06 Which of the following is true of both a permanent or temporary emergency generator installation?
  A. The generator should be located in a well ventilated area
  B. The installation should be grounded
  C. Extra fuel supplies, especially gasoline, should not be stored in an inhabited area
D. All of these choices

## Slide 127: G4E07 Which of the following is true of a lead-acid storage battery as it is being charged?
  A. It tends to cool off
  B. It gives off explosive oxygen gas
  C. It gives off explosive hydrogen gas
  D. It takes in oxygen from the surrounding air

## Slide 128: Battery Explosion
Notes: The facility was formerly a large computer/data center with battery room and emergency generators in Sacramento, CA. The company vacated the building, moved out the computer equipment but left the battery backup system behind.
The ventilation for the battery room appeared to be tied to a hydrogen monitoring system (which is pretty common). The Hydrogen sensor was in alarm upon emergency responders arriving at the scene (post-explosion). 911 callers reporting the explosion also reported hearing an alarm for 3 days prior to the explosion. This appears to have been a local alarm as it was not relayed to the Fire Department. Given how slowly batteries generate hydrogen gas, it appears the batteries were charging for a long period of time with no ventilation - the detector was alarming and hydrogen gas continued to build up until it found an ignition source. The best guess is the ignition occurred at or near a grounding strap on the battery racks but in a room full of batteries and electrical equipment, ignition sources are plentiful...especially when considering the sensitivity of hydrogen.
The lesson to pass on is that ventilation is CRITICAL with lead acid batteries. Great care should be taken to insure ventilation is adequate or even better that the batteries can NOT be charged without the ventilation system properly working.

## Slide 129: G4E07 Which of the following is true of a lead-acid storage battery as it is being charged?
  A. It tends to cool off
  B. It gives off explosive oxygen gas
C. It gives off explosive hydrogen gas
  D. It takes in oxygen from the surrounding air

## Slide 130: Solar Panel or Photovoltaic Module
Notes: Solar panels work on a process called photovoltaic conversion. The output voltage from each cell is fixed at 0.5 volts but current output changes with light intensity. These individual cells are wired in such a way that they provide the desired output voltage, generally from 12 to 48 volts. 12 volt panels can obviously be used to power radios or charge batteries (that power radios) where 48 volt panels are generally used to charge storage batteries for larger (residential-sized) electrical systems. It’s important when choosing a panel that it is wired for the correct voltage and can supply the current necessary.

## Slide 131: G4E08 What is the name of the process by which sunlight is directly changed into electricity?
  A. Photovoltaic conversion
  B. Photosensitive conduction
  C. Photosynthesis
  D. Photocoupling

## Slide 132: G4E08 What is the name of the process by which sunlight is directly changed into electricity?
A. Photovoltaic conversion
  B. Photosensitive conduction
  C. Photosynthesis
  D. Photocoupling

## Slide 133: G4E09 What is the approximate open-circuit voltage from a modern, well illuminated photovoltaic cell?
  A. 0.02 VDC
  B. 0.5 VDC
  C. 0.2 VDC
  D. 1.38 VDC

## Slide 134: G4E09 What is the approximate open-circuit voltage from a modern, well illuminated photovoltaic cell?
  A. 0.02 VDC
B. 0.5 VDC
  C. 0.2 VDC
  D. 1.38 VDC

## Slide 135: G4E10 What determines the proper size solar panel to use in a solar-powered battery-charging circuit?
  A. The panel's voltage rating and maximum output current
  B. The amount of voltage available per square inch of panel
  C. The panel's open-circuit current
  D. The panel's short-circuit voltage

## Slide 136: G4E10 What determines the proper size solar panel to use in a solar-powered battery-charging circuit?
A. The panel's voltage rating and maximum output current
  B. The amount of voltage available per square inch of panel
  C. The panel's open-circuit current
  D. The panel's short-circuit voltage

## Slide 137: G4E11 What is the biggest disadvantage to using wind power as the primary source of power for an emergency station?
  A. The conversion efficiency from mechanical energy to electrical energy is less that 2 percent
  B. The voltage and current ratings of such systems are not compatible with amateur equipment
  C. A large electrical storage system is needed to supply power when the wind is not blowing
  D. All of these choices are correct

## Slide 138: G4E11 What is the biggest disadvantage to using wind power as the primary source of power for an emergency station?
  A. The conversion efficiency from mechanical energy to electrical energy is less that 2 percent
  B. The voltage and current ratings of such systems are not compatible with amateur equipment
C. A large electrical storage system is needed to supply power when the wind is not blowing
  D. All of these choices are correct

## Slide 139: G4E12 What type of coaxial connector would be a good choice to use for 10 GHz feed-line connections?
  A. Type N
  B. Type BNC
  C. Type UHF
  D. Type F

## Slide 140: G4E12 What type of coaxial connector would be a good choice to use for 10 GHz feed-line connections?
A. Type N
  B. Type BNC
  C. Type UHF
  D. Type F

## Slide 141: G4E13 Where should you avoid placing a gasoline-fueled generator to power your station?
  A. Inside a building or outside an open window
  B. Close to cold water pipes or other grounded metal objects
  C. Close to a driven ground
  D. Downwind from your station

## Slide 142: G4E13 Where should you avoid placing a gasoline-fueled generator to power your station?
A. Inside a building or outside an open window
  B. Close to cold water pipes or other grounded metal objects
  C. Close to a driven ground
  D. Downwind from your station

## Slide 143: G4E14 What safety precaution should you observe when using a gasoline-fueled generator to power your home station?
A. Always ground the frame of the generator
  B. Use only generators that produce a clean sine wave output
  C. Make sure that the engine is well lubricated
  D. All of these choices are correct

## Slide 144: G4E14 What safety precaution should you observe when using a gasoline-fueled generator to power your home station?
  A. Always ground the frame of the generator
  B. Use only generators that produce a clean sine wave output
  C. Make sure that the engine is well lubricated
D. All of these choices are correct

## Slide 145: G4E15 During a commercial power outage, why would it be unwise to back feed the output of a gasoline generator into your house wiring by connecting the generator through an AC wall outlet?
  A. It presents a hazard for electric company workers
  B. You may draw too much current, overloading your generator
  C. Power may be restored to your house, damaging your generator
  D. All of these choices are correct

## Slide 146: G4E15 During a commercial power outage, why would it be unwise to back feed the output of a gasoline generator into your house wiring by connecting the generator through an AC wall outlet?
  A. It presents a hazard for electric company workers
  B. You may draw too much current, overloading your generator
  C. Power may be restored to your house, damaging your generator
D. All of these choices are correct