## Slide 1: ARRL – Teacher Institute
Albuquerque, New Mexico
Copyright 2009 - ARRL
Notes: 8:00 – 10:00
<number>

## Slide 2: Day 1 Review
Basic Electronics
OptoScope
Modulation / Demodulation Board
Soldering 101
Lessons learned?
Notes: <number>

## Slide 3: Day 2 Schedule
“Smoke Test” of 24-hour clock
Modulation / Demodulation Board Review
5 Building Blocks of Radio
Digital Signal Processing
Satellite Communications Demonstrations
  QSO
  Weather Satellite Imaging
  Satellite Tracking Basics
Notes: <number>

## Slide 4: 24-Hour Clock Project
Bring your project up for the “Smoke Test”
When approved, connect battery
Notes: <number>
24-Hour Clock Project
At this time, bring your 24-Hour board for the “Smoke Test”.
Please make sure you have removed all excess component leads and that there are no soldering bridges before we apply energy to the board.
When your board is approved, go ahead and connect the battery to see your clock at work.

## Slide 5: Satellite Tracking Basics

## Slide 6: Satellite Communications
Structure of Satellite QSO
Geography
  QSL Cards
  Gridsquares
  eQSL / LOTW
Types of Satellite Communications
  FM, SSB, CW, data
ARISSat-1
Notes: <number>
1:00 – 2:30

## Slide 7: Break

Notes: <number>

## Slide 8: Modulation Board Review
Connect USB OptoScope
Right-click My Computer icon
Properties/Hardware/Device Manager/ Port Com
+Sign (click) Listing (click)
Find USB Serial Port, Com#
Blue on Channel 1 Red on Channel 2
Notes: <number>
MODULATION BOARD REVIEW
-Board has rubber feet on.
-Software is installed.
-Connect USB Optoscope.
-Laptop may say “New hardware. Driver is installed.”
-Right click on My Computer icon. Go to PROPERTIES / HARDWARE / DEVICE MANAGER / PORT COM + SIGN {CLICK), Listing (click), Find USB Serial Port, COM #
Make sure BLUE lead is on Channel 1 and RED lead is on Channel 2. Leave green LEAD IN BAG. This will be used for and EXTERNAL signal source.

## Slide 9: Modulation Board Review
Open OptoScope Icon
Icon turns green
OptoScope is about $150 (discontinued)
Not full functioning
Screen shots, copy, save
Notes: <number>
Open Optoscope Icon.
If it doesn’t open, the COM Port # is incorrect. If it is open and functioning, the icon turns GREEN. If not, FILE / SET COM PORT and insert COM#.
OPTOSCOPE is about $130, less if ARRL price can be applied. Again, the Optoscope is not a full-functioning oscilloscope but then if ity “walks” away, the loss is minimized as opposed to $3.400 for a scope.
Added benefits are the screen shots / copy / paste/ save functionality.

## Slide 10: Modulation Board Review
Modulate a waveform onto a carrier wave
Square areas of board label what different circuits do
Tie points are to connect signal to OptoScope
Notes: <number>
Modulate a wave form onto a carrier wave. In other words, transmit a signal. The square areas on the Modulation / Demodulation Board demonstrate what different circuits do.
AUDIO FREQUENCY GENERATOR
RADIO FREQUENCY GENERATOR
MODULATION CIRCUIT = to the transmitter portion of the radio.
DEMODULATOR and FILTER = receiver portion of the radio.
Tie points to connect signal to Optoscope.
Be sure switches are off before inserting batteries. If batteries are matched, then there will be a wave representation on the screen. (I supplied a couple of you with mismatched batteries to test this.)
Turn board on. Turn board off.

## Slide 11: Modulation Board Review
Leads: Blue – T1 Red -T2 Black – Gnd
Channel 1 – 500mV and 200Us (Simulated audio signal)
Channel 2 – 500mV and 200Us (Simulated carrier signal)
Click Run
Notes: <number>
Connect Optoscope BLUE lead to T1, BLACK lead to GND, and RED lead to TP2. (Remember it is backwards.)
Set Channel 1 to 500mv and 200us. Simulated AUDIO SIGNAL.
Set Channel 2 to 500mv and 200us. Simulated CARRIER WAVE.
Select (click) RUN.
You should see two wave forms. Change the volume controls on both waves to see the net effects.
Note the PEAK Voltages on Channel 1. Check the frequency changes as the amplitude changes.

## Slide 12: Modulation Board Review
Change Channel 1 – 1V and 200us Change Channel 2 – 200mV and 200us
Select Channel 2 – Notice changes?
Notes: <number>
Change the setting scaling to 1v and 200mv. Notices how the signal expands.
Select Channel 2. Notice the effect on Channel 2 as Channel 1 is changed. Change the TRIGEER to Channel 2 and see how it reverses.
Turn OFF Channel 2. Appreciate the following vocabulary. Use it to describe the net effects of the signals.
Peak
Trough
Period of Wave
Frequency
Amplitude
Connect the amplifier to listen to tone. Turn on amplifier. Vary amplitude and frequency. Note changes and establish the relationship.
Changes in frequency will result in changes of pitch. Changes in amplitude will result in changes in ?
Relationship of frequency and period wave? (Inverse)

## Slide 13: Modulation Board Review
Select Channel 1 – Set centerline of Scope
Press STOP to capture it
Select CURSOR to measure period
Move TRIGGERS to the same point
Notice voltage deltas and frequency
File/Export/CONTROL6/ScreenCapture
Notes: <number>
Change to Channel 1. Set to centerline of scope. Press STOP to capture it. Select CURSOR to measure Period. Move triggers to the same point. Voltages are shown as is the delta in voltages. Frequency is also shown using CURSORS.
FILE
Export
Save as Bitmap.
Screen capture or CONTROL 6.
Print.
T line = Trigger
That is the Optoscope. Simple, effective, interesting.

## Slide 14: Break

Notes: <number>

## Slide 15: Science of Radio
Modulation / Demodulation
Information can be voice, video, data
Signal could also be digital
Over-Modulation
100% Modulation is most efficient
  but virtually unattainable
Notes: <number>
SCIENCE OF RADIO
Radio is many things. It is difficult to do it justice in just one presentation but that is all the time we have during the TI.
We began to discuss this when we talked about the modulation / demodulation activities. Combining an information / intelligence wave with a carrier wave is the process of modulation. Once the signal is received qt the receiver site, the carrier wave is stripped, leaving just the information / intelligence wave. Communication is complete.
Information / intelligence wave can be voice, video. It could be something as simple as Morse Code where either signal is ON (short, long) or OFF. Or it can contain lots of information like color, intensity, like in television. The signal could also just be digital.
Distortion occurs when signals are “Over-modulated.” See the effect of raising the radio frequency too high or too low on the Optoscope. Turn board OFF. Rescale settings to see net effects of modulation changes.
Superimpose audio signal over carrier wave signal on Optoscope. There may be a little shift in phase due to changes in electronics. These changes are not significant in audio signals but become critical when transmitting data.
100% modulation is most efficient. On the board, TP2 is internal modulation. TP5 is at the antenna. Note the difference.
Turn off board.
DEMODULATION
The radio wave has carried the intelligence signal to the receiver. The carrier wave needs to be stripped so that only intelligence remains. Connect Channel 2 to TP6 = output of demodulator. Connect Channel 1 to TP7 = output of filter.
Turn Optoscope ON. (No need to rescale.)
Radio frequency is jagged but is similar. Circuit removed shift of carrier wave but residue remains. The audio would be close to original signal but with some rasp to it (noise).
Move to TP7 = Filter Circuit. Rescale Channel 2 to 500us and 200mv. Now wave is better looking (less noise). We inject distortion when we modulate.
The carrier wave goes to ground.

## Slide 16: Science of Radio
1. Oscillator – changes DC to AC
2. Amplifier – strengthens weak signal
3. Rectifier – changes AC to DC
4. Mixer – combines two or more signals
5. Filter – separates signals
Notes: <number>
5 BUILDING BLOCKS OF RADIO
Oscillator – changes dc to ac
Amplifier – very small signal is strengthened (millionth of a volt)
Rectifier – changes ac to dc
Mixer – combines two or more signals.
Filter – separates signals.
Board Design
Oscillators – Top of board = fixed; bottom of board = variable
Amplifiers
Two Transformers – Mixer circuit is at top
Rectifier – AC to dc
Middle Integrated Circuit – Filter circuit separates signals
Optoscope – By using the jumper connectors, you can route the oscillator signal to various building blocks and use the Optoscope to see the what is happening to the signal.
Look at the VFO + ground point. J8, J9, J10 are used to get Oscillator signal to those areas.
Make sure board is OFF. Put BLUE (Channel 1) lead to VFO + gnd.
Set to 500us and 200 mv. To see the wave change form, rotate the volume control (potentiometer).
The battery provides dc; The oscillator converts dc to ac.
Set RED (Channel 2) lead to amplifier portion of circuit. Set to 1v or 500mv. BLUE Lead is output of oscillator. Notice the small phase shift and the small distortion present due to the design of the circuit. Practical limits of amplification is about 50%. To amplify more than 50, amplify the amplified.
Turn board OFF.
Look at J8, J9, J10. Set signal to Mixer, J8, Rectifier, J9 and Filter, J10.
Move jumper to J8. (Mixer) Input 1 and Input 2 on Mixer Circuit. We are combining 2 oscillator signals together. BLUE lead is Input 1; RED lead is Input 2. Rescale to 500 mv on both signals. Turn Optoscope on and see one waveform.
Compare frequency charts. Because this is a Balanced Mixer Circuit, we get 2 instead of 4 waveforms. Sum, Difference, plus 2 original signal outputs.
What you are seeing is only the sum and difference of the original signals.
Move the RED lead to OUTPUT Mixer. Rescale to 200mv. The resulting waveform is funky. Meassure by using the vertical cursors at the 2 same points = difference.
Measuring the Peak-to-Peak = addition of the 2 signals.
Turn board OFF.
Rectifier Circuit
Move the jumper to J9. Connect Jumper 1. Connect Jumper 3. The others are on one pin only.
This sets up a half wave rectifier. J3 to GRND. J1 sends signal to Rectifier.
BLUE lead output = VFO Amplifier. RED lead output = Half Wave Rectifier. Rescale RED to 500mv, BLUE to 1v.
Compare half wave with sine wave.
Turn board OFF. Move Jumper to 10. (Filter) Blue = Input, RED = Output. RED scale to 500mv, BLUE = 1v.
Turn board ON. See 2 sine waves. Vary the VFO to see RED effect as you vary frequency. Notice how amplitude increases / decreases. This is a band pass filter to pass a range of frequencies. It reduces or ATTENUATES undesired frequencies.
Frequencies above or below are attenuated.

## Slide 17: Break

Notes: <number>

## Slide 18: Digital Signal Processing Fundamentals

## Slide 19: Overview
What is DSP?
Converting Analog into Digital
  Electronically
  Computationally
How Does It Work?
  Faithful Duplication
  Resolution Trade-offs

## Slide 20: What is DSP?

## Slide 21: What is DSP?
The analog waveform is sliced into equal segments and the waveform amplitude is measured in the middle of each segment
The collection of measurements make up the digital representation of the waveform

## Slide 22: What is DSP?

## Slide 23: Converting Analog into Digital Electronically
The device that does the conversion is called an Analog to Digital Converter (ADC)
There is a device that converts digital to analog that is called a Digital to Analog Converter (DAC)

## Slide 24: Converting Analog into Digital Electronically
The simplest form of ADC uses a resistance ladder to switch in the appropriate number of resistors in series to create the desired voltage that is compared to the input (unknown) voltage

## Slide 25: Converting Analog into Digital Electronically
The output of the resistance ladder is compared to the analog voltage in a comparator
When there is a match, the digital equivalent (switch configuration) is captured

## Slide 26: Converting Analog into Digital Computationally
The analog voltage can now be compared with the digitally generated voltage in the comparator
Through a technique called binary search, the digitally generated voltage is adjusted in steps until it is equal (within tolerances) to the analog voltage
When the two are equal, the digital value of the voltage is the outcome

## Slide 27: Converting Analog into Digital Computationally
The binary search is a mathematical technique that uses an initial guess, the expected high, and the expected low in a simple computation to refine a new guess
The computation continues until the refined guess matches the actual value (or until the maximum number of calculations is reached)
The following sequence takes you through a binary search computation

## Slide 28: Binary Search
Initial conditions
  Expected high 5-volts
  Expected low 0-volts
  5-volts 256-binary
  0-volts 0-binary
Voltage to be converted
  3.42-volts
  Equates to 175 binary
Analog
Digital
5-volts
256
0-volts
0
2.5-volts
128
3.42-volts
Unknown (175)

## Slide 29: Binary Search
Binary search algorithm:
First Guess:
Analog
Digital
5-volts
256
0-volts
0
128
3.42-volts
unknown
Guess is Low

## Slide 30: Binary Search
New Guess (2):
Analog
Digital
5-volts
256
0-volts
0
192
3.42-volts
unknown
Guess is High

## Slide 31: Binary Search
New Guess (3):
Analog
Digital
5-volts
256
0-volts
0
160
3.42-volts
unknown
Guess is Low

## Slide 32: Binary Search
New Guess (4):
Analog
Digital
5-volts
256
0-volts
0
176
3.42-volts
unknown
Guess is High

## Slide 33: Binary Search
New Guess (5):
Analog
Digital
5-volts
256
0-volts
0
168
3.42-volts
unknown
Guess is Low

## Slide 34: Binary Search
New Guess (6):
Analog
Digital
5-volts
256
0-volts
0
172
3.42-volts
unknown
Guess is Low
(but getting close)

## Slide 35: Binary Search
New Guess (7):
Analog
Digital
5-volts
256
0-volts
0
174
3.42-volts
unknown
Guess is Low
(but getting really, really, close)

## Slide 36: Binary Search
New Guess (8):
Analog
Digital
5-volts
256
0-volts
0
3.42-volts
175!
Guess is Right On

## Slide 37: Binary Search
The speed the binary search is accomplished depends on:
  The clock speed of the ADC
  The number of bits resolution
  Can be shortened by a good guess (but usually is not worth the effort)

## Slide 38: How Does It Work? Faithful Duplication
Now that we can slice up a waveform and convert it into digital form, let’s take a look at how it is used in DSP
Draw a simple waveform on graph paper
  Scale appropriately
“Gather” digital data points to represent the waveform

## Slide 39: Starting Waveform Used to Create Digital Data

## Slide 40: How Does It Work? Faithful Duplication
Swap your waveform data with a partner
Using the data, recreate the waveform on a sheet of graph paper

## Slide 41: Waveform Created from Digital Data

## Slide 42: How Does It Work? Faithful Duplication
Compare the original with the recreating, note similarities and differences

## Slide 43: How Does It Work? Faithful Duplication
Once the waveform is in digital form, the real power of DSP can be realized by mathematical manipulation of the data
Using EXCEL spreadsheet software can assist in manipulating the data and making graphs quickly
Let’s first do a little filtering of noise

## Slide 44: How Does It Work? Faithful Duplication
Using your raw digital data, create a new table of data that averages three data points
  Average the point before and the point after with the point in the middle
  Enter all data in EXCEL to help with graphing

## Slide 45: Noise Filtering Using Averaging

## Slide 46: How Does It Work? Faithful Duplication
Let’s take care of some static crashes that cause some interference
Using your raw digital data, create a new table of data that replaces extreme high and low values:
  Replace values greater than 100 with 100
  Replace values less than -100 with -100

## Slide 47: Clipping of Static Crashes

## Slide 48: How Does It Work? Resolution Trade-offs
Now let’s take a look at how sampling rates affect the faithful duplication of the waveform
Using your raw digital data, create a new table of data and delete every other data point
This is the same as sampling at half the rate

## Slide 49: Half Sample Rate

## Slide 50: How Does It Work? Resolution Trade-offs
Using your raw digital data, create a new table of data and delete every second and third data point
This is the same as sampling at one-third the rate

## Slide 51: 1/2 Sample Rate

## Slide 52: How Does It Work? Resolution Trade-offs
Using your raw digital data, create a new table of data and delete all but every sixth data point
This is the same as sampling at one-sixth the rate

## Slide 53: 1/6 Sample Rate

## Slide 54: How Does It Work? Resolution Trade-offs
Using your raw digital data, create a new table of data and delete all but every twelfth data point
This is the same as sampling at one-twelfth the rate

## Slide 55: 1/12 Sample Rate

## Slide 56: How Does It Work? Resolution Trade-offs
What conclusions can you draw from the changes in sampling rate?
At what point does the waveform get too corrupted by the reduced number of samples?
Is there a point where more samples does not appear to improve the quality of the duplication?

## Slide 57: How Does It Work? Resolution Trade-offs
Bit Resolution
High Bit Count
Good Duplication
Slow
Low Bit Count
Poor Duplication
Fast
Sample Rate
High Sample Rate
Good Duplication
Slow
Low Sample Rate
Poor Duplication
Fast

## Slide 58: DSP
NYQUIST = Sampling rate must be at least two times the frequency
On the OptoScope changing the time base on the horiziontal changes the sampling rate
Notes: <number>
NYQUIST = Sampling rate must be at least two times the frequency. Nyquist was engineer who developed theories of noise, system stability and telegraph signaling.
On the Optoscope, changing the time base on the horizontal to change the sampling rate.

## Slide 59: Break

Notes: <number>

## Slide 60: Radio Direction Finding

## Slide 62: Break

Notes: <number>

## Slide 63: Satellite Communications
Notes: <number>
1:00 – 2:30

## Slide 64: Radio, Space & Wireless Technologies
Career & Technology
Ham Radio Licensing
  Skywarn (NWS/NOAA)
  ARES/RACES
  Perkins?
Radio Telescope
Fox Hunt
Circuit Building Skills
  Fabrication?
Robotics
Holography
Remote Sensing & Data Collection
Satellite Comms
Notes: <number>
Wireless Technology - How important is the technology to each of us?
Remote controls
Cell phone
Toothbrushes
Pregnancy tests
Terrorists were using wireless technology against us. Car bombs were being detonated by car door transmitters. To get 10’ plus distance, hold transmitter under chin, open mouth and press.
NASA is studying growing food in space to colonize the moon. President says cost will be $20B - $50B.

## Slide 65
www.powerpointemplates.com/
Thank You!