## Slide 1: ARRL – Teacher Institute
Rocklin, California
Copyright 2009 - ARRL

## Slide 2: TI – “Picnic” / Dinner
Johnny Garlic’s
Tonight at 6:30pm
Spouses, Friends, Family welcome!
If you have others coming, let me know…
Notes: <number>

## Slide 3: IMPORTANT : For tomorrow…
Ask hotel for a receipt showing your total amount owed for your hotel stay
  Needed for travel vouchers tomorrow
Bring copy of travel costs
  Airfare receipt
  Cab/shuttle fare
  Mileage report (Google Maps)

## Slide 4: Remote Control Basics

## Slide 5: Remote Control
How does a TV remote work?
Multiple Receivers
Multiple Devices
Multiple Manufacturers
Notes: <number>
Purpose: The objective of this activity is to explore the technology behind the common TV remote, how it works and how it could be used in every day life.
Overview: I bet the average home has a number of hand-held TV remote controllers. Virtually each entertainment device now comes with its own remote control, in fact, some entertainment devices will not work unless you use the remote control. Additionally, many remote controls are capable of controlling multiple devices, from different manufacturers…this activity addresses that capability. Along with addressing specifically infrared transmission systems, this activity can be used to study wave propagation.

## Slide 6: Remote Control
Infrared Light
Serial Communications
Notes: <number>
Two wireless technology concepts allow the remote control to communicate with the TV, DVD, VCR. The first concept is infrared light. The second is serial communications.

## Slide 7: Remote Control
Color Wavelength (nm)
Violet 400
Blue 470
Green 565
Yellow 590
Orange 630
Red 780
Near infra-red 800-1000
Infra-red 1000-2000
Far infra-red 2000-10000
Nanometer =1X10-9 m
Light ray = 980nm
Notes: <number>
ColorWavelength (nm)
Violet 400
Blue 470
Green 565
Yellow 590
Orange 630
Red 780
Near infra-red 800-1000
Infra-red 1000-2000
Far infra-red 2000-10000
The light portion of the electromagnetic spectrum is illustrated in figure 1. Listed in the table are the light color and the wavelength in nanometers. A nanometer is one-billionth of a meter or 1X10-9 meter. The light used in the standard TV remote to carry the commands from the user to the TV is the near infrared range frequency of approximately 980 nm. There is a light emitting diode (LED) in the remote control that sends out a light beam at a frequency of 980 nm. If you look at the end of the remote that you point toward the TV set, you will see a plastic window covering the LED, or you may actually see a little clear plastic dome exposed about 1/8 inch in diameter.

## Slide 8: Remote Control
TV has Infrared device receiver
Designed for light at 980nm
Receives light and converts it to electrical impulses that correspond to key codes
Notes: <number>
On the TV side, there is an infrared receiver device that is located somewhere on the front of the TV behind a plastic window. The location of the receiver is sometimes difficult to see but it is usually located near the manual controls on the TV. This receiver is specially designed to respond to infrared light at a frequency of 980 nm. It also has some very sharp filters that eliminate as much background light outside of the 980 nm frequency range as possible. These filters prevent bright sunlight from overwhelming the receiver, but the filters are not perfect. That is why sometimes when there is bright sunlight shining directly on the TV set you may have difficulty controlling the TV with the remote control. When you press a button on the remote, a special code assigned to that key is sent as a beam for infrared light by the LED. The infrared receiver on the TV in turn receives that beam of infrared light and converts it into electrical impulses that correspond to the key code and sends those impulses to a computer in the TV. If you darken the room and look into the remote window covering the LED you will see a faint blinking light coming from the LED. We can not see infra-red light with just our eyes, but you can detect some other light being emitted by the LED at the same time it is emitting infra-red light (that other light is called spurious radiation).

## Slide 9: Remote Control
What is the biggest problem using light to transmit?
Sun sends Infrared light
How does remote control tell the difference?
Notes: <number>
Using light to transmit information from the remote to the TV set sounds like a good idea, but there is a problem. Can you think of a problem that must be overcome before this system will work properly? (hint: we touched on the cause in the preceding paragraph) The problem is that the sun sends infrared light along with all the other colors of the light spectrum, including light at 980 nm. The problem is that there has to be a way for the TV infrared receiver to tell the difference between infrared light sent by the TV remote and the infrared light coming from the sun.

## Slide 10
SONY Control-S Protocol for TV
_________________________________
Remote Key Digital Code Sent (decimal) binary
1 (0) 000 0000
2 (1) 000 0001
3 (2) 000 0010
4 (3) 000 0011
5 (4) 000 0100
6 (5) 000 0101
7 (6) 000 0110
8 ( 7) 000 0111
9 (8) 000 1000
0 (9) 000 1001
Enter (11) 000 1010
Channel up (16) 001 0000
Channel down (17) 001 0001
Volume up (18) 001 0010
Volume down (19) 001 0011
Power on (21) 001 0101
Power off (47) 010 1111
Mute (20) 001 0100
Universal Codes
Developed by SONY
Notes: <number>
Now that we have covered how the signal goes from the remote control to the TV, next we will discuss how the individual keys (power-on, channel selection, volume control, etc.) are recognized by the TV. Each key is assigned a 7 bit binary code as shown in figure 2 . You have covered binary codes before; binary is based on two states, on and off, 1’s and 0’s. A bit of information is one character either on or off and the byte of chunk of information is made up of a number of bits, in this case 7 bits. As an example, if you press the 1 key on the remote control, the infrared LED will be flashed on and off the bits that represent the binary code for the 2. I cannot explain why the code for 1 is not sent, that is just the scheme that was set up for TV remotes.

## Slide 11
Null vs 0 Problem
Different Pulse Widths
TV Remote Pulse Widths
___________________
Binary Bit Pulse width in milli seconds (ms)
Start bit 2.4 ms
1 1.2 ms
0 .8 ms
Pause between bits .68 ms
Notes: <number>
TV Remote Pulse Width uses Start bit of 2.4 ms, 1 of 1.2 m, 0 of 0.8 m, Pause between bits of .68 ms.
There is a slight problem with sending on and off pulses of light to represent the binary bits of 1’s and 0’s, how can the receiver tell if no signal represents a 0 or just that the remote control is done sending. Well the system is set up to recognized different pulse widths as 1’s and 0’s and one other special bit, a start bit. Figure 3 lists the different pulse widths used. So when the infrared pulses are being received, a 2.4 ms pulse is recognized as a start pulse, a 1.2 ms pulse is recognized as the 1, and a .8 ms pulse is recognized as a 0.

## Slide 12
Gray = START BIT
Green = 7 data bits
Red = Device Code
SONY = 0000
Notes: <number>
Shown are illustrations of oscilloscope patterns of the signals of the first few keys of the remote control. You can see the start pulse which tells the receiver that the following pulses will represent a command, then you will see 7 bits (1’s and 0’s) that make up the command, and finally you will see a longer space and more bits. These trailing bits send out a device code. A unique device code is assigned to each type of equipment being controlled (TV, VCR, DVD, satellite receiver, etc.) and the equipment manufacturer (SONY, RCA, SANYO, etc.). This is how you can control many different types of equipment with one remote control. In this lesson we are looking at the commands sent to SONY TV sets because it is the simplest code.
Shown are SONY 0000, KEY 1 = decimal 0, KEY 2 = decimal 1.

## Slide 13
Gray = START BIT
Green = 7 data bits
Red = Device Code
SONY = 0000
Time Intervals of 20ms
Notes: <number>
Shown are KEY 3 = decimal 2 and KEY 0 = decimal 9

## Slide 14: Programming the Remote
Flashing red lights on appliances
Check for batteries in Remote
Find, press, hold KEY 1 (LED lights twice)
Press 0,0,0,0 (Remote acknowledges)
Select TV and Program
Notes: <number>

## Slide 15: Infrared Comms
BOE-BOT Instructor’s Board
Infrared is not rf; it’s electromagnetic wave
Major Problems: line of sight, interfering particles, scattering, light, especially Sun
Notes: <number>
BOE-BOT instructor’s board will use the power source from the BOE-BOT.
Use Light-Spectrum Chart can be used Infrared Range used by technology, uses Near Infra Red 800- 1000 nano meter range.
The medium we use here to send information from point A to point B is not a radio wave, it’s an electromagnetic wave.
The major problems in using light to transmit information with Infra Red:
Line of sight
Interfering particles
Scattering
Light, especially the sun
Receiving site has a problem. How can the receiver tell if the signal is IR or light from the sun?

## Slide 16: Infrared
Hams use PL (Private Line)
Used to ID a specific signal
IR modulates the light on 980nm at a rate of 37.5KHz
Pulse Width Modulation
Notes: <number>
Hams have been using PL (Private Line) for a long time. PL is used when we want to identify a specified signal, we override on that signal a sub-audible tone of a specific hertz (200 Hz).
If the signal is present, the receiver says “I get it” and responds’. IR modulates the light at 37.5KHz. The receiver is tuned a frequency of 980 nano meters and only to lights that are turned off and on at a rate of 37.5KHz.
What we are going to see is a series of data pulses that present 1, 2, 3, 4.
Another problem with using light is to identify is that if the light is present, it’s a 1. If the light is NOT present, is it because it’s a 0 or because there is an interference or because there is no signal.
In other words, how do you tell the difference between a 0 and no signal or interference?
A high pulse does not represent a 1. They vary the pulse width so a WIDE PULSE represents a 1.
A NAROW PULSE width is a 0.
PULSE MODULATION
Standardized Protocol for the code we have three different pulse widths to represent 0, 1 and a Start Bit.

## Slide 17: Infrared
Pulse 2.4ms Starts
1 is 1.2ms
0 is .8ms
Between Bits is .68ms
Notes: <number>
Chart
A pulse width of 2.4ms tells the receiver that we are starting.
A 1 is 1.2ms. 0 is represented by .8ms. Pulse between bits is .68ms.
Industry Standard
Using the Optoscope, your students should be able to measure the pulse widths and tell which one is a zero, 1, spacing or starting bit.
Receiver also needs a system for recognizing what band and type of equipment is being used.
Therefore a couple of things happen:
Chart LSB This is a series of pulses that you will see on the Optoscope.
In this case, pulse is actually inverted; high = 0, bottom part is actually pulse.
There’s a preamble that identifies the manufacturer followed by what type of equipment that data stream.
SONY has the simplest code. They came up with the use of IR for remote control. Their code is 0000 for their TV sets.
TV will look for the start bit, called data bits, and ask “Is this for me?”
When you press a number on the remote control, the signal is sent to the tv and the tv says, “I get it.”
20ms time intervals are used. If I see a 1, and then 20ms later I see another 1, I know it’s a repeat.
Chart
Key 0 = decimal 9 bit here is wider, 0 bit is narrower and so on.
There will be lots of lights here in a few minutes when we do the activity.
Programming the Remote
First make sure the remote has batteries.
Find and hold key 1 in the upper left. Press and hold. LED will light up twice. Press 0,0,0,0 The remote acknowledges it.
Select TV and program.

## Slide 18: Infrared
Pull out BOE-BOT Board
Four Receivers tuned to 980nm @ 37.5KHz
Look for RX Out & GND (Hook up scope)
Pull out USB cable
Put 4 feet on Board
Put everything else in BOE-BOT Box
Notes: <number>
Pull out the BOE-BOT Board.
On the board are four receivers. They are silver rectangular in shape. (IR Receivers)
On the TV sets are similar receivers behind a red lens, usually.
The receivers are tuned to 980 nano meters to look for modulation of that wavelength at 37.5KHz.
There are four on the BOE-BOT to make certain they pick up the signal.
Look near the variable resistor, a couple of pins say RX OUT. There’s a ground GRN Pin and an IR RX pin.
There’s where you will hook the Optoscope.
Small envelope that has four extensions and one plug. Pull out one plug.
We are going to connect the plug on the bottom of the board to connect the BOE-BOT power source.
Here is where things begin to get complicated.
Open up the BOE-BOT kit and pull out the BOE-BOT board called the BOARD OF EDUCATION.
The four extensions will be used tomorrow. Put them away for now.
Look for the larger silver envelope. It has the Board of education.
You will also find a silver baggie, you will need that also. It has the BASIC STAMP.
Pull out the USB cable from the box.
Pull out four rubber feet for the bottom of the Board.
Put everything else back in the box.

## Slide 19: Infrared
USB connector is to BACK of BOE-BOT
Plug in power supply
Look for ON / OFF switch
Get laptops running
Connect OptoScope and get it running
Notes: <number>
Turn the Board over and install the rubber feet. If the feet are not put on correctly, you will not be able to connect later. The rubber feet prevent the Board from shorting out.
On the BOT Board, notice where the USB connection is. That is the back of the Board.
Insert the Instructor’s Board into the plug so that the notch is matching from the Board of Education.
Align the pins and insert. This provides power source.
Look for the Board of education ON / OFF switch.
Get the laptops running. And the OptoScope running as well.
No batteries yet!

## Slide 20: Infrared
Set OptoScope to 2ms & 1 v
Blue – IR Receiver Black – GND
Put 9 volt batteries in
Set TRIGGERS to Falling Edge, Auto, Single Acquisition
Press & Hold a button on Remote and Hit RUN on OptoScope
Notes: <number>
Set the OptoScope to 2ms and 1v. Put BLUE lead to Instructor Board at IR receiver and BLACK lead to GRN.
Put 9 volt batteries in.
Set up triggers to Falling edge, Auto, Single Acquisition.
Press and hold a button on remote and hit RUN on the OptoScope.
Press and hold a button on the remote and hit RUN on the OptoScope.

## Slide 21
Infrared
Result is data stream capture
Everyone get a data stream?
Slide the top back & forth
Notes: You will capture one of the pulses on the OptoScope.
Did everyone get a data stream?
Slide the top back and forth.
This is the start bit. It’s supposed to be 2.4ms. Select CURSOR function. Turn on Vertical bars.
Measure the Start Bit. Read Auto = Measure next bit. Space is in between. 7 data bits, then SONY code.
(Students could determine data measurements for all keys on the remote control.)
In the TV or appliance, there is a PIC dedicated to monitoring the receiver, and programmed to look for code and capture the key and take the action for whatever is programmed for that key.
Press 0 has the Binary Code for 1. Press 8 has the Binary Code for 9.
BOE-BOT will respond to IR commands.
Put OptoScope away. You are done. Disassemble the Instructor’s Board off the BOE-BOT Board and put away.

## Slide 22: Break

Notes: <number>

## Slide 23: WAM? Textbook Slides
(Run “What’s a Microcontroller?” Slides Concurrently with this PowerPoint)
Notes: <number>
What’s a Microcontroller? PowerPoint Presentation should be run on a separate screen to provide step-by-step instruction and explanation to students.

## Slide 24: WAM? BOE-BOT
Keep WAM? and BOE-BOT separate
We’ll use WAM? today and then put away
SERVO today is standard (180º)
BOE-BOT SERVOS are modified
Need Board of Education, Basic Stamp, USB cable
Notes: <number>
What is a MicroController (WAM)?
There are 2 kits. One for BOE-BOT. Keep them separated.
MC is a separate course. We’ll use today and then put it away.
SERVO today is a standard servo, stops at 180 Degrees.
BOE-BOT servos are modified.
Open up package. Need Board of education, Basic Stamp, USB cable.

## Slide 25: WAM?
Small, limited but very powerful computer
Usually one chip to perform some function
Found in everyday consumer devices
  cell phones
  televisions
  MP3 Players
  toys
Notes: <number>
WAM
Small, limited, but very powerful computer. Usually has one Integrated Chip to perform some function.
Usually has a number of input / output lines to communicate with outside world. They are in every cell phone, television, Gameboy, etc.,

## Slide 26: WAM?
BASIC STAMP is a PIC
Easy to program
Power sources and memory are on BS
Very powerful
Number of BASIC STAMPS on ISS
Find BS – Silver envelope/green
BS vary in temperature range, speed & $
Notes: <number>
The Basic Stamp is a PIC.
Basic Stamp is easy to program. Power sources and memory are already on them. Very powerful.
There are a number of Basic Stamps on the International Space Station.
In the silver envelope, find the Basic stamp. Remove it. It is green. It means it is Basic Stamp2. Other Basic Stamps are color-coded.
The Basic Stamps vary in temperature range, speed and price.

## Slide 27: BASIC STAMP
BS is relatively expensive
Contain other parts that save money elsewhere
Middle – 2 brown rectangular = oscillator
BS need external time control device
Programs rated to last 40 years
2 black ICs = external memory
Notes: <number>
Basic Stamps are expensive but they also contain other parts that save money elsewhere. The painted notch on top left is the Index to orient. The bottom has an IC = PIC.
On the middle are two rectangular parts (brown), this is the oscillator.
Computers need some sort of time device that controls the clock signal. On the Basic Stamp, that source is outside.
We are going to put programs into the Basic Stamp. Even when the power is removed, it will remain there until it is replaced. Programs are rated to last 40 years.
The two black Integrated circuits are external memory that will translate your program (Parallax Proprietary) into digital (1s and 0s that tell the machine what to do. We will use PBasic language to program.

## Slide 28: BASIC STAMP
PBASIC Language
Top – power supply converts 9-15v to 5v
P0-P15 P16 = input/output pins we can control
Top – another black area = VDD = 5v
VSS pins = GND
VN – used to change voltage
Notes: <number>
We will use PBasic language to program.
At the top of the Basic Stamp is the power supply that converts 9 – 15 volts down to 5 volts.
Look at the Board of Education Board. Book and slide images are different due to evolution of the product.
Along the left side of the board are P0 – P15. 16 input / output pins we can control. So when we tell the computer Output 1, it will use Pin 1.
At top is another black area with VDD, Pins are 5 volts, CSS, pins are ground, VN (middle) used to change voltage. The jumper at the top is set to 5 volts.

## Slide 29: BASIC STAMP
Top – 2 larger plugs marked 12, 13, 14, 15 to be used to plug in SERVOS
Right Side – Red, White & Black = color-coded SERVO connectors
Other IC – voltage regulator (9v to 5v)
2 Power Plugs; 9 & 6 volts
Configured to use only one at a time
Notes: <number>
At the top are two larger plugs marked 12, 13, 14, 15. These are to plug in servos.
On the right side are red, white and black. Servo wires are color coded. Make sure servo plugs are inserted correctly.
The other Integrated Chip is the voltage regulator to convert 9 volts to 5 volts.
There are twp power plugs. One for nine volts, the other for 6 volts. They are configured so that both cannot be used at the same time.
Capacitor filters are used to take care of power surges.

## Slide 30: BASIC STAMP
USB Plug
Power Switch has 3 positions
0 = OFF
1 = Power to BS only
2 = Power to BS AND SERVO
When program is sent to BS, it starts running
Notes: <number>
USB Plug
Power switch with three positions. 0 = OFF. 1 = Power to Basic Stamp only. 2 = Power to Basic stamp and the Servo.
When program is sent to the Basic Stamp, as soon as it receives it, is starts running the program.

## Slide 31: BASIC STAMP
Use Position 1 to Send Program to BS
Don’t use Position 2 or BOE-BOT may run off the table
Push Button to RESET, re-start BS
Green LED shows there is power to board
Install BS on Board
Notes: <number>
Use position 1 to send program to Basic Stamp, not position 2 or the BOE-BOT might just run off the table.
Push the button to reset. Basic Stamp starts again.
Green LED shows there is power to the board.
Application socket is in the middle. Parallax uses it to plug into other products they produce.
On the BOE-BOT board, there is a notch to place the socket. Match the pins on the notch and press it into place using your thumbs; you will hear and feel a “thunk.”

## Slide 32: Break

Notes: <number>

## Slide 33: BASIC STAMP
Writing Code & dumping it into BB
Launch BASIC STAMP
Increase screen size
Left - Directory of computer
Below is a list of programs
Top are ICONS for Windows
“Untitled” tab at top for multiple BS
Notes: <number>
Writing Code for basic Stamp
We now begin writing code to communicate with the BOE-BOT and will dump it using the USB cable.
- Launch Basic Stamp.
- Increase screen size.
- Note area for writing the program.
- On the left is the directory of your computer.
- Below it is a list of the programs you have been working with.
- At top are typical ICONS for WINDOWS.
- “Untitled” tab at top for multiple Basic Stamp programs.

## Slide 34: BASIC STAMP
Use Green ICON at top
Top are 1.0, 2.0, 2.5 Programs are backward compatible
Use 2.5
Credit Card = used to check communication between BS & computer
Check Mark = syntax check
Notes: <number>
- We will use the Green Icon on top Icons.
- On top, at the center, are 1.0, 2.0, 2.5., programs are backward compatible.
- We will use 2.5.
- The Credit card looking ICON will be used to check communication between the Basic Stamp and the computer.
- The Check Mark Icon will be used for Syntax Check. This feature is not perfect but helpful. It does highlight the area where the syntax problem may be found.

## Slide 35: BASIC STAMP
Triangular Shaped Button – send program to BS
Magnifying Glass – transfer program from BS to computer for Debugging
Bible ICON – Help Menu
Plug USB into Board and into computer
(No batteries yet)
Notes: <number>
- The following ICON is for memory; it will not be used.
- The triangular shaped button is to send the program to the Basic Stamp.
- The Magnifying Glass ICON is used to transfer the program from the Basic Stamp to the computer for Debugging.
- The Bible ICO is the HELP Menu – this feature is very good! Type the issue and select from the options menu.
- Plug the USB cable into the Board of Education and also into the computer. No batteries yet.

## Slide 36: BASIC STAMP
Click on ID Card – Dialog box shows Comp Prt# and says “Loop back yes and echo yes.” Close Window.
Battery in Board
Slide switch to Position 1on BB. Do another ID check. Should read “B2 Version.” YES.
USB Version Problem if DeBug Window is open and you unplug
Notes: <number>
- Click on the ID Card. A dialog box opens that shows Comp Port Number and says “Loop back yes and Echo yes.” Close window.
- Plug a battery into the BOE-BOT.
- Slide witch to Position 1 on BOE-BOT. Do another ID Check. Dialog Window should recognize “B2 version #. Click, yes, click yes.
- USB version compilation. If you have a DeBug Window open, and you unplug, the computer gets really confused.

## Slide 37: BASIC STAMP
Begin to copy commands from book – DO NOT include DEBUG Commands
Use 2.5 Editor Version & BS 2 ICON
“Hello World” – first command by tradition
DEBUG in PBASIC
  Prints text in “debug window” on PC
Using lowercase, type “debug”
Notes: <number>
- When you begin to copy the commands from the book, do not include the DeBug Commands.
- I will change the fonts. This is for display only.
- Every program you write will require what version? And what Basic Stamp?
- We will use the 2.5 Editor Version. Click on the ICON.
- Select the Basic Stamp 2 ICON. Notice how it changes color.
- It has become almost a tradition that the very first programming line you learn is “HELLO WORLD.” We shall continue with this tradition.
- DeBug in PBasic means “Send back whatever I type.”
- Use lowercase letter and type debug When I hit return, debug becomes capital letters and turns blue. This means that the computer recognizes the command as a valid command.

## Slide 38: BASIC STAMP
Type “Hello World” Hit RUN & watch bottom of screen = Tocanized Successful
Set Position 1 on BB RUN
Tell computer to print “Hello World” many times Use Loop Command
Loop Command is Above Debug “Hello World” type Do Below type Loop Turns Blue
Notes: <number>
- Type “Hello World.” Hit run and watch the bottom of the screen. It turns green and reads “Tocanized Successful.”
- Set Position 1 on BOE-BOT, click on RUN. Computer returns “Hello World” Computers are very good at doing very boring jobs very, very fast, many times over without ever complaining.
- We want to tell computer to print “Hello World” many times. We use a Loop Command.
The syntax for a Loop Command is: Above DeBug “Hello World” type Do It turns blue. Below DeBug type loop It turns blue.
- Before we press RUN, let us think about these commands. Do will look for a loop and if it finds it, it will setup an infinite loop until power is removed. Press RUN ARROW.

## Slide 39: BASIC STAMP
“ “ to add spaces
Type “Hello World”, Press CR Turns Purple
Declare Variable to do LOOP a certain number of times (10 times)
After 2.5 Version type Counter
Counter_VAR_Byte
Bit=ON/OFF Switch 4 bits=I nibble 8 bits=1 Byte
Notes: <number>
To add spaces type “ “
- Type “Hello World”, Press CR It turns purple which menas Syntax error.
- To Do LOOP only a certain number of times, we need to declare a variable location to store a number.
- Say we want to print “Hello World” ten times.
- At the beginning of the program right after the Basic Stamp 2, Version 2.5 information, type Counter
- Count is reserved word but by adding er, it changes it and can be used.
- Counter_VAR_Byte This command reserves some space called Counter to be used as a variable with a size of 1 Byte
- Bit = ON / OFF switch 4 Bits = 1 nibble 8 Bits = 1 Byte

## Slide 40: BASIC STAMP
16 Bits, 4 nibbles, 2 Bytes = 1 Word
In 1 Bit = 0 – 255 In 1 Word = 65,535
Set VAR to minimum
If I use 1 Byte and exceed the limits = crash
Counter VAR Byte
For Counter 1 to 10
DeBug “Hello World”
Notes: <number>
- 16 Bits, 4 Nibbles, 2 Bytes = 1 Word (16 Bits Long)
- In 1 Bit you can store a 0 or 1 In 4 Bits, you can store 16 or Numbers 0 – 15
- In a Byte = 0 – 255 In a Word = 0 – 65,535
- To conserve memory, set VAR to minimum. If I use Byte and exceed the limits, the computer program will crash Basic Stamp 2, Version 2.5

## Slide 41: BASIC STAMP
Counter VAR Byte
For Counter 1 to 10
DEBUG “Hello World”
NEXT
Press RUN
Notes: <number>
Counter VAR Byte
For counter 1 to 10
DeBug “Hello World”
NEXT
FOR looks for NEXT This program will run 10 times and stop
I could have counted 20 to 30 or Counted 250 to 260
Press RUN

## Slide 42: BASIC STAMP
Change VAR to WORD
To add Counter #s:
FOR Counter 1 = 10 DEBUG Counter, “Hello World”
NEXT
To print, display codes are different! TEXT
Computer will return an error message
Notes: <number>
Now change VAR to WORD
To add counter #s For Counter 1=10
DeBug Counter, “Hello World”
NEXT
To print displays codes are different! TEXT
The computer will return an error message. To correct, go back to For Counter = 1 to 10

## Slide 43: Break

Notes: <number>

## Slide 44: BASIC STAMP
FOR Counter = 1 to 10
DeBug “Hello World”
NEXT Press RUN
ASCII Codes are different
ASCII Code for 1 is 49
ASCII Code for 2 is 50
Notes: <number>
FOR Counter = 1 to 10
DeBug “Hello World”
NEXT Press RUN
ASCII Codes are different ASCII Code for 1 is 49 ASCII Code for 2 is 50

## Slide 45: BASIC STAMP
Use BS to turn LED On/Off
Pages 47-50 in WAM? Book
Tale components from kit
Build the circuit LEDONOFF.bs2
Longer lead on LED is +
Start using the pictures but begin to equate component with symbol & schematic
Notes: <number>
Now we are going to use Basic Stamp to turn an LED ON and OFF.
Pages 47 – 50 in the book. Take the following components from the kit parts. Red, yellow or green LED and 470 ohm resistor (yellow, violet, brown)
Build the circuit LEDONOFF.bs2 The longer lead on the LED is positive, the shorter lead is negative.
Start using the pictures for the circuit building but begin to equate the picture with the schematic. Learning to read schematic is a fun and easy-to-do activity.

## Slide 46: BASIC STAMP
Pin 14 is current source to LED (High Voltage)
Setup basic Commands
  Do Loop
  Pause 250
  BS thinks in 1ms steps 250ms = ¼ second
Notes: <number>
Pin 14 is the current source to light the LED. Resistor is a current limiting resistor. Diode allows electrons to flow in only one direction. If when you run the program and if it does not work, chances are the diode was installed backwards.
Set up two Basic Commands. Set up a Do Loop On Pin 14 we want a high voltage , then Pause 250
Basic Stamp thinks in 1ms steps 250ms = ¼ second

## Slide 47: BASIC STAMP
Low = 0 Report it to Pin 14
Turn board OFF
Reverse LED and try it
Add ‘ to the PAUSE Command
‘ = Comment Line
Take ‘ out Change PAUSE to 500
Change Low = 250
Notes: <number>
Then Low = 0 Report it to 14 for ¼ second LED should flash. Turn Board OFF. Reverse LED and try it. It will not work. Reversing it will not break the diode.
Change the program by adding an apostrophe (‘) to the Pause Command
‘ = Comment Lines RUN program. What happens? The light appears to be on continuous but it is turning on / off at 1ms intervals.
Take ‘ off. Change Pause to 500 Change Low = 250
You should see longer ON than OFF. Pause can be as long as 65,550.
Now you can cause it to flash 15 times.

## Slide 48: BASIC STAMP
Counter VAR Byte
For Counter = 1 to 15
High 14
Pause 250
Low 14
Pause 250
NEXT
Notes: <number>
Counter VAR Byte
For Counter = 1 to 15
High 14
Pause 250
Low 14
Pause 250
NEXT
Turn power off. Unplug USB cord. Turn power on. It should run, press reset. Try it.

## Slide 49: BASIC STAMP
BS can be programmed millions of times
Page 57 WAM? Add a second LED
RUN it
Try alternating ON / OFF
Notes: <number>
The Basic Stamp can be re-programmed millions of times.
Chapter 2 Pages 57 Add a second LED plus a 470ohm resistor to circuit. Set up the circuit to Pin 15. Wire the circuit. Type the program. Run it. Try alternating the LEDs ON / OFF.

## Slide 50: BASIC STAMP
Pages 72 – 76 WAM? Pushbuttons
Leave other components on
Use Command Pin 3
Use DEC (Error message)
Notes: <number>
Chapter 3 Pages 72 – 76 We have been using the Basic Stamp to light up LEDs.
Digital Input – Pushbuttons. We will wire a switch circuit. Get a switch plus two jumper wires plus 220 ohm resistor (Brown, Black, Orange) Look at the switch. Pins 1 & 4 have an internal connection, pins 2 & 3 also have an internal connection.
Leave other components on. When we push button, we short circuit and close the circuit. Put the switch across no man land on the breadboard.
Use Command Pin. It will read voltage at Pin 3
If > 3.5v =1
If<3.5v = 0 When we push switch it will return a 0 or a 1. This is important? If we had a program error and current limiting resistors did not do their job, Pin 3 would fry. The current is rated at 35mA. When switch is up = 0. When switch is down = 1.
We are setting up an infinite loop. DeBuging value will display Pin 3 value or 0. Pasue ¼ second. Do it again. Test pushbutton.
Try a change. Try DEC It will display DeBug DEC IN3, Cr What happens?
Syntax says “I am going to do this. Error. Type DeBug “IN3”, DEC IN3, CR This could replace above.

## Slide 51: BASIC STAMP
Pages 80 - 83 WAM? Digital Input
Build the circuit
Type the program
Test it
Notes: <number>
Chapter 4 Pages 80 – 83
Digital Input – Pushbutton LED Circuit
Build the circuit.
Type program.
Test it.
IF – THEN Statement allows computers to make choices
IF Pin3 = 5volts or 1 do command
Turn on, pause, off, end
IF Pin 3 = something else, 0 will send
Else, pause, & do it again.
Page 81
Push Button LED Circuit
Adjust program so when button is pressed, green LED will flash, when not pressed, RED LED will flash.

## Slide 52: SERVOS
Pull out SERVOS from kit.
SERVOS are used in robotics, airplanes, manufacturing, printers, …
Move gears, “feel” & “hear” the movement
Precise movement
Notes: <number>
SERVO MOTOR and ELECTRONICS
Pull out Servos from the kit. Move gear with your fingers. Hear the gears as they move.
Servos are used in robotics, airplanes, manufacturing.
Inside the Servo :
When the motor turns, the output sends a signal to a variable resistor
The variable resistor’s values changes
A 555 IC serves as a VFO with specifications of 20ms width = 1.0 – 2.0
The output of the IC is a square wave oscillator signal of 0 – 5 volts
The signal is received by a comparator. Signal is determined by the VFO
The comparator receives a digital signal. Either a 0 or a 1.
If the value of the signals are not equal, the comparator sends a signal to the motor to turn and the process starts again
If the value of the signals are equal, then no signal is sent and the motor stops
The system is looking for a pulse width = 20ms
It is also looking for 1.0 – 2.0 ms (average 1.5)it.
IF – THEN Statement allows computers to make choices
IF Pin3 = 5volts or 1 do command
Turn on, pause, off, end
IF Pin 3 = something else, 0 will send
Else, pause, & do it again.

## Slide 53: SERVOS
As motor turns, send signal to a variable resistor
A 555 IC serves as VFO with 20ms & width = 1.0 - 2.0
Output is square wave signal = 0 – 5 volts
Comparator receives digital signal (0 or 1)
If values are NOT equal, Comparator sends signal to start again
Notes: <number>
SERVO MOTOR and ELECTRONICS
Pull out Servos from the kit. Move gear with your fingers. Hear the gears as they move.
Servos are used in robotics, airplanes, manufacturing.
Inside the Servo :
When the motor turns, the output sends a signal to a variable resistor
The variable resistor’s values changes
A 555 IC serves as a VFO with specifications of 20ms width = 1.0 – 2.0
The output of the IC is a square wave oscillator signal of 0 – 5 volts
The signal is received by a comparator. Signal is determined by the VFO
The comparator receives a digital signal. Either a 0 or a 1.
If the value of the signals are not equal, the comparator sends a signal to the motor to turn and the process starts again
If the value of the signals are equal, then no signal is sent and the motor stops
The system is looking for a pulse width = 20ms
It is also looking for 1.0 – 2.0 ms (average 1.5)it.
IF – THEN Statement allows computers to make choices
IF Pin3 = 5volts or 1 do command
Turn on, pause, off, end
IF Pin 3 = something else, 0 will send
Else, pause, & do it again.

## Slide 54: SERVOS
Controlling Motion is performed by BS
Pages 112 – 118 SERVO Control
Internally computer counts at rate of 2ms
Task
Do turn (1000) left Pulsout 14, 1000
Do turn (500) right Pulsout 14,500
Do turn (750) middle Pulsout 14, 750
Notes: <number>
Chapter 4 Controlling Motion
If the comparator senses disparity of frequencies, it will turn motor to change VFO until comparator is equal, then the motor stops.
Basic Stamp input controls motor running. When the Basic Stamp stops, the motor runs free.
PowerPoint Presentation Pages 115 = 118
Clockwise 2.0ms pulse to servo
When comparator says the signals are equal, the motor stops.
Counter 1.0ms pulse to Servo
Pages 112 – 118
PowerPoint Presentation
RED = 5 volts Black = GRN White = Pin 14
Plug Servo into Jack 14 White LED on Pin 14
Servo plug into Board
Command to send a Pulse Pulseout 14 means send a pulse to Pin 14
Internally computer counts at rate of 2ms (2 x 1000 = 2000ms)
2ms = 1000 count 1.5ms = 750 count 1.5ms = 500 count
Pages 115- ___
Write code for servo Movement
For counter = 1 to 150
LED will pulse at rate
Varying the pulse duration causes degree of turn. Change duration.
Task Do turn (1000) left Pulseout 14, 1000
Do turn (500) right Pulseout 14, 500
Do turn (750) Middle Pulseout 14, 750
Then add Do Loop
Task Pages 125 – 128
Servo Velocity
Type code on slide as program
Put into Do Loop
Pages 131 – 133 Servo Control with Pushbuttons
“Duration” replaces “counter”

## Slide 55
www.ARRL.org
Thank You!