## Slide 1: ARRL – Teacher Institute
Rocklin, California – Parallax HQ
Copyright 2009 - ARRL
Notes: 8:00 – 9:00
<number>

## Slide 2: OptoScope
Basic Electronics
Setup Laptop
CD from BOE-BOT BOX
Auto Start CD
Basic Stamp Editor Version
Install USB – Use 4.0 Version for XP
Use 5.1 Version for Vista
Open OptoScope
Notes: <number>
Review Agenda
Put basic Electronics away
Setup computers
Break into your BOE-BOT box – retrieve CD.
Stay together as we install programs.
Auto start CD.
Software on left hand side.
Install Basic Stamp Editor Version 2.4 – Double click on defaults.
Install USB – Use 4.0 version for Windows XP; use 5.1 for Windows Vista.
Open oscilloscope.
Put four rubber feet on the Optoscope.
Get out USB cable. DO NOT plug into laptop.
Plus USB port into laptop. – It should read “Driver is installed and ready to use.” If not, raise your hand. DO NOT proceed, wait for further instructions please.
Under WINDOWS, select START and right click.
Select PROPERTIES and DEVICE MANAGER.

## Slide 3: OptoScope
Install Rubber Feet on OptoScope
Settings: COM Port Settings
Blue Lead = Channel 1
Red Lead = Channel 2
Limitations:
  1MHz bandwidth
  Not a full scope
  Used to demonstrate Basic Electronics
Notes: <number>
Parallax Optoscope
Settings: COMM Settings
Blue Lead = Channel 1. Red Lead = Channel 2.
VISTA Hit RUN to see if the Optoscope is connected. XP: go to File, COMM PORT, SETTINGS.
Optoscope limitations. 1 MHz bandwidth. Not a full scope. Used to demonstrate BASIC ELECTRONICS. Root Mean Square measurements are close but not accurate. To see the full effect, compare the Optoscope with an oscilloscope to better understand the limitations. None-the-less, the Optoscope is a very neat and nifty tool. The students like using it because it brings electronics into their visual consciousness.

## Slide 4: OptoScope
Snapshots of screens
Ideal for Use with ARRL Boards
Notes: <number>
The CAPTURE / PICTURE screen allows you to take snapshots for PowerPoint presentations and to record circuit conditions. The Optoscope is ideal for use with the ARRL Activities Boards before you.

## Slide 5
Horizontal
Vertical
Channels 1 & 2 On / Off
Conclusion
1
2
3
4
Frequency
OptoScope
Notes: <number>
DEMONSTRATE ON OPTOSCOPE Horizontal
Vertical
Channels 1 & 2 On / Off
Frequency

## Slide 6
Root Mean Square
Auto Measurements
Trigger Sampling
5
6
7
OptoScope
Notes: <number>
RMS (Root Mean Square) which is the Direct Current equivalent of an AC voltage.
AUTO MEASUREMENTS are close.
TRIGGER SAMPLING POSITIONS

## Slide 7: OptoScope Functionality
UNDERSTANDING SIGNALS
  Outstanding way to learn oscilloscope
Modulation / Demodulation Board
Notes: <number>
UNDERSTANDING SIGNALS is the best introduction to using the Optoscope’s functionality.
Get rectangular board with 2 volume control knobs labeled MODULATION / DEMODULATION Board.
ARRL’s Activities Board Concept
Mark Spencer developed them to easily and readily demonstrate Basic Electronic principles. He makes them during the wintertime when he is snowbound (of sorts) in his mountain retreat. Initially they were in kit form but he discovered the kits were not being built or they were being built wrong. Boards are available in stock. Send letter requesting boards to Mark on school stationery. They are, however, for instructor use, not student use.

## Slide 8: Modulation / Demodulation Board
Modulation
  adding an intelligent waveform to a carrier wave
Demodulation
  stripping the carrier wave away to retain original intelligent waveform
Basis for radio communications
Notes: <number>
Modulation is adding an intelligent waveform to a carrier wave and then demodulation is stripping the carrier wave away to retain the original intelligent waveform. This is known as radio.

## Slide 9: Modulation / Demodulation Board
Amplitude – Frequency Knobs
Audio Plug
Frequency Generator Section
Oscillator simulates +15KHz Signal
Modulation Circuit = Transmitter
Demodulation Circuit = Receiver
Tie Points & Ground
Notes: <number>
On the board, one knob regulates amplitude, the other knob regulates frequency.
There is a plug-in jack for AUDIO that can be used with an audio frequency amplifier or computer sound card. The tone is obnoxious but …
On the left side of the board is the audio frequency generator section. It generates /simulates intelligence we will use to demonstrate modulation.
On the center of the board is another oscillator that simulates radio frequency +15KHz.
At the bottom of the board is the modulation circuit. This is the transmitting portion of a transmitting radio.
At the bottom right of the board is the demodulator filter circuit that simulates the receiver. A radio receiver is mainly a demodulator that receives the signal and strips away the carrier wave, leaving only the intelligence = music, voice, data.
There are tie points on the board to connect Optoscope probes. FIND t1. Next to it is the GND (-) terminal. Connect the Black colored probe to the GND. Connect the BLUE lead to T1.
There is only one GND connection required as all of the GND points are connected on these particular boards. This may not be the case with other circuits.
If the signal you are looking at is not referenced to ground, then move black lead to provide the necessary reference point.
TP2 and GND on top of the board are reversed- they are switched. T2 is on Top of Board, GND is on the Bottom. Make sure the RED lead is connected to the top.

## Slide 10: Modulation / Demodulation Board
Make sure both switches are OFF
Connect batteries (observe polarity)
Turn on
Blue – TP1 Black – Gnd Red – TP2
Select Channel 1 on Laptop
Settings to 50mV for vertical – 200us for horizontal (1& 2) - RUN
Notes: <number>
It is possible to hurt the board if you really wanted to. Best way is to have the switch turned ON and then try to connect the batteries backwards. There is no protective diode to power supply which would prevent this happening. A diode allows electrons to flow in only one direction. Diodes are especially important when you are trying to charge a battery. If the terminals are backwards, the reverse flow of electrons will fry components.
So, make sure both switches are OFF and clip two (2) 9-volt batteries to the board. Then swich the board ON. If you are not getting signals from the Optoscope at any point, first check the batteries to make sure they are good and are placed on the board correctly.
Connect the BLUE lead to TP1. BLACK lead to GND. RED lead to TP2. (Remember T2 is backwards.)
On the laptop, select Channel 1 by clicking on the BLUE icon. Change the settings to 50mv for vertical and 200Us for horizontal.

## Slide 11: Vocabulary of a Wave
Waveform
Peak
Trough
Period
Frequency
Amplitude
Tone from the board
Notes: <number>
Varying the amplitude goes to zero (0) as the increase of the wave takes shape and tone rises. LOUDNESS
Varying the frequency causes an increase in the pitch of the signal.
Frequency = 1/period period = 1/frequency
Use the CURSOR key to capture period of signal.
Press PRNTSCRN to save captured shots of signals.
HOW DOES INFRARED WORK? Or How does my remote control work?
Using the Optoscope, set the Trigger function to SINGLE acquisition. The settings are at 1ms and 500mv.
Press key #2 on the remote control. This is the SONY CODE. Since SONY developed the remote control, they had first bite at the codes setup.
Put the Optoscope away for now.

## Slide 12: Break

Notes: <number>

## Slide 13: Soldering 101
A Really HOT Topic

## Slide 14: Soldering 101
Developing accomplished solder-ers
Follow the steps
Portion of 24-hour clock
Complete project at home
“Smoke Test” first thing tomorrow
Notes: <number>
3:00 – 4:00
Clear the table. Put books and all of the resource materials on the floor. Batteries included. (Get it?)
We are going to learn to solder. Even if you are an accomplished solder-er, please go through the steps with us because these are the same steps you will use to train your students to becoming accomplished solder-ers- of- the-future.
SOLDERING 101
There is a PowerPoint presentation on the CDs. We going to solder a portion of the 24-Hour Clock. You will then finish soldering tonight and in the morning, the first line of business will be the “Smoke Test.”
The construction manual is on the CD. DO NOT solder the battery clip. If you do, testing the board will become impossible.
Review SOLDERING 101 PowerPoint slides to include PIC information and How the 24-Hour Clock Works.
Let’s get started. Find the large yellow envelope for your kits bag. Plug the soldering iron, making sure the tip is not resting on the tabletop or anything else of value since whatever it’s on will burn. Make sure everyone has a pair of diagnal cutters, portion of solder and soldering iron for use at home or in the hotel tonight.

## Slide 15: Soldering
The process of making an electrical connection by melting low-temperature metal alloys around component leads
Soldering is just as much an “Art” as it is a “Science”
We will:
  Go over some soldering vocabulary
  Illustrate graphically soldering techniques
  Solder a few components on the 24-hour clock
  Complete the board as homework
  Construction manual on CD#1

## Slide 16: Soldering Process in Brief
Turn on soldering iron and let it get to temperature
Clean soldering tip with a damp cloth or sponge
Install the component and hold in place with a physical connection
Heat the component lead and the adjacent circuit board pad – apply the right amount of heat (art)
Touch solder to the component lead and pad - melt the right amount of solder (art)
Remove solder
Remove heat (art)
Hold steady until cool
Inspect the connection (art and good eye)

## Slide 17: Vocabulary
Circuit Board
PCB
Components
Component side
IC socket
Pins

## Slide 18: Vocabulary
Point-to-Point wiring
Physical (mechanical) connections
Lugs
Component leads
Junctions

## Slide 19: Vocabulary
Component side
Component outline
Silk screen
Double sided circuit board (top side)
Top trace
Solder mask

## Slide 20: Vocabulary
Double sided circuit board bottom side
Solder pads
Through hole
Foil trace
Pad
Ground plain
Soldering side
Multi-layer board

## Slide 21: Vocabulary
Surface mount component
Pitch
Pin #1 designation on IC

## Slide 22: Vocabulary
Tinning
Wetting
Surface tension
Flow

## Slide 23: Vocabulary
Connection
Volcano
Shine or sheen
Dull or crusty
Cold solder joint
Tack-solder

## Slide 24: Vocabulary
Soldering Iron
Tip
Soldering Station
Tip cleaning

## Slide 25: Solder Types
Rosin core and Flux
  Flux type is used for household soldering
  Rosin core is used for electrical wiring (reduced corrosion potential)
Rosin and flux are chemical compounds that clean the metal surfaces that are being soldered
  The rosin or flux melts first to contact the joint
  The rosin or flux float the impurities away from the metal surfaces and to the top surface of the solder joint
  Produces the smoke you will see associated with soldering
You will be using rosin core solder

## Slide 26: Rosin Core Solder
Outer tube of low melting alloy
  Tin
  Lead
    (Industry is moving toward lead-free)
  Silver
  Copper
  Other specialized metals
Inner core is the rosin

## Slide 27: Solder Specifications by % Alloy

## Slide 28: Soldering Process in Brief (again)
Turn on soldering iron and let it get to temperature
Clean soldering tip with a damp cloth or sponge
Install the component and hold in place with a physical connection
Heat the component lead and the adjacent circuit board pad – apply the right amount of heat (art)
Touch solder to the component lead and pad - melt the right amount of solder (art)
Remove solder
Remove heat (art)
Hold steady until cool
Inspect the connection (art and good eye)

## Slide 29: Soldering Process
Insert component from the “component side” of the PCB and bend leads out to physically hold the component steady and in place
When you can’t bend leads – “Tack Solder” one lead to hold component in place

## Slide 30: Soldering Process
Touch the tip to the component lead AND the pad
Apply just enough heat
  TLAR (That Looks About Right)

## Slide 31: Soldering Process

## Slide 32: Soldering Process
When you have heated the joint just the right amount (TLAR) touch solder to lead and pad (not to the tip)
  Do as I say, not as I do!
  Why I sometimes will use the tip?

## Slide 33: Soldering Process
The melting solder will flow around the joint
  Called wetting
  Surface tension will produce a nice “Volcano” looking joint
Keep the tip in place until TLAR

## Slide 34: Soldering Process
Remove solder then tip and allow joint to cool
  Hold steady while cooling
Inspect for good joint (TLAR)
  Reheat “cold solder” joints
Clip and remove excess leads (safety first, watch for flying leads)

## Slide 35: Good vs. Bad Solder Joints
Cold solder joints are probably the cause of most circuit problems!
You need to use caution not to overheat a joint (TLAR)
  But don’t get overly concerned except for the most delicate components

## Slide 36: Some Safety Concerns
Don’t solder while circuit is powered
Use well ventilated and lighted work space
Don’t touch the solder tip – it’s hot (dahhh)
Static discharge protection – not a hazard for you but can destroy some sensitive components
Watch for flying leads when clipping excess

## Slide 37: Your Turn
We’ll solder a couple of components on the 24-hour clock board
Complete the board over the evening
FOLLOW THE DIRECTIONS ON THE CD!!
Don’t get anxious – don’t power the board until inspected
Return tomorrow for board inspection

## Slide 38
www.ARRL.org
Thank You!